## Slide 1: The LHC machine: Run 2 and beyond
Mike Lamont for the LHC team

## Slide 2
LS1 - descent into the underworld again

## Slide 3
« Old Splice » « Machined Splice » « Consolidated Splice »
« Insulation box »
« Cables » « New Splice »
Total interconnects in the LHC:
  1,695 (10,170 high current splices)
Number of splices redone: ~3,000 (~ 30%)
Number of shunts applied: > 27,000
And a lot more besides…

## Slide 4: Superconducting Magnets and Circuits Consolidation (SMACC)
Collaborations with NTUA (Athens), WUT (Wroclaw) and support of DUBNA
Monumental effort
Over 350 persons involved
Including preparation: ~1,000,000 working hours
No serious accidents!
Jean-Philippe Tock

## Slide 5: Powering tests
All ~1700 magnet circuits taken to nominal current level one by one
  Rigorous checks of quench protection, energy extraction, interlocks, power converter, ELQA
  Some circuits are more critical than others…
6 months
cumulative number of powering tests
3000
Following sector by sector cool-down

## Slide 6: Dipole training 1/2
154 dipoles per sector, powered in series
Ramp the current until single magnet quenches - “training quench”
Repeat as necessary

## Slide 7: Dipole training 2/2
From this morning…
All magnets have been trained to well over 7 TeV in SM18 before installation
Extensive re-training was not expected
Training: frictional energy released during conductor motion

## Slide 8: LHC - 2015
Target energy: 6.5 TeV
  to be confirmed at end of powering tests!!!
Bunch spacing: 25 ns
  strongly favored by experiments (pile-up limit around 50)
Beta* in ATLAS and CMS: 80 to 40 cm
  Lower quench margins
  Lower tolerance to beam loss
  Lower intensity set-up beams
  Hardware closer to maximum (beam dumps, power converters etc.)
Energy
  Electron-cloud
  UFOs
  More long range collisions
  Larger crossing angle, higher beta*
  Higher total beam current
  Higher intensity per injection
25 ns

## Slide 9
LHC bunch structure - 2015
1 SPS batch
(288 bunches)
26.7 km 2800 bunches
Abort gap
1 PS batch
(72 bunches)
25 ns bunch spacing
~2800 bunches
Nominal bunch intensity 1.15 x 1011 protons per bunch

## Slide 10: 25 ns & electron cloud
10 eV
5 eV
200 eV
2 keV
Beam screen
25 ns
Typical e– densities1010–1012 m–3
Possible consequences:
  instabilities, emittance growth, desorption – bad vacuum
  excessive energy deposition in the cold sectors
Electron bombardment of a surface has been proven to reduce drastically the secondary electron yield (SEY) of a material. This technique, known as scrubbing, provides a mean to suppress electron cloud build-up.
Electron cloud significantly worse with 25 ns
SEY

## Slide 11: Squeeze in ATLAS
Image courtesy John Jowett
β* = 15 cm
7 microns
β* = 55 cm
 | βtriplet | Sigma triplet | β* | Sigma*
Nominal | ~4.5 km | 1.5 mm | 55 cm | 17 um
HL-LHC | ~20 km | 2.6 mm | 15 cm | 7 um

## Slide 12: Crossing angle
work with a crossing angle to avoid parasitic collisions.
Separation: 10 -12 s
geometric luminosity
reduction factor:

## Slide 13: 2015: beta* in IPs 1 and 5
Many things have changed. Start carefully and push performance later.
Start-up: β*= 80 cm – (very) relaxed
  2012 collimator settings
  11 sigma long range separation
  Aperture, orbit stability… to be checked
Ultimate in 2015: β*= 40 cm
  To be deployed later in the year

## Slide 14: 2015 commissioning strategy
Low intensity commissioning of full cycle – 8 weeks
First stable beams – low number of bunches
Special physics: LHCf and Luminosity calibration
Scrubbing for 50 ns
Intensity ramp-up with 50 ns
  Characterize vacuum, heat load, electron cloud, losses, instabilities, UFOs, impedance
Scrubbing for 25 ns
Ramp-up 25 ns operation with relaxed beta*
Commission lower beta*
25 ns operation

## Slide 15: 2015 Q1/Q2
FIRST BEAM 25th MARCH
(at the earliest!)
SCRUBBING FOR 50 ns

## Slide 16: Q3/Q4 2015
SCRUBBING FOR 25 ns

## Slide 17: ATLAS and CMS performance
 | Nc | Beta* | ppb | EmitN | Lumi [cm-2s-1] | Days (approx) | Int lumi | Pileup
50 ns | 1300 | 80 | 1.2e11 | 2.5 | 4.8e33 | 21 | ~1 fb-1 | 25
2015.1 | 2592 | 80 | 1.1e11 | 2.5 | 7.6e33 | 30 | 3 fb-1 | 21
2015.2 | 2592 | 40 | 1.1e11 | 2.5 | 1.2e34 | 48 | 8 fb-1 | 34
Conservative beta* to start
Conservative bunch population
Reasonable emittance into collisions
Assume same machine availability as 2012
Official GPD luminosity target for the year: 10 fb-1

## Slide 18: Run 2
 | Peak lumi E34 cm-2s-1 | Days proton physics | Approx. int lumi [fb-1]
2015 | 1.3 | 100 | 10
2016 | 1.5 | 160 | 35
2017 | 1.7 | 160 | 45
2018 | 1.7 | 40 | 10

## Slide 19: 10 year plan
Run 3: 14 TeV c.m. with peak luminosity of ~2x1034 cm-2 s-1
Run 2: 13 to 14 TeV c.m. with peak luminosity of ~1.7x1034 cm-2 s-1
Long years – 13 weeks Christmas stop
Interspersed with long shutdown every 3 to 4 years
Ions very much part of the plan
LS2: 18 months
Connection of LINAC4
LHC Injectors Upgrade
EYETS 19 weeks
Extended year end technical stop (CMS)
LS3: 30 months
High Luminosity LHC

## Slide 20: HL-LHC - goals
Prepare machine for operation beyond 2025 and up to 2035
Devise beam parameters and operation scenarios for:
  total integrated luminosity of 3000 fb-1 in around 10-12 years
  an integrated luminosity of 250 fb-1 per year
  mu ≤ 140 (peak luminosity of 5x1034 cm-2s-1)

## Slide 21: How?
Beam from injectors
  High bunch population, low emittance, 25 ns beam
Lower beta* (~15 cm)
  New inner triplet magnets - wide aperture Nb3Sn
  Large aperture NbTi separator magnets
  Novel optics solutions
Crossing angle compensation
  Crab cavities
Dealing with the regime
  Collision debris, high radiation
  High machine availability
  Beam stability, losses etc.

## Slide 22: HL-LHC: key 25 ns parameters
Protons per bunch | 2.2 x 1011
Number of bunches | 2750
Normalized emittance | 2.5 micron
Beta* | 15 cm
Crossing angle | 590 microrad
Geometric reduction factor | 0.305
Virtual luminosity | 2.4 x 1035 cm-2s-1
Levelled luminosity | 5 x 1034 cm-2s-1
Levelled <pile-up> | 140

## Slide 23
BOOSTER: 160 MeV to 2.0 GeV
PS: 2 GeV to 26 GeV
LINAC4: H- at 160 MeV
LHC Injector Upgrade (LIU): A cascade of improvements across the whole injector chain to reach the HL-LHC target
1. Beams from injectors

## Slide 24: The critical zones around IP1 and IP5
More than 1.2 km of LHC
Plus technical infrastructure
(e.g. Cryo and Powering)…
ATLAS
New triplet Nb3Sn
required due to:
-Radiation damage
-Need for more aperture
2. We also need to modify a large part of the matching section
e.g. Crab Cavities &
D1, D2, Q4 & corrector
3. For collimation we also need to change the DS in the continuous cryostat: 11T Nb3Sn dipole
CMS
2. Lower beta*; 3. crossing angle compensation

## Slide 25: HL-LHC & LIU
Projects firmly established and key parts of CERN’s mid-term planning

## Slide 26: Conclusions
2015 goal is 25 ns at 6.5 TeV
  Scrubbing++ required – even then electron cloud could remain an issue
Lot of stuff to sort out again but there’s a lot of Run 1 experience
Non-aggressive parameter choice/strategy to start with, aiming to re-establish stable operation with 25 ns before pushing performance
LIU/LHC firmly established with planning out to 2035.