## Slide 1: Proposal for measurements
G. Arduini, E. Métral, G. Rumolo

## Slide 2: Understanding of the e-cloud and estimations from simulations
Need to constrain the models in order to provide guidance from simulations:
  Compare vacuum pressure rise for 12/24/36 bunches following a train of 12 bunches (fixed distance) but sufficiently apart
  Compare vacuum pressure rise for different spacings of the trains injected in the LHC. e.g. 2 trains of 12 bunches with increasing spacing in the SPS (min 225 ns)
  Measure threshold for pressure rise as a function of bunch intensity (36 bunches)
  Measure heat load vs number of batches assuming constant spacing between trains (with 24 bunches?). Could be done during scrubbing

## Slide 3: Scrubbing strategy
Scrubbing:
  With 12 bunches: not much happening in point 3 and 7.
  With 24 bunches we are limited to ~84 bunches at present so not saturating but steps are larger
  With 36 bunches: losses  not efficient at this stage  need a first step with 24 bunches
  Can we increase the threshold for the closure of the vacuum valves?
What is the margin that we need at 450 GeV in order to stay below interlock level during the ramp? Are there positions where synch light and e-cloud sum-up. Where?

## Slide 4: Other issues
Do we understand the losses with 36 bunches, is this related to the electron-cloud.
Two approaches:
  Follow the evolution of the losses as a function of the scrubbing injecting 36 bunches at different stages of the scrubbing
  Measure instability characteristics (with head-tail monitor and damper pick-ups) when reducing the gain/switching OFF the transverse feedback

## Slide 5: Other measurements to be done
UFO measurements with large number of bunches. Get this as part of the scrubbing?
Beam-beam at 3.5 TeV + short physics fill for ATLAS (min 24 on 24 bunches  108 on 108?)
Quench test at injection. Conditions required?
Test high intensity injection (2x36). Need to have some scrubbing before testing it.
Aperture measurement in the triplets. Can this be done during the ion run (during the stop for source refurbishment?)