## Slide 1: Thursday 10 March
Injection of 8b of 75 ns – no problems.
  Consistent (identical) trajectories between SPS cycles.
Dump protection.
  TCSG – TCDQ cross-calibration with orbit bumps. New positions and offsets of TCDQ defined wrt TCSG in IR6.
  IR6 extracted beam aperture (to be finished): [deg] [sig] 0 10 30 12 60 22 90 11.5 180 12 210 14.5 240 17

## Slide 2: Thursday 10 March
Inject-dump delay checks.
  Synchronization issue found (and understood/fixed – clock delay) on B1.
B1
B2

## Slide 3: Thursday PM – ramp & squeeze
Ramp and squeeze attempt with nominal bunch for collimation setup at end of squeeze – lost beam.
  Orbit corrector settings ‘reset’ – as possible source of OFB difficulties in stabilizing the orbit.
  Lost at beta* = 3.5 m due to negative Q’.
Ramp and squeeze attempt with nominal bunch – no 2.
  Step by step.
  Prepared damper functions. Damper on when going into collisions.
  Check Q’ – ok all along after correcting the functions.
  Orbit – residual excursions better, systematic incorporation of RT trims, some global corrections mostly at the end.

## Slide 4: Thursday PM – orbit in squeeze
Spikes were larger in previous ramps, in particular at the end of the squeeze (factor ~2-3 better).

## Slide 5: Going into collisions
Large orbit excursions when going into collisions, bem dumped on beam loss. B1V unaffected – a smell of controls problem…

## Slide 6: Going into collisions
Problem was tracked to a wrong back-incorporation of orbit correction from the previous night affecting 3 strong correctors involved in separation knob. Not clear why this happened…
There is a kick missing here !

## Slide 7: More R&S
Following the issues with the collisions, decide to insert another last ramp-squeeze-collide with 2 probes.
  Very smooth and moderate RT corrections.
  Collimator squeeze functions (preliminary !)

## Slide 8: Squeezed TCTs
Problems to find collisions with probes.
  Collisions seen in IP8 only…
XPOC detected TSU problem after dump – to be checked.

## Slide 9: Aperture measurements at 450 GeV
Measured loss level ratio TCP-aperture MQ9.L7.B2

## Slide 10: News from beta*
‘Final’ values from K-modulation:
Errors around 4-10%.
Imbalance is 2.5 +- 8%.
Optics team feels uncomfortable to correct such a small effect given the uncertainty.
Beam/plane | IR5 | IR1
B1H | 1.50 | 1.53
B2H | 1.48 | 1.57
B1V | 1.52 | 1.50
B2V | 1.52 | 1.57

## Slide 11: Today
Until late afternoon:
  Collimator setup at end of squeeze.
  Collide.
  Collimator setup in collisions.
Then injection-dump.
Night: loss maps and other validations.