## Slide 1: Saturday 26th March
9:15 Problem with RB78 temporarily solved. It's running on one Thyristor bridge only and without the active filter
LHCb polarity change
IR6 interlock BPMs reconfiguration and tests
  Check IR6 BPMs with 8b per beam:
    No interlock for windows completely closed, for both beams, as expected
  Checking BPM IR6 intlk with 16b
    B1 dumped when moving from 0.75 to 0.25 mm as expected - beam position was +0.5 mm
    B2 dumped when moving from 1.21 to 0.71 mm as expected - beam position was +0.8 mm

## Slide 2: Saturday afternoon
  Checking BPM interlock with full pattern and new count/turn settings
    Worked OK for B1 and B2
    B1 dumped between +0.13 and -0.37 mm (position was 0.08 mm)
    B2 dumped between +1.0 and +0.5 mm (position was +0.55 mm)
    OK to fill with new pattern
16:15 Next 1.38 TeV attempt
  Beams dumped (SIS on TCDQ/beam position)
  Joerg identified the cause in a BPM which started to develop an offset today. He opened the thresholds to recover the margin
18:20 Stable beams
  bigger emittances (around 3 microns from SPS)
  different filling scheme avoiding offset collisions

## Slide 3: Updated IR6 interlock BPMs
bunchCntWin1 changed from 70 to 75;
turnCntWin1 changed from 100 to 5;
Left the other values unchanged
  bunchCntWin2 250; turnCntWin2 10
All position values unchanged.
As a result, the interlock will now only become active when 15 or more bunches are out of tolerance in IR6.
The interlock thus becomes active at injection only when 15 or more bunches are circulating
*** IMPORTANT: NO RAMP OF FEWER THAN 80 BUNCHES ALLOWED UNTIL THE INTERLOCK IS MODIFIED BACK TO THE INITIAL VALUES *
Brennan Goddard

## Slide 4: 1650
Reyes

## Slide 5: 1653 – start fill

## Slide 6: Incoming
Sat PM | 1.38 TeV | 
Sat night | 1.38 TeV stable beams | 
Sunday AM | VdM scans | 
Sun PM | Transfer lines tests - Injection loss calibration before the shielding (needs to be done before TS) | 2 h
Sun PM/night | 1.38 TeV | 
Mon 06:00 | Dump beams for TS | 

## Slide 7: Noted – Per Hagen
Will the “soon to come” fill 1664 be celebrated? with or without crossing angle…