## Slide 1
Summary of Week 41
Machine Coordinators: G. Arduini, J. Wenninger
Main aims:
Luminosity production
MDs

## Slide 2: Week 41
High pil-up
Cryo Pt. 6
25 ns MD

## Slide 3: Fill Overview (Mon 08:00 – Mon 08:00)
Summary of Week 30
G. Arduini, J. Wenninger
Main aims:
Adiabatic increase of peak luminosity by emittance reduction
Luminosity production
Fill | Peak L [1033 cm-2s-1] | Length [h] | Int. L [pb-1] | Phase | Dump cause
2200 | 3.29 | 2 | ~15 | STABLE | IT L8 PC
2201 | 0.00 | 3.9 | 0.1 | STABLE | OP dump (High pile-up test)
2202 | - | - | - | ADJUST | CRYO PT. 6 (SEU?)
2204 | 3.34 | 13.1 | 99.8 | STABLE | Vacuum spike (BGI)
2208 | 3.39 | 13.6 | 102.4 | STABLE | OP dump
2210 | 3.48 | 6.2 | 58.7 | STABLE | RQ5.R5 QPS (SEU)
2215 | 3.26 | 1.5 | 15.7 | STABLE | CURRENT LEAD RB.A56 (SEU)
2216 | 3.34 | 11.4 | 92.8 | STABLE | RQT12.L5B2 (PC)
2217 | 3.46 | 1.2 | 13.1 | STABLE | RF (HOM – 4B2)
2218 | 3.49 | 2.6 | 28.7 | STABLE | RQT12.L5B2 (PC)
2219 | 3.5 | 15.5 | ~122 | STABLE | 
Total |  |  | ~550 (85) |  | 

## Slide 4: Main achievements (c/o ATLAS)
Bunch population > 1.4x1011 p
Peak Stable Luminosity Delivered | 3.50x1033 cm-2s-1 | Fill 2219 | 11/10/16, 06:14
Maximum Luminosity Delivered in one fill | 122.44 pb-1 | Fill 2219 | 11/10/16, 06:14
Maximum Luminosity Delivered in one day | 135.45 pb-1 | Thursday 13 October, 2011 | 
Maximum Luminosity Delivered in 7 days | 546.35 pb-1 | Mon 10 October, 2011 - Sun 16 October, 2011 | 
Maximum Peak Events per Bunch Crossing | 29.83 | Fill 2201 | 11/10/10, 07:59
Maximum Average Events per Bunch Crossing | 29.83 | Fill 2201 | 11/10/10, 07:59

## Slide 5: Integrated luminosity
> 5.1 fb-1 in both high luminosity experiments!!

## Slide 6: Statistics
70 h in stable beams  42 % (47 %)
6 h for high pile-up test
12 h for 25 ns MD
Major stops (33 h)
  Cryo Pt6 (Tue) 24 h
  Injectors (Mon,Wed) 7 h
  Power converters (Sun) 4 h
  TDI pt.2 – controls (Sun) 2 h

## Slide 7: Sun/Mon
08:08 Beam dump due to power converter problem on RQT12.L5B2. End of fill #2218. 29 pb-1 in 2.5 hours.
10:30-11:30 Access for power converter problem.
Vacuum spike observed during injection of first train of 144 bunches of beam 2  no losses observed
15:30 STABLE BEAMS #2219 3.5x1033 cm-2s-1 with 1.4x1011 p/b
Several problems with DIP re-publishing to CMW  fixed yesterday evening  caused lumi spike in LHCb
Overnight LHCb reported issue with the filling pattern (being investigated)
07:00 OP dump End of fill #2219 ~122 pb-1 in 15.5 h

## Slide 8: Abort gap cleaning tests
Lumi ATLAS
Lumi CMS
B1 AG pop
B2 AG pop
50%
100%
E. Gianfelice, J. Uythoven, D. Valuch

## Slide 9: Abort gap cleaning tests
When cleaning switched on there is a small effect on the luminosity lifetime
Tested different strengths and 2 different excitation windows lengths
Proposed strategy: leave abort gap cleaning off and switch it on as soon as abort gap population reaches 1x1010 p and lower than 1x1011 p. Announcer giving a warning when 1x1010 p level in the abort gap is reached
E. Gianfelice, J. Uythoven, D. Valuch

## Slide 10: TDI vacuum
Important reduction of the vacuum activity during coasts after opening the TDI gap after injection to +/- 55 mm instead of +/- 20 mm (bunches were slightly longer for this fill)
+/-20 mm
+/-55 mm

## Slide 11: Other intensity effects
Monitored temperature interlocks on collimators  marginal for TCP.B6L7  increased threshold from 55 to 700C after OK from Ralph and vacuum.

## Slide 12: High pile-up MD
1 high intensity bunch per beam (+ probe).
  At injection 2.4E11, 2 mm.
Significant transverse blow-up while sitting at injection and in the ramp.
  To be analysed…
15:30 Stable beams fill #2201, 5x1030 cm-2s-1.
  Average pile-up of ~ 32 events.
  Emittances ~2.8 to 3.6 mm at start of the fill.
  Emittances ~3.4 to 4.7 mm towards end of fill.

## Slide 13: 25 ns MD
Setting-up
Reference meas. variable spacing
6.325 ms
732 + 660 b
3.625 ms
1092 + 1020 b
3.625 ms
1020 + 156 b
Limited by pressure rise on MKI8. Now limited to 2.5x10-9 mbar. No injection interlock level during the scrubbing run and pressures of up 10-8 mbar reached.

## Slide 14: Heat load
Reference meas. variable spacing
6.325 ms
732 + 660 b
3.625 ms
1092 + 1020 b
L. Tavian

## Slide 15: Vacuum
Reduction of approx. Factor 4 in all the Cold Warm Transition of Stand Alone Magnets after 2 hours
After that period possible to inject 1.4x1011 p/b with no important vacuum instability so far  would be good to have another period of ~24 h this week to test potential effects on high intensity 50 ns operation
G. Bregliozzi

## Slide 16: Emittances along trains

## Slide 17: RF stable phase shift along batches
E. Shaposhnikova, JF Esteban Muller

## Slide 18: Pending issues
Injection of high intensity beam (>1.4x1011 p/b) requires stopping the North Area extraction during LHC filling to avoid ZS (electrostatic septum) sparks.
ALICE background
A fault on the powerPC of the PAD in UJ16 prevents anyone going into UJ16 until after the access piquet makes an intervention. This intervention is not yet scheduled, and will wait until needed

## Slide 19: Upcoming
Access for QPS reset in Sector 78
Physics
90 m Beta*
Pending: loss maps
Week 42 Coordinators: B. Holzer, M. Lamont