## Slide 1: IR2 aperture measurements: results, actions and proposal
C. Alabau, G. Arduini, R. Assmann, R. Bruce, M. Giovannozzi, G. Müller, S. Redaelli, J. Wenninger
Latest results
Actions
Proposal
Acknowledgements: V. Baglin, P. Bestmann, J. Jowett, K. Weiss

## Slide 2: Latest results
Latest aperture measurements (vertical plane only)
  Separated beams-> 0.7 mm
  External crossing angle -> 120 mrad (internal -> 20 mrad)
  Two additional bumps used (similar to previous measurements)
  Results
    Beam 2 (V) -> triplet aperture 15.0-15.5 s
    Beam 1 (V) -> aperture bottleneck 12.5-13.0 s
  Comments
    TCDD was found to be an aperture limit (14.0-15.0 s) for Beam 2. It was opened to ±15 mm and this solved the problem.
    For Beam 1, the bottleneck was located upstream of the TCTVB.4L2. Its location could not be identified.

## Slide 3: Recap of results
Beta*=1 m
  Standard criterion:
    TCT at 12 s
    Triplet aperture at least at 14 s
  For ion run TCTVs will be fully opened (interference with the ZDC)
Plane | External crossing angle (mrad) | Aperture Beam 1 (s) | Aperture Beam 2 (s)
V (crossing) | 120 | 12.5-13.0 | 15.0-15.5
V (crossing) | -80 | 15.5-16.0 | 16.0-16.5
H (separation) | -80 | 16.0-16.5 | 15.5-16.0

## Slide 4: Actions
Verification of alignment of collimators and vacuum chambers (ABP-SU): nothing abnormal found.
Radiation survey (RP): nothing abnormal found.
Status of bellows and RF fingers (TE-VCR): X-rays do not show any issue. One module non-conform, but not serious.

## Slide 5: Proposal
Ion commissioning
  The conditions:
    b*=1 m
    External crossing angle of 80 mrad
  Have been stated to be fully acceptable at the last LMC.
  Proceed with commissioning using external crossing angle of 80 mrad.
  Later it might be considered to make an attempt to increase the external crossing angle (100 mrad – moderate – 120 mrad – bold).
  Overhead is measurement of loss maps (with the risk of stepping back in case of problems).
Technical stop
  Consider the installation of a mobile BLM in the region upstream of the TCTVB (left of IP2) to study aperture bottleneck.