## Slide 1: Fri/Sat 4-5.11.11
Thu – Fri: Recovery of MKD in SPS (40h lost due to this). Only single bunches – all bunch train MD’s are cancelled.
Procedure for Fri night and Sat morning:
  Call in team contact ~1h before MD start
  MD teams should leave coordinates and special requests with the EIC
  No fixed times but follow through program once we have beam back (now estimated for ~18:00). Ramps lost will be repeated.
  MD's later in the list have a lower probability to happen but if our luck changes completely we might make it through almost all of it (you never know)…

## Slide 2: Adapted MD Program
Tight collimation test
  Contact: R. Bruce, S. Redaelli
  Beam: 1b per beam
  Time: 1 ramp + 1h at flat top (~3h)
Quench test injection, BLM calibration, beam shape
  Contact: R. Schmidt, D. Wollmann, C. Bracco
  Beam: 1b per beam
  Time: 3h at injection
BI (BSRT 3.5 TeV and/or matching monitor)
  Contact: F. Roncarollo
  Beam: 2b per beam
  Time: 1 ramp + 2h at flat top (~4h)
ATS
  Contact: S. Fartoukh
  Beam: 1b per beam
  Time: 6h total
RF tests
  Contact: E. Chapochnikova
  Beam: 8b per beam
  Time: 1 ramp + 1h at flat top (~3h)
Ramp and squeeze
  Contact: S. Redaelli
  Beam: 1b per beam
  Time: 1 ramp + squeeze (~2.5h)

## Slide 3: Fri/Sat 4-5.11.11
19:27 Beam back in LHC.
21:56 Start ramp. Lost…
  Wrong scaling time for OFB (1s vs 680s), OP dump as precaution.
00:01 Ramp started with tight collimators. Squeeze.
  Settings: 4/6/8 sigma (IR7), 9.3 sigma (IR1/5)  lower beta* settings
  Some beam losses  not a very good orbit correction by feedback
00:55 Loss maps
  Results look very nice on first sight  end of run feasibility for tight settings looks OK
  Detailed analysis to be done…

## Slide 4: Ramp and Squeeze

## Slide 5: Collimation Settings (Tight = Relaxed 7 TeV)

## Slide 6: Beam 1 H loss map

## Slide 7: Sat 5.11.11
02:15 MD on quench limit, beam shape, TCLIB loss calibration
  Beam shape: Within the available 1h of circulating beam, we managed to perform 4 full slow scrapings. 2x20um step size, 60um step size and 80um step size. The scraping with 80um step size was performed with a frequency 1/8s, the others with 1/4s.
  TCLIB BLM calibration: slow full beam scraping: 50 um steps (90 steps) with a pilot bunch. Detailed data analysis will follow (normalization factor for FLUKA simulations). Observed that the monitor with RC filter shows a signal which is just a factor 2 higher than the non filtered monitor (factor 180 expected, factor ~20 measured during last MD)
 The unquenchable LHC magnets… (at 450 GeV at least)

## Slide 8: Bunch shape measurements

## Slide 9: Sat 5.11.11
02:15 MD on quench limit, beam shape, TCLIB loss calibration continued…
  Quench test:
    closed TCLIB collimator to 1 mm gap and -3 sigma offset
    Beam 2 inject and dump, pilot bunch of 3e10 p+
    BLM monitors at TCLIB and Q6 in saturation (> 1000% ratio to dump)
    We increased the current of Q6.L8 magnet in steps of 200 A until 2200 A (5 TeV operation) and recorded QPS signal
    QPS didn't show any significant variation when increasing the beam current ==> NO QUENCH or QUENCHINO recorded. Data analysis will follow but up to now it looks like the signal was just induced by showers on the electronics (TCLIB intercepts the full beam ==> too diluted energy deposition at Q6 to cause a quench).

## Slide 10: Sat 5.11.11
05:49 MD on BI…
  BSRT Studies 3.5 TeV
    We manage to record almost all the data we wanted (beam position and size while bumping a small emittance and a large emittance bunch). We couldn't measure in parallel also the pilot bunches (some BSRT acquisition SW problems) but this was not the priority. For amplitude we scanned 4 different longitudinal positions of the cameras in order to characterize the system magnification and focusing.
    At the same time we took frequent WS (quality of Beam 1 WS data to be verified, since we nneded to boost the PM gains to max to have decent profile, which is not normal).
    The collected data need to be analyzed and will give meaningful information about the BSRT vs WS calibration at 3.5 TeV and the imaging system magnification when taking light from the D3 (never measured experimentally before).
  Some data on influence of the beam position on the FBCT reading

## Slide 11: Influence beam position on FBCT reading

## Slide 12: Ahead
Next: some matching monitor checks at injection
9:30 ATS (already at ATS injection optics)
16:00 Start of ion commissioning  unlikely that we can do anything for the RF MD and combined ramp and squeeze
For discussion:
  Proposal to install movable BLM’s during upcoming TS to have better resolution where losses in IR2 aperture measurements start. Repeat aperture measurement…
  Crossing angle & beta* in IR2 ( Massimo)
  Plan of ion commissioning before technical stop ( John)

## Slide 13
Layout A4L2.C (vertical)
Q4
TCT
ID800
Q3
TDI
TCT - TCD
TCDD
LSS2L :
  TCTVB
  TCDD
  VAB
  BPMSX
  D1L2
D1L2
VPIA.A151.4L2.X
VGPB.120.4L2.X
Giuseppe Bregliozzi

## Slide 14
TCDD
LSS2L :
  TCTVB
  TCDD
  VAB
  BPMSX
  D1L2
D1L2
VPIA.A151.4L2.X
VGPB.120.4L2.X
Layout A4L2.C (vertical – zoom)
Q3
TDI
ID800
TCT - TCD
Tunnel checks (vacuum, survey, RP): no indication
Worry: change of IR2 layout over christmas stop – will reduce aperture…