## Slide 1: Commissioning plan for p-Pb run, update on filling schemes
John Jowett
With input from: many people

## Slide 2: Commissioning plan
Starts after basic setup of injectors and LHC by OP
For parameters and other details, see LMC presentations on 5 & 12/12/2012
Will evolve depending on progress, kept up to date on the usual LHC ions commissioning page
  http://lhc-commissioning.web.cern.ch/lhc-commissioning/commissioning-ions.htm
But … some details to be finalised when everyone is available for consultation.

## Slide 3: Update on filling schemes
First physics with same scheme as pilot run
  13 bunches/beam, 8 collisions/experiment
Intermediate scheme (next step …)
  96 bunches/beam,
  (48,48,48,24) collisions/experiment
  G:\Projects\ILHC\JMJ\pPbFilling\Intermediate
Main scheme
  318 bunches/beam,
  (276,276,276,42) collisions/experiment
  G:\Projects\ILHC\JMJ\pPbFilling\Main
ALICE Minimum Bias Scheme, if needed in first days
  (316,318) bunches/beam,
  (274,94,274,90) collisions/experiment
  G:\Projects\ILHC\JMJ\pPbFilling\ALICEMinimumBias

## Slide 4: BACKUP SLIDes

## Slide 5: Physics requirements
ALICE, ATLAS, CMS: equivalent p-p luminosity
ALICE
  Beam reversal p-Pb to Pb-p half-way through
  Spectrometer polarity reversals in both
  Initial period of min. bias running
ATLAS, CMS
  No luminosity limit
  Switch to p-p at
LHCb
LHCf may like short run at beta*=11 m ?

## Slide 6: Ideal course of the p-Pb run – from LPC
Integrate 30 nb-1 in ALICE as quickly as possible but respecting the constraints:
  Means getting to this luminosity in ALICE quickly, most likely if we start with small β* and conservative intensity (reasons later)
  Initial minimum bias ~ during luminosity ramp-up
  Beam reversal and 2 polarity reversals
Get similar (or more) luminosity in ATLAS or CMS
Get several nb-1 in LHCb
Then switch to intermediate energy p-p operation

## Slide 7: Baseline performance extrapolated from Pilot Fill
Already close to ALICE maximum luminosity with emittances of pilot fill, good Pb intensity, fairly conservative proton intensity – leaves room to try to increase it up to a factor ~3 (level ALICE if necessary).
Can easily be worse if we have blow-up or losses at injection or ramp (from moving encounters, IBS, …).
Unequal beam sizes were OK in pilot fill with higher β*.
Emittance increase will probably reduce luminosity for all experiments and pile-up for ALICE.
This is our preferred first goal for the run. But, on the basis of present knowledge, it is by no means a “safe set of parameters” (except for optics).

## Slide 8: Off-momentum optics, beta-beating, etc
We are very well prepared to handle the new squeeze in ALICE, correct for off-momentum beta-beating and set up the collimation system.
Collimation working group
Waiting for approval

## Slide 9: Squeeze time (from J. Wenninger)
Parallel squeeze of all IPs to 0.8 m takes 874 s.
Existing squeeze to 3 m in ALICE/LHCb (1.5 m in IR1/5) takes 529 s.
In half the fills: 240 s to flip the ALICE angle and collide
  Limitation on corrector at Q6 that changes by ~90 A for a max dI/dt of 0.68 A/s when flipping the ALICE crossing angle

## Slide 10: Luminosity in the pilot run

## Slide 11: Encounters around an IP with 200/225 ns spacing
Encounter points at 0., 100., 112.5, 200., 212.5, 312.5, 325., 412.5, … ns from IP.
Collisions at IP only