## Slide 1: Summary of Week 4 pPb physics
Machine Coordination:
Mike Lamont & Jan Uythoven
Ion coordination: John Jowett

## Slide 2: The week in beam currents
Back to 338 bunches, all dumps by BPMS low intensity limit ions
Dumps RF manip
Pb 248 bunches
Protons no burn off in collision
Pb: large burn off
UFO ALICE ?
Access
Struggle with beam SPS and QPS problem
SPS problems
PS POPS
BPMS limit
5e12 charges

## Slide 3: Lumi’s over the week
ALICE finished low-bias data taking on Thursday
LHCb
1e29 cm-2s-1
ATLAS & CMS

## Slide 4: Production of 2 nb-1 / day

## Slide 5: Fill statistics – ALL fills
Fill | Day | Peak L [cm-2s-1] | Stable beam [h] | Int L [nb-1] | Dump
3479 | 21/01/2013 | - | - |  | RF cogging
3480 | 21/01/2013 | - | - |  | RF cogging
3481 | 21/01/2013 | 6.10E+28 | 10:11 | 1.2 | Operator
3482 | 22/01/2013 | 6.40E+28 | 11:55 | 1.5 | BPMSA.B4R6.B2
3485 | 23/01/2013 | 1.00E+29 | 09:23 | 1.9 | BPMSA.B4R6.B2
3486 | 24/01/2013 | 1.10E+29 | 05:27 | 1.35 | BPMSA.B4R6.B2
3489 | 24/01/2013 | 8.44E+28 | 05:59 | 1.1 | BPMSB.B4L6.B2
3490 | 25/01/2013 | 1.00E+29 | 06:29 | 1.4 | BPMSB.B4L6.B2
3493 | 25/01/2013 | 9.50E+28 | 05:17 | 1.1 | BPMSB.B4L6.B2
3494 | 26/01/2013 | 8.50E+28 | 06:21 | 1.1 | BPMSB.B4L6.B2
3495 | 26/01/2013 | 9.50E+28 | 06:11 | 1.2 | BPMSB.B4L6.B2
3496 | 27/01/2013 | 9.00E+28 | 06:02 | 1.2 | BPMSB.B4L6.B2
3497 | 27/01/2013 | - | - |  | UFO ALICE?
3498 | 27/01/2013 | 1.00E+29 | 06:11 | 1.4 | Operator
 | Polarity change |  |  |  | 
47 % in Stable Beams, Total Lumi 14.4 nb-1

## Slide 6: Excellent availability – stats pages

## Slide 7: RF cogging / BLM thresholds
First fills of the week beams dumped on BLM losses 9L7.B2 at moment of frequency change to bring proton and ions beams on the same RF frequency.
BLM thresholds pushed up at quads 7, 9, 11 R&L at 7
Shower from primary collimator
B2

## Slide 8: … source of the problem: understood
Protons and ions injected at their central frequency
Moving frequencies to ‘common’ mean value at 4 TeV, so later on one can make collisions
This moving of the frequencies is done in steps
command "lock both frequencies on beam 1" was executed while the frequency trim was still on going.
A pause was added and no overshoot anymore
Orbit evolution during cogging and re-phasing.
Overshoot in mean orbit

## Slide 9: BPMS interlock
BPMSs are interlocked BPMs at point 6 which check that the orbit is such that the dumped beam will pass through the dump channel
  Interlock set at +/- 3 mm
4 BPMSs for each beam at either side of IP6
For low (ion) intensity the signals become noisy and bunches are seen outside the window
  Happens between 3 – 4 e9 charges for the ion beam
Interlock per ‘window’
  100 turn window increased count 70 -> 500 -> 2000 false counts on one BPMS
  After this change this specific BPMS did not trigger anymore but the next one did…

## Slide 10
B1
B2
3.65p/bunch
Zooming vertical axis
B1 and B2 bunch charges
23/1/2013 @ 20:30:38 IR6 BPMs analysis
Eva Calvo
25-10-2013
LHC status

## Slide 11: Dump of fill 3494
BPMSA.B4R6.B2 2000/100
BPMSB.B4L6.B2 70/100
Would have dumped if window not changed
This BPMS dumped

## Slide 12: Roman Pots – moved in
Modified sequence for moving in the pots tested with the specialist: OK
Since then both TOTEM and ALFA moved in at the beginning of the fill by the operation crew
  Vertical only at 13 
  Proton side only
  Loss maps made with pots in
No problems so far

## Slide 13: Longitudinal blow-up at injection
At injection, to reduce increase of transverse emittance
1.4 ns target
Worked after some testing during injection steering
Observables
  Initial lumi: does not seem to be match larger. Not really gained.
  BSRT / BGI: needs further analysis, no absolute calibration

## Slide 14: ALICE UFO (?) / BPMS / Polarity reversal

## Slide 15: ALICE polarity change: last night
ALICE spectrometer polarity change.
External crossing angle changes in collision: needs set-up of collimators at IP2 (TCTs).
First cycle:
  No beam: change polarity, change target external Xing in physics.
  Inject. Correct H orbit by hand, incorporate into ramp GRADUAL_OUT (~almost like 1/E).
  Run through the cycle with a few bunches up to end of squeeze. Orbit FB will take care of any residual error up to end of squeeze.
  3 minute test on FT to calibrate the BPM scale with RF frequency trims (for energy calibration).
  Run collision BP, TCTs in IR2 to be handled separately, I recommend opening the TCPs temporarily to 6 sigma to avoid losses from the orbit change. The H orbit in physics will require a correction. Find collisions in IR2 (if needed). Incorporate back orbit trims (! rule).
  Align the TCTs around the new orbit in IR2. Perform loss maps etc
Offline:
  Prepare new TCT functions for IR2 (collision BP).
  Update all orbit and COD interlocks (SIS+Kajetan).
  Feed-forward orbit RT trims (if worthwhile).
Second cycle:
  Validation of corrections and TCT functions. Test on FT.
Jorg and collimation team

## Slide 16: Last Night
20:10 Operator dump
22:47 Ramp for collimator set-up, orbit, lumi, TCTs
  Took 15 mins to align 4 IP2 TCTs
01:30 Loss maps
  Full set of betatron loss maps performed (preliminary analysis: all OK), as well as negative off-momentum loss map
02:39 Beams dumped by negative off-momentum loss maps
03:33 Lost RB.A12 power converter fault
04:15 Cycling
05:25 Water circuit problem affects the booster, no protons
07:23 Beam back
07:57 Ramp started
Now
  Another low intensity ramp for IP2 collimator validation and positive off momentum loss map
  Followed by preparation for VdM scans

## Slide 17: The Plan
Shorter term plan
  Polarity change – done
  Verification fill with low intensity and loss map: on now
  V/d Meer scans = today
  Ion source refill – Wednesday
  pPb to Pbp change – about Thursday / Friday
Between ion source refill and quench tests in 2 weeks:
  pPb physics ! Possibly pp intermediate energy run
  ADT set-up for quench test preparation: 4 – 6 hours
  BSRT tests at 450 GeV few hours with few trains of 1.4e11 bunches
    In parallel dump B1 at injection with high intensity trains for pick-up test
  Real time squeeze test (beta* levelling) – 4 hours
  Longitudinal damper tests, at injection, 1 beam only, 2 – 4 hours
Mon 11th Feb: quench tests for 48 hours
Bye-bye-beam

## Slide 18: Access
Access requests:
  Wire scanner, J.Emery, point 4, 2 hours.
  Collimators UJ33, test position sensors, M. di Castro, A.Masi, 20 minutes.
  “Train”, B.Feral, D. Paulic, PM56/UL55, 1 h during working hours
  BGI, M.Sapinski, R4, ½ h
  LHCf has a problem in a part of the frontend electronics placed in the tunnel, we would like to ask a two hours access at the next opportunity in the shadow of the other activity. Takashi Sako
  Quench Test on Q6.L8 – the scope is not yet in place, 1h in the UA. Mateusz Bednarek
  CMS cryogenics – filter to be cleaned
  Ludovic Mourier 165232 Restore pump for QRL insulation vacuum in sector 45 (which has a leak)
  LHCb – 3 hours
  ODH detector is in ALARM in UJ1
Up to the next coordinators: Bernhard Holzer, Jorg Wenninger
  After V/d Meer