## Slide 1: Ion Commissioning: Thursday & Friday
B1 Inj., Circ. & Capture
B2 Inj., Circ. & Capture
Optics Checks BI Checks Collimation Checks
First Ramp Collimation Checks Squeeze

## Slide 2: Debunching at injection

## Slide 3: Friday Morning: Collimation checks at 450 Z GeV
Check collimator alignment
  Gap centers checked for 11 collimators per beam. Reproducibility from proton to ion at 0.4mm level. OK for injection nominal settings and probably for intermediate settings as used at 3.5TeV.
Loss maps: Betatron cleaning inefficiency:
  Leakage to dispersion suppressor: 0.5% - 2%
  Experimental IR's: clean
  Arcs: 0.1%
  RF: clean
Loss maps: Momentum cleaning inefficiency:
  Leakage to dispersion suppressor: 0.5% - 4%
  Experimental IR's: 10% (TCTH in IR1, b2), 1% (TCTH in IR5, b1)
  Arcs: 0.3%
  RF insertion: 0.5%

## Slide 4: Conclusions from Ralph A.: collimation @ 450 GeV
Loose about factor 50-100 in cleaning efficiency for ions, compared to protons. This is expected (ion fragmentation and dissociation)
Main losses in predicted locations, namely the dispersion suppressor magnets. Maybe losses occur somewhat earlier in space than expected
We see a large 10% leakage into IR1 from IR3 losses for beam 2. It is not clear what ion species escapes IR3 and travels to IR1. To be analyzed in detail
OK for injection and ramp to 3.5 TeV
As ion species form independent "beams" we worry about potential high energy losses into IR1. Therefore request of full set of loss maps at 3.5TeV before a squeeze is performed
                DONE

## Slide 5: 141 BLM screen dumps in 1.5 hours !
Momentum losses B1 -1000Hz
Momentum losses B2 -1000Hz

## Slide 6: Asynchronous Beam Dumps at injection
Dump protection OK: There was essentially no leakage to the TCTs during the async. dump of both beams, so I think everything is fine! Chiara Bracco

## Slide 7: BGI:
not uniform signal strength, in general better for vertical BGIs.

## Slide 8: Schottky data – Ralph Steinhagen
Plus: Re-verified FB operation - FB's OK

## Slide 9: 16:25 start first ramp – no beam losses
There is light a bit above 0.5 Z TeV
Bunch length up at injection, down during the ramp
Emittances on flat top: B1; H=5.5 , V=5.6 B2; H=5.8 , V=8.7

## Slide 10: More loss-maps at 3.5 Z TeV – ok-ish
negative frequency trim of -1000Hz for negative off momentum loss map

## Slide 11: 22:15: first squeeze finished: perfect trajectory
Wirescans afer squeeze: B1-H: 7.1 B1-V: 6.5 B2-H: 6.8 B2-V: 10.1
Wirescans @ injection: B1-H: 4.5 B1-V: 3.1 B2-H: 5.1 B2-V: 4.5

## Slide 12: First programmed dump at 3.5 TeV
No surprises for dump of a bunched beam at 3.5 TeV
B1
B2

## Slide 13: Beta Beat Checks at 3.5 Z TeV, squeezed
AC-dipole fixed from last night: reboot controls
Looks very similar to protons
Rogelio

## Slide 14: Work over night
Asynch dump tests at flat top
  to be analysed in detail but looks ok
Next ramp: loss maps after the squeeze
  To be analysed in detail
B2: Q_H trimmed to 0.34

## Slide 15: Chromaticity through the ramp

## Slide 16: Plans
Saturday | Find collisions 2 x 2 bunches Collimation – loss maps Asynchronous dump Stable beams 2 x 2 bunches | 
Sunday | Stable beams, increase # bunches 2 x 17, 2 x 128 bunches |