## Slide 1: Thursday 04/11 - Morning
Access until ~13:00
  Mostly for BI for BPMs and ion changes
  ALICE, CMS
Pre-cycle
Proton checks:
  BCT calibration with ~15 probe bunches
  BPM orbit reference for high sensitivity setting

## Slide 2: Thursday PM – ions in the lines
18:00 : Ions extracted to TI2/8 TEDs.
  A bit of steering of the trajectories. No problems.
B1 in TI2 before correction (wrt proton reference)

## Slide 3: Thursday PM – ions to the LHC
Adjustment of the offsets LHC-SPS to place ions bunch on the MKI of B1.
20:20 First 75+ trajectories in the LHC.
B1 turn 1 compared to proton closed orbit – not bad !!

## Slide 4: Circulating B1
20:30-22:00 RF : placing bunch into correct bucket.
  BLM thresholds on IR2 triplet magnets set back to 0.1 (were reduced to 0.03) to avoid unnecessary PMs from beam to TDI.
22:00 B1 captured and circulating for many seconds.
B1 ion orbit compared to proton orbit – no steering !

## Slide 5: B1 progress

## Slide 6: Beam2
01:00: Beam2 injected OK.
01:50: Both beams circulating.
  Lifetimes around 10-20 hours.
  Stepwise losses on B1.

## Slide 7: Optics measurements
Initially some problems with AC dipole in H, solved by kicker expert – arming issue.
  Q-kicker used.
Optics in good agreement with protons.
  Many BPMs do not trigger in capture mode.

## Slide 8: Losses with kicks

## Slide 9: Beam parameters
Intensity:
  Around 1-1.2E10 – sometimes even too high to be a probe beam cannot inject into empty ring).
Emittance:
  Both beams around 1.0-1.2 um just after injection (! with Pb gamma) – nominal. Proton equiv. emittance 2.5-3 um.
  Beam is blowing up quickly to 3-4 um.
Energy calibration: from RF frequencies of protons and Pb:
  fRF[p] = 400.788876 MHz
  fRF[Pb208]=400.784230 MHz
  >> Energy[p] = ~450.0 GeV – prel. error around 0.4 GeV

## Slide 10: Plans
Friday 5/11 – AM | Collimation 450 GeV, loss maps BI, RF
Friday 5/11 – PM | First ramp, collimation checks, possibly squeeze.
Friday night – Saturday | Collimation on flat top, squeeze etc