## Slide 1: Saturday 06/11
Triplet R8 tripped during ramp for collision setup.
Lost status of access door (YCPS04=Uj56) and patrol in Pt5.
  Patrol found the door (slightly ~ 1 cm) open, but contacts were such that LASS saw it closed – until the patrol was lost.
Access to Pt8 to fix triplet PC RQTX.R8.
  Triplet finally back in operation around 18:00.
Pre-cycle. Beam delayed by MKI problem and water problem in TT2.
Beam in at 21:30.
  BPM interlock test.
  Ramp & squeeze.

## Slide 2: Saturday lat evening
00:30: Colliding in all IPs with TCTs at 25 sigma.
  With proton settings for Xing and lumi scan knobs (ALICE separation to 0).

## Slide 3: Saturday PM – collision setup
Xing in ATLAS and CMS to 0. Xing in ALICE to 0 effective Xing angle.
  External angle -140 urad.
Optimized orbit and beam overlap.

## Slide 4: Saturday night
01:45 TCT collimator setup.
04:02 Beam dumped during TCT movement in Pt2.
  Triggered while moving in TCTVB.4L2 between 15-20 sigma.
  5 TCTs setup in B1, 3 TCTs set up in B2
    All TCTH B1, 3 TCTH B2 (miss Pt2), TCTVA.4L5.B1
QPS OK issues on RB.56.
  Two issues on the same circuit: heater PS.
Access finishing soon…
Intensity issue on the ion source (factor 2 weaker than in the last few days).
  Investigating…

## Slide 5: Dump

## Slide 6: Bunch lengthening

## Slide 7
Emittance increase seen by BSRT – V plane

## Slide 8: Collimator loss map end of squeeze (b* 3.5 m)
Loss map analysis (R. Assmann):
  Leakage IR7 to:
    DS: 1-2%
    Arc: 0.1-0.3%
    IR3: up to 30% (H plane)
    Exp. IRs: clean

## Slide 9: Plan
Sunday AM | Collimator setup to finish
Sunday PM & Night | Loss maps (betatron & off-momentum) Asynch dump test Stable beams 2x2
Monday++ | 4b cycle and injection Stable beams 17x17, 128x128 etc