## Slide 1: Summary of week 25
R. Assmann, J. Wenninger
with the support of many !
Goals:
Luminosity production
1236 bunches

## Slide 2: Fill overview
Fill length – saw the extremes !
  very long or super short
Fill | Bunches | Peak L (cm-2s-1) | Length (h) | Int. L (pb-1) | Dump cause
1883 | 1092 | 1.1E33 | 18 | 47.5 | SIS – no orbit data
1889 | 1236 | 1.26E33 | 2.7 | 10.7 | AUG TI2
1890 | 1236 | 1.15E33 | 14.1 | 45 | Cryo Pt5
1893 | 1236 | 1.15E33 | 0.6 | 1.8 | Vacuum B2, IR4
1894 | 1236 | 1.15E33 | 2.1 | 8 | Vacuum B2, IR4
1895 | 1236 | 1.15E33 | 0.3 | 0.4 | Vacuum B2, IR4
1898 | 1236 | 1.15E33 | 1.8 | 7.3 | S34
1900 | 1236 | 1.25E33 | >6 | 22 | 
Total |  |  | 46 | 142 | 
46 hours over a week : 27%
Friday !

## Slide 3: Week 25  Sunday PM
1092
1236
1.4E14
SPS RF
Strike
Thunderstorm
1E33
2 days lost…
Intensity
Luminosity

## Slide 4: Records – all (except lumi?) in week 25
1236 bunches colliding at 3.5 TeV
Stored energy : 81 MJ
Longest fill 1883 @ 1092b : 18 h
Most productive fill 1883 : 47.5 pb-1
Record luminosity : 1.26(7) x 1033 cm-2s-1
  More or less same peak with 1092 and 1236.

## Slide 5: From 1092 to 1236, and beyond
Initial fill with 1236 saw more or less the expected intensity increase.
Subsequent fills (except last) had lower luminosity.
  Mixture of lower bunch intensity, possibly larger emittance.
  Emittance differences are difficult to evaluate.
  Rocky operation did not encourage to push bunch intensity.
At the present stage increasing bunch intensity or lowering emittances can have more effect on L than increasing the number of bunches.
In principle we could move on to 1380 bunches – was foreseen at some point for Sunday.
  Machine protection is no longer dictating the pace.

## Slide 6: Integrated luminosity
Approaching 1.2 fb-1.
We have peak lumi, but we have too little integrated lumi !
~0.12 pb-1/week
~0.2 pb-1/week

## Slide 7: ‘Faults’ – the integrated L suffered from
The major events:
  Cryo problem (compressor Pt8) week 24 ~ 3 days,
  Thunderstorm in week 25 ~ 1 day.
The usual suspects:
  Dump by and access for QPS (or EPC).
  Injection issues.
Random events:
  SPS RF noise,
  AUG TI2,
  Work stoppage,
  SIS interlocks.
Weekly systematic ‘series’:
  Vacuum spikes/valve closures in IR4.
A proper mix of those takes us out very effectively !

## Slide 8: Cryogenics
Last Monday a problem was discovered on one of the compressors in Pt8 – clogging the oil filters.
  Compressor had to be stopped.
Serge’s team is making miracles.

## Slide 9
QUI
Leaky HX (Jan’11)
TuA (Spring11)
P8 configuration, last week
CCs
CCs
CV615 valve (P2)
Tests for relocation
Validated for P2 (TS) !
Sector 78
Sector 81

## Slide 10
QUI
Leaky HX (Jan’11)
TuA (Spring11)
P8 configuration, week-end
CCs
CCs
CV615 valve (P2)
Tests for relocation
Validated for P2 (TS) !
Sector 78
Sector 81
Extra flow
Until next Tech. Stop if CP6 oil filter OK, otherwise …
Similar to CP6_P4 ?
Some 35’000 hrs since Jan’07 !!!
Limitations

## Slide 11: Cryo bake-out L8
During stop:
Temp BS >> Temp Mag
=> Bearly visible effect, re-cooling process confirmed ?
“Bake-out” at 35K-40K
Heater
Tinlet
Toutlet
Vac. gauges
Valve

## Slide 12: Thunderstorm – Wednesday afternoon
A pretty bad power cut:
  Lost all sectors,
  Almost all experimental magnets,
  Cryo in pt8 (due to cooling water stop),
  All patrols around Pt3,
  Many crates in underground area – power.
24 hours to recover, given by cryo.
  Many people could hide in the shadow of cryo: repair on Thursday morning rather than Wednesday night.

## Slide 13: Vacuum IR4
Problem started in night of Saturday to Sunday.
3 consecutive fills dumped by B2 vacuum interlock in IR4 – valves closing.
Identical signatures for all dumps.
  Not understood. Consistently seen on all nearby gauges.
  Sunday morning vacuum interlock threshold increased from 4E-7 to 2E-6 for VVGH.1174.5R4.R.
D3.R4
D4.R4
Q6.R4
Beam2

## Slide 14: Vacuum spikes fill 1894
Spike during stable beams
Dump

## Slide 15: Last night
It is still there… and we got close. Saved by the threshold increase.

## Slide 16: BLM signal – vacuum dumps
For all dumps the BLM @ BGI downstream of vacuum spike region B2 shows unusual losses over ~ 1 second.
  Loss is orders of magnitude below BLM dump threshold

## Slide 17: SIS interlocking of beam position at TCSG/TCDQ IR6
One squeeze was dumped on orbit excursion at the TCDQ in IR6 – one BPM developed a lightly offset.
  Eventually readjusted the reference as it goes into the safe direction  closer to the TCDQ.
  Check alignment after TS?
  Nice case for BPMs integrated into collimators.
Squeeze
Ramp
Collisions

## Slide 18: Injection
Injection continues to be delicate.
Variability of the trajectories in TI2/B1 seems to come from the MSE extraction septum in SPS LSS6.
  Ripple of 2E-4 (@ 20’000 A) – EPC is on it.
TI2 is very sensitive to transverse and longitudinal tails in the H plane.
  One collimator with large H dispersion at 4.5 betatron sigma close to the LHC. Critical source of beam loss crosstalk..
Due to drifts of various elements, it is no longer possible to center beams in collimators (or in the BPM nearby) and to inject perfectly on the closed orbit.
  Too many constraints.
  Realignment to be considered…

## Slide 19: MSE correlation
Simulations of the observed PC ripple/noise (from logging) point to the extraction septum MSE as source.
  ‘Logic’ as this is by far the strongest magnet string (~10 mrad).
Verena, Lene

## Slide 20: B1 MKI pulse length
During the trajectory optimization on Monday, it was observed that the 144 bunches of B1 do not fit on the injection kicker waveform.
  The last 5 bunches are systematically kicked.
  Pulse length for beam 1 shorter than for beam 2:
    beam 1: 7.85 us
    beam 2: 8.1 us.
The MKI pulse length was increased by 200 ns on B1.
  Situation is now much better.
  One could increase by another 50 to 100 ns.

## Slide 21: Loss maps
The periodic (1/month) loss maps were performed in the night from Thursday to Friday.
  Full set at injection. Some signs of degradation.
  H, V and dp/p < 0 in collisions at 3.5 TeV. Looking good.
450 GeV, H, B2 – not so nice…

## Slide 22: UFO front – status Sunday PM
No drastic change with 1236 bunches…
1236
T. Baer

## Slide 23: But last night….
Strong UFO activity at the MKI in 2. This time correlated with vacuum activity.

## Slide 24: And a large UFO last night – MKI2
Saved by recent threshold increase?

## Slide 25: Lifetimes
B1 lifetime frequently worse than B2 – cause not understood. Clearly visible in IR7.
  Example of fill 1898.

## Slide 26: Lifetimes
B1 lifetime was lower in all fills except fill 1890.
  Larger emittance of B1?
B1
B2

## Slide 27: Shit happens… in particular with SW
In the last fill an automated system (code name BIGSISTER), when (re)started on a test server, accidentally switched the mode to BEAM DUMP during stable beams…
Seems to have been a big mess – sorry !

## Slide 28: Powering
RPLA.26R2.RCBH26.R2B1 needs access to repair.
  We can operate without it for the moment. Nor urgent.

## Slide 29: Next
From MPP side it is OK to move to 1380b.
  But vacuum spikes still present.
  Today is the last chance before the MD/TS.
Tuesday late afternoon: 90 m optics setup + some data-taking for TOTEM/ALFA.
Wednesday morning MD -> TS next Monday.