## Slide 1: Tuesday morning
Magical fix of QPS quench loop problem in S23 and S56
Access for EPC (supported by QPS) to investigate a possible loose contact on the circuit RSF2.A81B2:
  no loose connection was found and EPC changed the power module.
EN/EL also profited from the access to install a monitoring tool on the electrical distribution of the QPS of RQ10.L8 (tripped several times in the past).
ATLAS and CMS in access.

## Slide 2: Tuesday morning
After fixing all hardware problems, some difficulty to run the collimators (FESA class and proxy restarted at point 7) and to unlatch a fault on the SIS (old version – missed software update).
Performed a dry ramp and check that everything was working fine. Brought the machine back to injection.

## Slide 3: Tuesday afternoon
15:15 Beam (52 hours after initial lightening strike)
16:09 Lost a BLM crate, cfv-sr7-blmr. Christos Zamantzas checking…
16:19 BIC IPOC failed as one of the BICs did not send the postmortem buffer. Proxy issue?
  Problem resolved (Bruno Puccio & co) around 18:00
16:36 A. Masi also re-calibrated the TCLIB.6R2.B1 after the power cut.
  This time with the injection plateau as reference. The difference to the previous position are now in the order of 20 um to the previous values. The interlock levels were trimmed back to the original ones.

## Slide 4: Tuesday afternoon continued
17:08 Electrical network glitch
  RD1.LR5 - FMCM
  LHCb dipole
18:30 Beam back briefly and then BLM crate problem reprised
18:45 Crate CFV-SR7-BLMR is completely down now and cannot be rebooted by Christos.
  In the end he did not change anything. The crate is up and running. The problem is not understood and might reoccur.
20:15 Beam back

## Slide 5: Early Wednesday morning
Inject and dump
  after the modifications of the LBDS BIS inputs during the technical stop.
  10 times per beam
  XPOC never latched...and is also faster than it used to be.
Beam Presence Flags
  Values from the logging: B1 -> 1.27e9p B2 -> 1.24e9p
Without beam - trip of the Q6.L8B1 due to the water flow problems again. Reset but it tripped again - access from the CV team.
Postpone the collimation studies (including injection loss maps) until this morning.

## Slide 6: Wednesday morning
The access in P8 lasted until about 3h00.
Precycled the whole machine and injected probe beams at around 4h30 for a pilot ramp, squeeze and collide.
Run through the full nominal cycle without problems.
Ramp and squeeze done with radial modulation. Collapsed the separation bumps but did not optimize collisions.

## Slide 7: Incoming
Pilot + 2 nominal bunches
  1 hour in stable beams
  Loss maps at 3.5 TeV
Verification tests:
  TCDQ and TCSG relative position checks
  Asynchronous dump 450 GeV B2
  Loss maps at injection & collimator checks
48 bunches per beam - stable beams for 3-4 hours
Continue with the satellite collision scheme 264b, 840b
  CMS back sometime Friday…