## Slide 1: Saturday 7.4.2012

## Slide 2: Saturday Morning and Afternoon
7:58 Fill 2483 (264 bunches) dumped by reference orbit set to zero in V plane in the last step of the squeeze  new SIS interlock triggered as it should
Problem investigation
Fill 2484 to test the procedure for collisions in IP8 (3 bunches);
12:13 dumped by OFSU problem during squeeze
Fill 2485: Corrected the beam process for going to LHCb tilted crossing without having head-on collisions at LHCb.  tested successfully
Loss maps: B1 H + V, B2 H + V + longitudinal (-500 Hz)
19:17 – 20:47 stable beams fill 2486 (84 bunches)
  Average intensity
    start of ramp: 1.35x1011 ppb
    start of stable beams: 1.33x1011 ppb
  Initial luminosity: 2.9x1032cm-2s-1
  1.4 pb-1delivered in 1:36 hour

## Slide 3: Saturday Night
22:00 – 23:23 no beam from SPS: trip of main power supply (Depart 18 kV BA3) – only 36b missing for B2
0:48 – 5:09 Fill 2488 stable beams (264 bunches)
  Average intensity
    start of ramp: 1.34x1011 ppb
    start of stable beams: 1.31x1011 ppb
  Initial luminosity: 9.6x1032cm-2s-1
  10.5 pb-1delivered
7:17 Fill 2489 stable beams (264 bunches)

## Slide 4: Orbit feedback missing reference
Problem with transmission (or reception) of the references to the OFSU
Caught with the new SIS interlock
Found a way to diagnose the problem before launching the squeeze  repeat the sequencer task sending the orbit references till they are received all right
Origin of the problem to be investigated/solved next week
Missing orbit reference

## Slide 5: OFSU crashing during the Squeeze
Problem unrelated to the previous one
OFSU reconnected automatically and with the correct reference orbit, but it was disarmed.
   rearmed it  it did take the correct reference, but with a scaling factor of zero  beam dumped by SIS
   if it had not been rearmed, it would have continued with a frozen orbit reference and the SIS would not have dumped. It would have driven the orbit towards the collimators.
   SIS interlock for OFSU down was reduced to 9 sec during the squeeze by Joerg, to catch this problem. Deployed and tested successfully.

## Slide 6: LHCb tilted crossing
Translating of the procedure into functions:
0 – 40 sec:
  Reduce vertical separation -650 um-> -100 um
40 – 60 sec:
  create vertical crossing angle 0 -> + 90 urad
100 sec – 220 sec:
  create horizontal separation 0 -> + 42 um to get the beams in the leveling plane (diagonal)
  collapse horizontal crossing angle -> 0 urad
All positions calculated relative to the measured (30.3.) position of the head-on collisions.
All signs apply for beam 1 and have the opposite sign for beam 2.
All settings for positive LHCb polarity.

## Slide 7: Fill 2486
LHCb: beams stay separated during the physics process; automatic leveling worked fine
CMS: collapsing of the separation goes to far  updated settings
Some vacuum activity
  4L8 and 6R7

## Slide 8: Fill 2488 – 264 bunches
Atlas and CMS separated to 75% peak luminosity and stay with constant offset for 1st hour
Atlas and CMS at 100% for 2nd hour
3rd hour separated to 75% again (2:59)
3:20 – 3:50 Sudden losses on several bunches
4:04 back at 100%
5:09 beams dumped

## Slide 9: Fill 2489 – 264 bunches
Atlas and CMS separated to 95% peak luminosity and stay with constant offset for 1st hour
8:24 Atlas and CMS at 100% for 2nd hour

## Slide 10: Fill 2488 – 264 bunches, cont.

## Slide 11: Others
Tune change in the collisions beam process:
  B1: previous increase was reverted back to a flat function
  B2: increase by 2E-3 both planes
ADT: increased by a factor of two (from 0.02 to 0.04) on Friday
Trip of ADT (module H2B1)
At the moment: tune FB off during squeeze and collision
Problems:
  Orbit feed-back reference
  High losses on some bunches

## Slide 12: Planning

## Slide 13: Planning
Friday till Monday the morning meeting will be at 9:00
Tuesday 8:30 summary of the week
2-3 fills and 4-6 hours with 264b and 624b (cycle validation)
3 fills and 20 hours with 840b, 1092b, 1380b (intensity/lumi related problems)

## Slide 14: Intensity ramp-up
2-3 fills and 4-6 hours with 48b, 84b, 264b and 624b (cycle validation)
3 fills and 20 hours with 840b, 1092b, 1380b (intensity/lumi related problems)
MP checklists after 84b, 624b, 840b, 1092 bunches
Regular MP checklists every two weeks when operating with 1380b
Bunches | Max number of bunches injected | Alice
3 | 1 | Main-main
48 | 12 | Main-satellite
84 | 36 | Main-satellite
264 | 36 | Main-satellite
624 | 72 | Main-satellite
840 | 108 | Main-satellite
1092 | 108 | Main-satellite
1380 | 144 | Main-satellite