## Slide 1: Monday morning
08:30: Fill with 2 nom. bunches/beam to collisions.
  LHC polarity – (PC).
  Vertical lumi scan correction consistent with polarity +.
  Horizontal lumi scan corrections differ by 60 um/beam ~ 1 sigma.
  Functions for collision BP updated with the new settings.
10:00 TCT alignment check in IR8.
  LHCb separated to initial state for leveling.
  TCT settings consistent with pol+ settings within 0.5 sigma.
11:00 Loss map with standard collimator settings (the ones established for LHCb pol+).
  Betatron and off-momentum (+500 Hz), all OK.
  Losses for V plane B2 down a factor 20 in IR2 – as expected with corrected TCTV position.
  B1V loss map OK but weak (too little beam)  to be repeated.

## Slide 2: Morning/ afternoon
12:00 In the ‘shadow’ of the ramp-down exchange of a weak BLM card – generated fake dumps correlated to temperature. Introduced a delay of 4 hours…
  Problem with a BI BLM application for HW parameters due to a special crate configuration.
17:00 Start of TDI check – nominal position 6.8 sigma
  Jaw alignment with ADT blowup, TCP defines reference.
  TDI.B1 upper/lower : 6.4/6.5 sigma
  TDI.B2 upper/lower : 6.5/6.6 sigma
  Both TDIs are slightly further in, but within tolerance.
  Checked protection of TDI for oscillations in phase with TDI – ok.

## Slide 3: TCP versus TDI
TDI losses
TCP losses
TDI position

## Slide 4: BPM interlock IR6
BPM crate in IR3 fixed.
BPM interlock check IR6.
  Quality of the results have not improved. Too many triggers (again) on a BPMSA.B4R6.B2.
  Checks not complete – to be done (again).
  More sensitive with probe to injection oscillations? tbc

## Slide 5: Evening
20:30 RF cavity phasing for B1.
  Check after discovery of loose cable before TS1.
  2 modules were found 9 deg out of phase.
  Settings now close to April 2011 situation.
23:30 Loss map at flat top.
  Betatron and off-momentum loss map (+500 Hz). Looking good.
During the recovery problem with mode change.
  DB storage issue – solved by CO-DB expert.
03:00 Filling for 84+4 bunches.
  Injection not great… 1.2E11 / bunch.
05:30 Stable beams
  Lumi peak in LHCb when going to collisions?
  IP5 (again) rather far off.

## Slide 6: LHCb lumi

## Slide 7: Early morning
06:03 Power glitch – 400 kV
  Site wide glitch.
  All PCs tripped.
  All exps off except for CMS.
Cryogenics partially affected (S12, S34, S45, S81).
  Cold compressor Pt2 stopped, quickly restarted.
Access.
  LHCb, ALICE…

## Slide 8: Plan…
Recover machine – end of the morning?
84+4b / length scale
  What about ATLAS?
MKI8 kicker synchronization
480b
…and loss map in collision to be repeated.