## Slide 1: 10.12.2009
-Spend night from Tuesday to Wednesday recovering from QPS problem in
sector12 (RCBXH1.R2)
Problem could be overcome by masking PC in the PIC configuration.
-09:15: both beams circulating
-10:00: Starting LHCb run with spectrometer off
-11:00: starting transverse IP adjustment test in IP5
worked fine from machine point of view
but lifetime of Beam2 degraded rapidly  test not useful for CMS
-12:00: Preparing access for work related to high intensity beam operation:
    access in IR2, IR8 and IR6 for LBDS
    access collimators: IR3 (PRS module in electronics rack)
    access in IR4 (RF damper & BI for synchrotron light undulator)
    access for some miscellaneous activities (TOTEM)

## Slide 2: 10.12.2009
-17:00: Finished access
Some problems with ACO23 and triplet orbit correctors in
-18:00: synchrotron light monitor at 400 A
-18:30: Beams again ready for injection; starting LBDS studies:
-inject and dump mode in Beam & circulating Beam
-21:15: Lost Cryo in S78 (heater for RQTL7.R7B2)  requires intervention
continue beam studies on TED before access at 00:00
-01:15: recovering powering conditions after access
several technical problems (trip of RQS & RSS circuits in S23;
RQ6.L8B1 [cable water fault]; trip of RSD1/D2.A67) could all be rest
RCBXH1 & 2 R8 tripped during pre-cycle
-03:40: circulating beam back again

## Slide 3: 10.12.2009
-04:00: Problems with injecting 4th bunch for Beam2
Problem related to abort ‘gap keeper’ adjustment
 requires access or new filling scheme
 continue for now with 3 bunches per beam
-06:00: Prepared fill with 3 on 3
Beam1 lifetime not good due to vertical tune (3rd order resonance)
-07:45: Beams dumped and preparing new fill with better tune settings
-

## Slide 4: 10.12.2009: Plan for the day
-test transverse IP adjustments in IP5 at beginning of next fill
(quick optics verification at end of next fill)
-9:00: finish stable beam setup for higher intensities
(asynchronous dump with unbunched beam etc.)
-noon: Injection test with higher bunch intensity (single bunch).
-early afternoon: Collimator setup verification with higher intensities (e.g. 2 1010 / bunch).
-Late afternoon and night: Stable beam collisions at 450 GeV with high bunch intensities:
4 x 2 1010 per beam