## Slide 1: Friday
08:00 Quick reset RCBXV1.R1
Pre-cycle
Check of beam in transfer lines
11:00 Start inject and dump
  BLMs in S56 giving no signal
  wrong settings in TI8
  PM from BLM 7R8
  Inject and dump – only 1 turn (10, 100 demanded)
  Circulate and dump
  Orbit correction required – L2 – Alice?
  Measure and correct tune (nominal) and chromaticity (2,2)
  injection oscillations
  beating not nominal – effect of access/limited precycle?

## Slide 4: Friday afternoon
TDI to tight settings and re-positioned to beam
15:34: over-injecting beam 1 & 2 OK
Long voyage of discovery
  Switching cycles in SPS between PROBE and INDIV
  Re-phasing issues in SPS on INDIV
  Transfer line trajectories different
  Frustrating times as witness pilot kicked out when higher intensity beam from SPS doesn’t come(oscillating BPF – 5.2 e9 OK for flag and over injection)
  20:30 – 2e10 injected with over-injection
  Rough adjustment of TCDIs in line to minimize down-stream losses (clear issue)
Brennan & team…

## Slide 5: Friday evening
Now working with INDIV only
  inject 8e9 and QKICKER down to 5.2 e9
  inject 6 e10
    BPM interlock in IP6 fires (x2)
    Disable interlock
    Then get caught by orbit excursion interlock
    Mask and BPM sensitivity set to low before injection of 6e10
00:03 6e10 in
  injection losses OK
  orbit good
00:30 8.8 e10
00:42 11.5 e10 in but RF loses it – beam still circulating in various buckets

## Slide 6: This morning
Scrape beam on primaries and dump what’s left
6e10 circulating, lifetime around 600h. This beam is for Philippe to adjust the RF for higher bunch intensities.
01:48 11e10 injected OK
  orbit tune emittances etc
6:13 STABLE BEAMS

## Slide 9: Losses around ring with 11e10

## Slide 11: Program
Pre-cycle
Re-establish circulating beams
  new values for b3 decay and snapback in place, chromaticity to be carefully measured and corrected
High intensity tests at 450 GeV
Test ramp (check Q’ in snapback)
Leading into squeeze
  quick run through to 2 m in IP 1&5
  squeeze to 2 m, in IP8
Go for stable beams overnight


Possibly to be on hold