## Slide 1: Tuesday 17.8.
Morning: Bunch Train Studies:
  08:00: Ramp down after unsuccessful ramp for Beam2 loss maps (Beam2 dumped by SIS);
    QPS errors: RQTD_A56B2 & RQTL11.L5B2. (resolved by swapping boards);
  09:30: injection of probe beams: XPOC error due to wrong published energy (4106 GeV);
  09:00 to 11:00: Setting up of the SPS for new Hyper cycle for bunch trains.
  11:00: Setting up the SPS for injection into LHC (orbit & transfer line trajectories etc.)
  12:30: QPS problem for RQTF.A81B1  switch boards;
  12:50: Injection of first train into LHC  (injection into wrong bucket traced back to missing seyting needed in the rephasing)
  14:40: First Successful injection of train into LHC
  Switching on the crossing angle in Pt 2 at 100 urad, in steps of 50 urad (target 170 urad). Worked O.K. but losses above dump threshold observed in Pt 2 with the 100 urad settings.
   ready for other systems (ADT, RF…) to make test on 1 train of 4 bunches ( B1)

## Slide 2
Orbit in the LHC for injection with bunch trains:
Orbit after LHCb
spectrometer
polarization
change:
Top: initial orbit
for new polarity
Bottom:
After correction.

## Slide 3
Beam Losses in the LHC during injection with bunch trains

## Slide 4: Tuesday 17.8.
Afternoon:
Dispersion measurement IR3 & loss map for Beam2 at 3.5 TeV:
  16:00: Lost beams when turning on the Q feedback (locked onto hump).
  Lost Beam 1 during orbit corrections  unclosed spectrometer bump with inverted LHCb spectrometer polarity (new know for closing the bump in IR8).
  18:20: Start ramp.
  20:00: End of squeeze and adjust.
  20:20: Dispersion measurement for both beams:
    Dispersion beat for Beam1 slightly larger than for Beam2.
  21:00: Measuring loss map for Beam2 with DFRF = -1000Hz (beam moves outwards)  Hierarchy for Beam2 seems to be violated.

## Slide 5
Tune and Hump with damper on:
Beam 2: Vertical tune and Hump signal
are approximately equally
strong with damper on.

## Slide 6
Dispersion measurement:

## Slide 7
Dispersion measurement: Beat in normalized Dispersion

## Slide 8: Collimators – Loss maps on momentum Stefano Redaelli, Walter Venturini, Joerg Wenninger
1bx1b, Physics conditions -1000 Hz RF trim
BLACK = collimators
RED = warm elements BLUE = cold elements
TCTs see about ~0.01 of the primary loss spike and the cleaning efficiency to the cold elements is 99.25% (4 stage hierarchy is respected).
Operation with 25 bunches can continue in these conditions
To be repeated for B2

## Slide 9
Loss map for Beam2 with RF frequency trim:
Beam 2 loss
map for
DFRF = -1000Hz

## Slide 10
Beam Losses in the LHC during injection with bunch trains
Daniel Wollmann:
The hierarchy is violated in this case: The TCSG.B5L3.B2 acted as primary collimator.
One can also see, that the losses
on the TCLA.A5L3.B2
are quite high
(~64% of the losses at
the TCSG).

## Slide 11: Tuesday 17.8.
Night: Struggling to get beam into the machine:
  22:10: QPS problem on RQTD.A56B2 and RQTL11.L5B2  switched boards;
  22:30: Problem with fast BCT for Beam1  no beam signal on page one;
  00:20: Beam 1 probe dumped due to RQTL10.R7B2 trip (redundant power supply)  could be reset after check with MP3 expert;
  00:50: SPS has problems with the longitudinal blowup  no nominal bunches;
  01:50: Beam1 pilot dumped due to vacuum valves going in for S23; Valves closed for both B1 and B2. Problem appears to be a circuit breaker on a rack for the electronics of the gauges and pumps around Q6L3.  requires access
  02:50: Finished access; Fault was caused by 220V power bar trip, most likely due to overloading. They balanced the load by using an adjacent 220V power bar.
  03:00: Pre-cycling S23 & S34 (RCBWV5.L3B1, XPOC, BQM in SPS);
  04:00: Start new injection setup;
  06:30: Loss of QPS OK on RQF.A67 stops injection (twice);

## Slide 12: Wednesday 17.8.
Morning: Physics fill with 25 bunches:
  07:00: Injection;
  07:25: Start ramp;
  09:00: End of squeeze and stable beams;
  Emittances: ex1 = 3.0 mm; ey1 = 3.0 mm; ex2 = 3.4 mm; ey2 = 4.0mm;
  Initial peak luminosity: L = 3 1030 cm-2 sec-1;
  Planned end-of-fill studies:
   Damper studies ay 3.5 TeV

## Slide 13: Wednesday 18.8.
Morning: Keep physics fill in until afternoon.
  End-of-fill studies for damper and L readjustment.
  Short access for quench heater power supply repair in S12.
Afternoon:
  Collimator studies for IR3.
Evening:
  New Physics Fill.

## Slide 14: Week 33
Open Issues for next Technical Stop:
  CMS cooling for central tracker.
  Ion pumps in dump line MKB (B2 only 4 out of 8 pumps working; few days intervention).
  BLM racks (in buildings SR1 and SR5 and both at position BY02): would like to correct the way the power cable for the multi-plug arrives inside the rack.
  QPS boards: several boards had to switch from channel A to B.
  Access team to replace oxydized connectors for PAD-PX24 (3 hours).
  CV needs to replace a motorization of the water valve of the sector 56 (3h).
  RCBH18.R7B2 – Miguel Cerqueira Bastos.