## Slide 1: Wednesday 16/3
08:30 – Dumped physics fill with 3 x 3 bunches
AM: Investigations on tune feedback Ramped 8 nominal bunches again, which stayed in this time, although perturbations still there. Collide 8 bunches. Dump.
PM: No beam
  Problems with RF re-phasing: “there is a large static error on the synchro loop”
  BST MASTER reboot
  PS no beam
Evening: Continue investigations. Spectrum looks very different for 32 bunches compared to 8 bunches
  20:40 Ramp 32 nominal bunches
  Lost because of RQTD trips – but different signature
  Problem with timing distribution
Night: Requalification of systems. Collimator problem.

## Slide 2: The 8 bunch ramp that stayed in - lucky
Tune-trim B2 H
OK when tunes moved for collisions

## Slide 3: Tune feedback / spectrum issue
  Problem: With 8 nominal bunches beams were lost at 3.5 TeV twice on Tuesday. “100 Hz” peaks in tune spectrum for B2 H makes tune feedback jump around, resulting in RQT trip.
At injection: Changing damper gains at injection -> makes tune measurement more stable
At 3.5 TeV switch off ADT -> perturbing lines still too large relative to tune lines.
Reduction of damper gain

## Slide 4: 32 bunches at injection – spectra look different
32 bunches
8 bunches
ADT off

## Slide 5: Ramp 32 bunches
Lost in ramp RQTD.A12B2 and RQTD.A67B2 tripped off
But tune signals were proper this time
Previous trips were RQTF and at flat top
RQTD U-res not noisy, but is sudden spike
PM, XPOC, logging thoroughly messed up
  Switching the LHC Timing Gateway from A->B
Jump in Time

## Slide 6: QPS of RQTD reacted correctly

## Slide 7: Recover
As a result of this timing card switch, preformed a set of checks to confirm that the timing was OK and that the dump and PM was behaving as expected. Tests done:
  Dry dump to check PM
  Dump with pilot at injection to test PM etc
  Ramp with pilots and then taken through the collisions BP
Tried to fill physics with 3 bunches – waiting for experts to report on “timing issue”
  Collimation problem, TCTH.4L5.B1 position interlock at start of squeeze, expert working.
  BPM calibration problem

## Slide 8: The Plan
Confirmation from experts everything ok
  Timing
  Collimation
Ramp 32 bunches, aiming for stable beams
To do:
  Collimation energy interlocks