## Slide 1: Saturday 23/4
09:30 Important blow-up during filling due to large drift in chromaticity. Dump and re-fill.
10:20 Beam 1 kicker not firing due to missing pre-pulse. Beam (36 bunches) on TDI cleanly
12:30 Stable beams #1732. 480 bunches/beam. Initial luminosity up to ~5.2x1032 cm-2 s-1 (ATLAS)/~4.8x1032 cm-2 s-1 (CMS).
06:20 Power glitch. End of fill #1732
  Close to 24 pb-1 in ATLAS after almost 18 hours in physics.
  Integrated 25.6 pb-1 in one day.
We are now at 132 pb-1 delivered.
We are now recovering (6 sectors tripped)

## Slide 2: Chromaticity decay
After 1.5 h form injection field still drifting by +2.5/hour H and -2/hour V

## Slide 3: Failed injection
Missing pre-pulse form LHC RF distribution while injecting Beam 1 only  logging going to be implemented to understand behaviour in the future
Beam (36 bunches) on TDI  ALICE detector triggered the beam dump+BLMs
Vacuum valves closing near to TDI due to outgassing. Fast recovery.

## Slide 4: #1732
>0.5 x 1033 cm-2 s-1

## Slide 5: #1732
Need tight control of the chromaticity at injection within 2 units
Reason for tighter limits as compared to scrubbing not clear, yet:
  Different filling pattern?
  Operation of the damper to be optimized?

## Slide 6: #1732
No blow-up along the trains

## Slide 7: #1731
Blow-up observed along the trains responsible for the poorer performance

## Slide 8: #1732 vs. #1731
ATLAS:
  1732
  1731

## Slide 9: #1732

## Slide 10: Beam lifetimes
Tested effect of the octupoles on the beam and luminosity lifetime. No clear sign observed.

## Slide 11: Satellites and intensity distribution
After adjustment of the extraction kickers in the PS yesterday no satellite visible after the 12/36 bunches train (should be the case for fill 1732). Some satellites close to main bunches (~10 ns?)
Still some work to be done in equalizing bunch intensities

## Slide 12: Plan
Fill for physics with 480 bunches (trains of 72 bunches)

## Slide 13: Issues
Logging of pre-pulse distribution for injection by RF
BSRT  stability of the pattern (take the BQM?) and fixed display