## Slide 1
LHC Status Sat Morning 9-July
Bernhard Holzer, Ralph Asmann, Kati et al
Tentative Planning:
Fri 22:00h cryo ok expected in the complete machine
last sector 81 switching on power converters, preparing restart
Sat 00:00h precycle, injection of one pilot per beam, test ramp the pilots to check
whether everything is ok.
Sat 03:00h injection 1 pilot & 1 nominal bunch per beam,
loss maps at injection,
1h collisions for ATLAS (the other experiments will surely profit)
important for this Atlas run is the “pilot-on-pilot”, declaring stable
beams is not needed but might be helpful.
Afterwards: loss maps at collision (same beam can be used).

## Slide 2
LHC Status Sat Morning 9-July
Bernhard Holzer, Ralph Asmann, Kati et al
Tentative Planning:
Sat 08:00h precycle, injection: 48 bunches per beam
new fill pattern for “satellite collisions in ALICE”
keep in stable beams for 3-4 hours (depending on the experiments)
Further planning:
using the new fill patterns
establish collisions
264 bunches per beam ... some hours collisions
840 bunches per beam ... a nice long collision run
1380 bunches per beam ... back in business (hopefully)

## Slide 3
9. July
To Do List
B2 TCDQ positioning 450 GeV
- cross-check of offset between TCSG and TCDQ jaw, with beam
- asynch dump test for B2 with pilot bunches or with 1-2 nominal bunches, at 450 GeV.
- during first pilot ramp, monitoring of TCDQ jaw position wrt interlock thresholds (anyway data logged) and comparison with last ramp.
Injection system:-
On MKI – B1 work has been performed on the terminating resistors. As a result the MKIs are likely to fail in IQC. A few tens of pulses are required to obtain statistics, then call Etienne Carlier who will update the IQC – MKI limits (call during day time).
- When we start to inject the longer trains from the SPS (for Alice satellite collisions) we most likely need to extend the MKI pulse length slightly and change the mcs reference values accordingly. Check with Brennan when this needs to be done.

## Slide 4
9. July
Status
19:19h hardware commissioning
20:46h trip of Atlas toroid and solenoid
22:33h ramping up ALICE SOLENOID
04:10h Cannot close the extraction switches of RQF/D A78.
04:14h Updated estimation from cryo:
full recovery at about 8 am