## Slide 1: Thursday
Access, access, interventions.
  RF investigations – localized the problem.
  MKIs.
  Optical fibers IR7 monitoring (fibers for LHC access system !).
  Cryo interventions (auto-resets Pt 5/7, compressor config, etc).
  WPS/HLS in Pt5.
  CV Pt5.
  QHPS in S12.
  ATLAS, ALICE, CMS.
  SIS fix for RF voltage, MKI temperature intlk now independent for 2 & 8.
  Master thresholds for 10 TCSGs IR7.

## Slide 2: Thursday evening
Dry ramp and squeeze to 1.5 m, followed by squeeze test to 1.0 and 0.55 m.
  RF interlock in SIS good again.
  1 m OK, 0.55 m  trip of all RQ6’s. Seems to come from B2.
  Beta* information not correct below 1.5 m. New conversion tables I to beta* checked. They will be updated during the TS.

## Slide 3: RF on beam1
Philippe BAUDRENGHIEN:
Without beam, Cav4B1 at injection settings had a large phase noise, locked at 4x frev. Cured by cold reset of the firmware.
Similar issue found on Cav4B2 – with lower amplitude. Not solved by reset. Gain reduced on loop for the moment.
All cavities checked.
Cav4B1
Cav4B1
after reset

## Slide 4: SPS
Magnet in place and ready for pumping ~17:00.
First beam ~21:30.
Conditioning of the local vacuum with 50 ns beam.
  4 batches at 450 GeV at 23:05, conditioning…
  Extractions slightly readjusted in H.
00:00 LHC closed – last RF access finished.
01:40 Beam back in the LHC.
Injection oscillation corrections with 12b.
Filling a bit rocky.
  Interrupted by a reboot of the timing FEC (mastership issues).

## Slide 5: Bunch lenths

## Slide 6
Vacuum activity at MKI in the ramp.
Stable – ‘modest’ Lumi given the intensity of almost 1.3E11/b.

## Slide 7
B1 lifetime low, but no dip when colliding..

## Slide 8: Today
Physics.
Loss maps in collisions, probe+2b – slotted in when it fits (daytime).

## Slide 9: Fill Overview
Fill | Phase | Peak L [1033 cm-2s-1] | Length [h] | Int. L [pb-1] | Dump cause
2009 | STABLE | 2.1 | 15.3 | 76 | Sector 81 trip (QPS quadrupoles)
2010 | STABLE | 2.05 | 18.8 | 85 | RQT12.R7B1 (QPS-SEU?)
2011 | STABLE | 2.1 | 8.5 | 45 | SIS interlock (comm. To RF FEC)