## Slide 1: Mon 26.03.12
8:00 lost cryo compressor in p2
  Problem due to noise picked up by instrumentation, cryo operator knows how to mask it if it comes back.
  Accesses:
    BPMD, exchange of RCVB25.R4B1, BI for the BSRT
    Cable adapters were removed from BPMD cables in IR6 in order to check if the multiple triggers came from reflections generated at their level.
  LBDS asynchronous beam dump test (with no beam). Kicker synchronization was OK, but asynchronous with the beam.
  Orbit reference changes now in a display of YASP. During the ramp/squeeze the current target orbit is highlighted in yellow.
  Tests performed on RD34.LR7, FMCM problem.
11:00 Cryo is back - access ongoing...
  trying to sort out the problem with RCD.A34B2. Fixed…
13:00 Machine closed. Pre-cycle.

## Slide 2: YASP Improved Display Reference Orbit

## Slide 3: Mon 26.03.12
14:30 Injecting...
  Problems with communication to PCs leading to beam dumps. Loss of energy interlock on SIS. Cleaning up rogue clients solves the problem.
  Sequencer:
    Added task to switch off the energy feedback in the ramp-down sequence
    Added task to disable the RT trims at the start of the collisions sequence.
  Deployed new OFC version that includes the feed-forward corrections on the energy trim bump. New functionality not yet enabled/settings remain the same as yesterday. Ralph St.
  Investigating orbit- & energy-FB issue, and problem of '0' RT reference glitches on 120 A CODs.
    The RT inputs of LSS/DS 120 A CODs seem to jump to exactly 0 at regular intervals. We could not find any arc corrector with this problem.
    Understood and fixed: Interference between orbit and tune feedbacks.
  Orbit reproducibility now OK! Ready for collimation setup.
    Problems with OFSU process crashes

## Slide 4: Mon/Tue 26/27.03.12
17:45 Preparing to inject nominal.
  18:50 Beam went on the TDI. Erratic trigger just before injection. Called Etienne who will be looking.
  LBDS: problem of checking retrigger signal
Summary of injection protection setup
  Started with setup of TCDIs in TI 8:
    measured center
    put them to +/- 5 sigma, trimmed in values and thresholds
    checked with injection of nominal and losses were OK
    details in entry 8 at 00:37
    validation still to be done
  Checked TCLIA.4R2 (critical one after ALICE polarity flip last year)
    checked only lower jaw angle with 0 and +/-1.5 mrad
    found symmetric results - --> no angle to be applied
  TCLI centers not checked, TCLIB to be set at 8.3 instead of 6.8 sigma

## Slide 5: Mon/Tue 26/27.03.12
  Setup of TDIs:
    angular alignment, found angles and center for both TDIs
    same angles (within meas. accuracy) as last year, applied angles
    rechecked with beam based alignment (defined edge with TCP)
    found sigma 0.75 for B1 and 0.76 for B2 instead of nominal 0.57 mm
    trimmed in settings and thresholds for nominal sigma --> more conservative
    injected nominal bunch with losses OK ( bad inj. oscillation for B2)
    validation still to be done
  Results for TDIs:
    left jaw angle [urad] right jaw angle [urad] TDI.B1: +65 -750 TDI.B2: -170 -140
  Final settings in mm for TDIs:
    LU LD RU RD TDI.B1: 9.14 9.29 -1.54 0.11 TDI.B2: 6.92 7.29 -2.58 -2.27

## Slide 6: Tue 27.03.12
Pre-cycle
06:41 – injection probe beam
07:40 – Ramp
08:04 – 4 TeV

## Slide 7: Ahead
Tuesday
  08:00 -13:00 Pilot (and later nominal) bunch through full cycle (4TeV), collimation expert to manually adjust TCT's to measured orbit shifts, test of fast 4TeV collimation alignment
  14:00 - 22:00 TCDQ setup at 450 GeV
  23:00 Pilot bunch through full cycle (4 TeV)
Wednesday
  05:00 - 20:00 Collimation setup at 4 TeV
  21:00 Injection and beam dump work (until Thu 05:00)
Commissioning measurements to be scheduled:
  k-modulation with nominal bunch intensity for beta*=0.6m
  additional aperture checks at 4 TeV with beta*=0.6m
  Loss maps…