## Slide 1: Monday 10th December - morning
08:15 prepare for access
Access:
  UJ87 for TDI.4R8 fix
  UX67 and PM18 for cryo check
  UX451 for checking cabling for BQK
  ATLAS
  CMS
  UJ56 for IT alignment control system check
  Intervention on IT.L5 monitoring has been fixed (by reset of crate, crate has been left on internal supply mode, which doesn't compensate for cable length, but this is not considered problematic as the difference is small anyway)
  UL55 for QPS power cycle on B9L5
    Still the same problem on magnet B9L5 after QPS reset..

## Slide 2: Monday 10th December - afternoon
11:50 Cycling
13:00 Injecting probes
Test ramp, squeeze to 1 m, and collide with new collimator functions
Beam lost in collision BP
  Orbit from 0.6m does not work well enough --> lost B1. Next time we start from the end of squeeze orbit and set-up the collisions completely
14:20 Beams dumped
15:50 re-injecting – 3 nominals through cycle
17:06 Beam lost on flat-top – cryogenics – heat wave - sector 81

## Slide 3: Mon 10th to Tues 11th December
22:40 Cryo-start – given with reservations – front still propagating through the arc
  Cycling again
Set-up at 450 GeV: TDI.4L2
  Error on upper left limit – couldn’t retract – piquet (JEROME, LENDARO) called – noisy LVDT
  Standard LVDT (still) gives an interlock on the gap – switch to spare
  Workaround: open thresholds to parking; move out TDI; re-close
02:50 Flat-top
03:30 Looking for collisions (JW assisting from home)
Incorporated the lumi scans at the knob level and the orbit H and V at the K level.

## Slide 4: Tuesday 11th December - morning
05:00 Beams dumped
Back around again with 3 nominals for collimator set-up
08:00 Beams colliding – collimator team into action (Stefano and Gianluca)… ongoing

## Slide 5: Program
Tertiary set-up in collisions – loss maps at end of exercise
TCT set-up end squeeze (loss maps & asynchronous dump)
Plus 1 – 2 fills to finish loss maps (push these to overnight)
Couple of hours today (in between the ramps for the loss maps) during working hours to verify the injection of the h=9 25 ns beam
Once the loss maps are finished Wolfgang and Daniel will need 2-3 hours to set-up the damper with lower bandwidth for minimizing noise in collisions and in particular for the physics run.
First 25 ns ramp approximately tomorrow morning