## Slide 1
Controls for LHC startup
E. Hatziangeli Sep. 2008

## Slide 2
Timing
No issues. New versions of the LHC gateway RT task, LTIM and CBCM performed correctly without any problems
XTIM rock solid!
Access to equipment - Equipment servers (FESA/CMW)
BT, Collimators, RF OK
BI
  BLM OK BPM some FEs instabilities observed by the concentrator – BI investigates
  Observed BCT, BTVs,, BSRT,.. FEs accessed by several clients => degradation of FEs
    Solution with CMW fanout GW (one cliet access the FE) is being investigated - deployed asap
PO stable
  New CMW release today to correct rare bug (asynchronous CMW commands) causing crashes
E. Hatziangeli Sep. 2008

## Slide 3
Logging
Full logging on all systems applied => No data loss, no issues observed
  General logging
  LHC Collimators
  BPM logging
  BLM logging
  FGCs – 0.5Hz fixed rate + on change
Database
  Timber was used extensively => lots of queries => high CPU usage
    Investigating solutions to spread the system load over all of the hardware resources in the cluster
RBAC settings
RBAC-policy = lenient
RBAC behaved correctly during the test
  Last minute OP decision to use “Public” Consoles in the center of LHC bay for LHC Operations => had to be quickly authorized for operations
Plan to move to stricter policy soon for PO and BI
  Property protected : token needed and rule is checked
  Property not protected : grant and no token needed
E. Hatziangeli Sep. 2008

## Slide 4
Looking into ….
High load on consoles – CCM visual indicator to be implemented
Certain GUI applications take a lot of resources – being investigated
JMS service does not handle well misbehaving clients – exponential backup will be implemented in JAPC
FESA/CMW consolidation continues – less critical bugs are being addressed
RBAC
  automatic renewal of token will be implemented
  Improvements on the A1 role picker component
OASIS
  Signal configuration – commissioning support of the system
Logging
  New requests for logging is being processed (BI, RF, ..)
E. Hatziangeli Sep. 2008

## Slide 5: Summary
Stable performance of the Controls Infrastructure, no issues on Timing, Logging, Databases, RBAC, FESA/CMW servers, ..
Controls successfully supported the LHC startup
E. Hatziangeli Sep. 2008