## Slide 1: Week 34
Physics fills (bunch intensity 0.9  1.1e11 p):
  #1298 (Sun/Mon): 48b x 48b. Beam dump due to fast beam losses in IR3 (MQ22.R3). (8h18).
  #1299 (Tue): 48b x 48b. Duration physics 3h16. Beams dumped due to RD1.R2 trip.
  #1301 (Tue/Wed): 50b x 50b. Duration physics 14h26. End-of-fill studies.
  #1303 (Thu): 50b x 50b. Duration physics 13h14. Beams dumped with fast beam loss event Q25.R5. Luminosity > 1031 in ATLAS and CMS!
  #1305 (Fri): 50b x 50b. Duration physics 3h30. End-of-fill studies. Delivered integrated luminosity in 2010 > 3,000 nb-1
  #1308 (Sat/Sun): 50b x 50b. Duration physics 13h42. Programmed dump.
  #1309(Sun/Mon): 50b x 50b. Duration physics 11h00.
Total time in physics in past 7 days: 67h26 (~40% of time), > 1.5 pb-1
In addition, commissioning work…
About 3 shifts lost with access in LHC or injectors.

## Slide 2: Current History (up to Sun noon)
Massi Ferro-Luzzi
48b x 48b
Bunch-train commissioning
50b x 50b

## Slide 3: New Record Lumi

## Slide 4: Integrated Luminosity in 1 Fill
370 nb-1 over 13 hours.

## Slide 5: New Fill Pattern
Goal: Avoid parasitic crossings in IR2 and IR8.
Therefore: 48b x 48 b  50b x 50b
Expect: Lower losses and higher luminosity lifetime.

## Slide 6: Intensity Loss Fill 1298 (first 2 h)
  IPs: 1 5 2 8 - 1 5 8 - 1 5 2 - 1 5 - 2 8 - 8
1 LR in 2 (33m)
1 LR in 2 (33m)
1 LR in 8 (33m)
1 LR in 8 (33m)
1 LR in 2 (22m)
1 LR in 2 (22m)
no Long Range interactions
with Long Range
48b x 48b

## Slide 7: Intensity Loss Fill 1295 (first 2 h)
  IPs: 1 5 2 8 - 1 5 8 - 1 5 2 - 1 5 - 2 8 - 8
1 LR in 2 (33m)
1 LR in 2 (33m)
1 LR in 8 (33m)
1 LR in 8 (33m)
1 LR in 2 (22m)
1 LR in 2 (22m)
no Long Range interactions
with Long Range
48b x 48b

## Slide 8: Intensity Loss Fill 1301 (first 2h)
  IPs: 1 5 2 8 - 1 5 8 - 1 5 2 - 1 5 - 2 8 - 8
no Long Range interactions
with Long Range
50b x 50b

## Slide 9: Intensity Loss: summary across fills
48 bunches
50 bunches

## Slide 10: End of Physics Fills
In total 7 physics fills over last week.
2 fills dumped by fast loss events: MQ22.R3 and Q25.R5.
1 fill dumped by QPS trip
2 fills ended with end-of-fill studies (normal end).
2 fills ended with programmed dump (normal end).

## Slide 11: Beam Dump with Fast Loss
Q25.R5

## Slide 12: Beam Dump with Fast Loss
Q22.R3

## Slide 13: Other Beam Loss Events
Fast beam loss spike at primary collimators.
RF trips.
Beam dump due to losses during chromaticity measurement.

## Slide 14: Loss Spikes in Stable Beams
Intensities
Loss at primary collimators B1

## Slide 15: Loss Spikes in Stable Beams
factor ~30 in BLM at TCP
not visible in lifetime
~50 h

## Slide 16: RF Trip: cavity 2B1

## Slide 17: Dump During Chroma Measurement

## Slide 18: Other Work on Physics Beams
Tune feedback
Loss maps for regular collimation monitoring
Beam distribution and loss modulation
Luminosity-Induced Losses

## Slide 19: Tune Detection Improvement
Tune detection affected by noise ion the beam.
Reducing the time-constant responsible for the DC suppression of the peak voltage variations of the longitudinal carrier to help reliable detection.
N.B. gains stayed the same.
See curves: Blue before, red after change.
R. Steinhagen

## Slide 20: Beam Loss Maps (Regular Monitoring)
Beam 1 vertical
Beam 2 vertical
IR7 cleaning still quite good since June 12 setup. Being analyzed in detail.
IR3 anomaly probably also seen for beam 2  will be fixed with bunch train setup. Not done yet.

## Slide 21: Measuring Tails (10 min end-of-fill)
Jaw towards beam
Beam Loss
Jaw position
TCP.D6R7.B2

## Slide 22: Beam Intensity
- 1.5e11 p
- 3.5 %
Beam dumped from beam loss on Q5 in IR7 (warm) with 84 s integration time!

## Slide 23: Beam Distribution: Beam 2 Tail V
sy = 0.27 mm
~ 5.7 s
~ 4.7 s
~ 3.7 s
3.5% of beam within 1.5 s

## Slide 24: Beam 2 H Tail after 3h30 of Physics
Florian Burkart et al

## Slide 25: Loss Locations Around Ring
IR7 TCP: 30,000 mG/s
IR7 Q5 (warm): 1,700 mG/s
IR7 Q8 (SC): 18 mG/s
8 s

## Slide 26
IR7 Q10 (SC): 0.8 mG/s
IR6 TCSG: 900 mG/s
IR6 Q5 (SC): 12 mG/s

## Slide 27
IR5 TCTH: 6.5 mG/s
IR5 Q11 (SC): 1.3 mG/s
IR3 TCLA: 8 mG/s

## Slide 28
IR2 TCTVB: 5.5 mG/s
IR2 TCTH: 1 mG/s
IR1 TCTVA: 3.7 mG/s

## Slide 29
IR8 TCTVB: 4 mG/s
Easily identify all collimation-related losses around the ring.
Notice temporal shift between measurements around ring (8s). Could explain puzzling previous observations: cold losses before losses at collimators!
See loss distribution and efficiency for vertical losses.

## Slide 30: Luminosity-Induced Losses IR1: Selection
IR1 TAN L
IR1 TAN R
IR1 Q3L (SC)
Beam dump

## Slide 31: Luminosity-Induced Losses IR5: Selection
IR5 TAN L
IR1 TAN R
IR1 Q1R (SC)
Beam dump

## Slide 32: Luminosity-Induced Losses IR8: Selection
IR8 Q1L (SC)
IR8 Q1R (SC)
Beam dump

## Slide 33: Luminosity-Induced Losses IR3
Luminosity: ~ 5e30 cm-2 s-1
Induced losses Q7.L3: 5e-7 Gy/s
Quench limit Q7 at 3.5 TeV: 4.7e-3 Gy/s
factor 10,000 margin at 3.5 TeV for factor 2,000 in lumi  might become critical for luminosity at 7 TeV with lower quench limit (predicted bottleneck – high dispersion)
IR3 Q7 L (SC)
Beam dump

## Slide 34: Bunch Train Commissioning
Work hampered by bad quality of injected 150 ns trains.
Problems:
  SPS tune kicker acting randomly.
  SPS transverse blow-up not working.
  SPS scraper breaking.
Some injections OK, then really bad losses.
Might have seen first SEU error due to heavy beam loss at transfer line collimator.
Seen interesting effects on beam lifetime.
In the end out of 2 shifts only a few hours for work on transverse damper.

## Slide 35: Losses in TI2 and LHC Ring (14h03)
Beam 1

## Slide 36: LHC Inj. Losses (16h14, Beam 2)
At same time:
Loss of QPS-OK on RB.A81, on magnet A8R8
4 nominal bunches
injected

## Slide 37: Long-Range Effects on Lifetime (450 GeV)
1b x 1e10
per beam
4b x 1e11 without
crossing angle 2 beams
4b x 1e11, 1b x 1e10 no crossing angle
4b x 1e11 with
crossing angle in ATLAS&CMS
2 beams

## Slide 38: Beam 2, horizontal plane, kicking a batch of 4 bunches/150ns by Q kicker. Graph shows how oscillation of each individual bunch is damped. Beam was gone before measurement of bunch 4
Daniel Valuch, Maarten Schokker, Gerd Kotzian

## Slide 39: Verification of damping times for different electronic gain values. 150ns settings, beam 1, horizontal plane. Note that currently used gain at injection is set to -20dB.
Daniel Valuch, Maarten Schokker, Gerd Kotzian

## Slide 40
Transverse Damper Planning
complete low noise set-up with new firmware for all dampers, started 27.08.2010
evaluate the 150 ns scheme now deployed
run for Physics with this scheme (already used in a few fills)
introduce the required improvements after 20.09.2010
required improvements are:
full damping strength for edges of batches
full damping strength for bunches at large spacing
improvements may need a filling scheme identifier from control system (LSA) communicated to damper software / crates
W. Hoefle

## Slide 41: Outlook Bunch Train Commissioning
See Malika’s presentation at last LMC.
Possible sequence of detailed tasks (my view):
  Recover machine from technical stop. Run 1 nominal bunch through full cycle with present setup.
  At 3.5 TeV measure beta*, triplet-to-beam offsets with k change technique.
  At 450 GeV, introduce crossing angles.
  Commission injection (incl. protection) for at least 12 bunches per train (nominal bunch intensity). Sufficient for factor 3 intensity increase.
  Check instrumentation, RF and transverse damper. Tune if necessary.
  Re-establish reference orbit for 450 GeV.
  Perform required re-setup of ring collimators (depends on orbit changes). Regenerate collimator functions for ramp, including change to 10 A/s.
  Qualify collimation and protection with loss maps at 450 GeV. Asynchronous dump test.
  Commission ramp to 3.5 TeV with 10 A/s and with crossing angles.
  Re-establish reference orbit at 3.5 TeV before squeeze.

## Slide 42: Outlook Bunch Train Commissioning
Continued…
  Perform required re-setup of ring collimators (depends on orbit changes). Include new setup for momentum cleaning of beam 2 (not working).
  Qualify collimation and protection with loss maps at 3.5 TeV before squeeze. Asynchronous dump test.
  Re-commission the squeeze, with any possibly required changes in beta* for IR2 (from 3.5m to 10m?).
  Measure beta* and triplet-to-beam offsets with k change technique.
  Optimize collision point.
  Re-establish reference orbit at 3.5 TeV after squeeze.
  Perform required re-setup of ring collimators (depends on orbit changes).
  Qualify collimation and protection with loss maps at 3.5 TeV after squeeze. Asynchronous dump test.
  Ramp with high intensities.
  Check instrumentation, RF, transverse damper and feedbacks at 3.5 TeV. Tune if necessary.

## Slide 43: This week…
This week: Mike Lamont and Gianluigi Arduini