## Slide 1: Tuesday
08:30 – 14:30 Accesses
14:30 – 16:30 Pre-cycle and wait for the SPS still verifying the beam to be delivered
16:30 – 21:30 Difficulties at injection with Beam 1 in spite of the small emittance  go to filling scheme with max. 16 bunches/injection. As a set-up of the injection is required.
22:40 Collisions but for a short time  dump due to BLM in LSS7
Not possible to inject with intermediate emittances (~1.8-2 um)  Reduced intensity and go back to small emittance. In spite of that and of steering not possible to inject 16 bunches  Start preparing VdM scan.

## Slide 2: Access
Access:
  Injection area investigations (radiation survey, alignment, X-ray)
  Installation of a magnetic probe L3
  Cryogenics in PM85
  UPS in UX45  One battery will need to be changed during the technical stop
  Current lead for RCBXH3.R1: leaky cryo-valve, temporary fix. Final solution during tech. Stop
  RCBH15.L6B1 power converter replacement
  Intervention on energy extraction switch for RB.A81: found bad connection on a micro-switch but not clear whether this is the source of the trips observed (probably not)
  RadMon installation close to the controls of the solenoid
  In parallel: change of GPS repeater

## Slide 3: Injection area investigations at the MSI
Suspected aperture restriction at the transition MSIB-MSIA
Confirmed by radiation survey showing a maximum (although small: ~4 uSv/h) at the suspected transition

## Slide 4: Injection area investigations at the MSI
Alignment survey did not show any important misalignment at the MSI, only some important tilt observed at the BTVSS
Chart: Survey of the MSIs in LSS2
| 3086.2886499999986 | 3091.088639999999 | 3091.4556499999999 | 3094.8556400000002 | 3117.7136500000001 | 3121.7136399999999 | 3122.16365 | 3126.1636399999998 | 3126.6136499999998 | 3130.61364 | 3131.0636500000001 | 3135.0636399999999 | 3135.5136499999999 | 3139.5136400000001 | 3139.888649999999 | 3140.6386399999997 | 3159.6266499999992 | 3163.0266399999991 | 3163.4076500000001 | 3166.80764
Horizontal | 4e-05 | 3e-05 | 3e-05 | 3e-05 | 0.00035 | 0.00086 | -3e-05 | 0.00024 | -0.00023 | -8e-05 | -0.00017 | -0.00025 | 6e-05 | -0.0001 | -0.00038 | -0.00058 | 0.00011 | 0.00013 | 0.00013 | 0.00015
Vertical | 0.00091 | 0.00089 | 0.00089 | 0.00087 | 0.0006 | 0.00071 | 0.00057 | 0.00086 | 0.00078 | 0.00063 | 0.00076 | 0.00062 | 0.00062 | 0.00066 | 0.00104 | -0.00044 | 0.00057 | 0.00056 | 0.00056 | 0.00055
tilt | 0.07 | -0.16 | -0.2 | -0.3 | -0.34 | -0.1 | -1.15 | 0.08
D. Missiaen

## Slide 5: Injection area investigations at the MSI
There is a clear problem with the RF fingers at the transition. Not clear how did it get worse suddenly. Need to find a different injection trajectory, for the time being while preparing an intervention for the technical stop or the Christmas stop
JM. Dalin
New setting-up to be done this afternoon after the VdM scan

## Slide 6: Injection
Difficulties to inject trains of 24 bunches in spite of the small emittances at injection (~1.3-1.6 mm)
Increased vertical bump of the injected beam at the MSI area
Change of the filling scheme to 256_240_8_224_8 with 17 injections and bunch trains with a maximum of 16 bunches
Finally got 256 on 256

## Slide 7: Collisions
Lifetime dip to ~1 hour recovering to 5 hours
BLM 83 s running sum triggered the beam dump
Luminosities compatible with emittances of ~2 mm for a beam-beam tune shift of approximately >0.02 (for bunches seeing 3 collisions)

## Slide 8: Collisions

## Slide 9: Today
AM: Van der Meer scan. Should be kept to the minimum necessary
PM: Injection setting-up with up to 24 bunches for B1.
Night: Physics

## Slide 10: Outstanding requests for studies
Periodic loss maps (not really MD)
  Betatron loss map done week 40.
Orbit shift versus TCT check: collide 1 bunch and check the TCT center change as compared to predicted orbit change.
BI
  PLL studies during ramp
  Commission BGI in preparation to ions – switch on at injection
  Other BI studies – list to be updated
  Test of 'dynamic' references for the OFB (varying Xing.separation bump): injection, then test of ramp + first part of squeeze.
BT
  Abort Gap Cleaning – on at injection for physics
  Injection Studies 32 Bunches when required (344 bunches)
Setting-up of the SPS with tighter batch spacing (225 ns) - ongoing

## Slide 11: Access Requests
Verification of the flange alignment between MSIB and MSIA
IR1 solenloid (for e-cloud suppression) controls

## Slide 12: Scheduled lift maintenance
Some preventive maintenance has been requested on the LHC lifts, and agreed according to the following planning:
  Wednesday 13 October: PZ65 from 8h to 12h00; PM76 from 13h30 to 17h30
  Thursday 14 October: PM45 from 8h to 12h00; PZ45 from 13h30 to 17h30