## Slide 1: Friday 26.11.
05h44: Stable beams #1521. 121b x 121b. Length: 4h10.
09h54: Beam dump.
  Instability on electrical network (RD.LR1 tripped).
  ATLAS solenoid ramp down.
Look at Q9.R2 trip from Thursday…

## Slide 2: Trip of RQ9.R2 on November 25, 08:06:39
As already noticed by A. Verweij, there is a symmetric development of a voltage signal in the two halves of RQ9.B1; the two voltage loops go from the current leads up to the magnet mid point
U_2_B1
U_1_B1
U_Res_B1
M. Pojer

## Slide 3: Trip of RQ9.R2 on November 25, 08:06:39
1- Similar signals were observed during the symmetric quenches on the dipoles
2- An EM disturbance would have produced a much noisier signal
Could radiations be at the origin?
No counts were recorded on the RADMONs from 4.R2 up to 12.R2 in the
time frame from 6h30 e 12h00
Courtesy of M. Calviani
M. Pojer

## Slide 4: Trip of RB.A81 on November 25, 23:59:00
I_ref
I_meas
U_Res
The PC in SPA  I_ref goes to 0 and current goes down  U_Res rises and generates a FPA
M. Pojer

## Slide 5: Friday 26.11.
11h01: Injection. Second oven (ion source) is on.
12h28: Start ramp.
13h32: Stable beams #1522. 121b x 121b.
  Turnaround: 3h38.
  Luminosity: 2.8e25 cm-2 s-1.
  Length: 8h09.
21h41: Beams dumped on request.
  BPM calibration needed to correct temperature drift on the electronics in SR7.
  CV piquet has installed temperature monitoring at the crates concerned and will monitor the temperature over the weekend. At the moment the temperature is 22 degrees.
22h18: ALICE access required to fix trigger problem on half of their muon chambers.

## Slide 6: SR7 Temperature – BPM Calibration

## Slide 7: Improving the turn around in LHC
Two new sequences have been created:
PREPARE LHC FOR INJECTION (ALL BUT PCS)
INJECTION PROBE BEAM
To improve the turn around in LHC.
RAMP DOWN – PRECYCLE COMBO V01
PREPARE LHC FOR INJECTION (ALL BUT PCS)
INJECTION PROBE BEAM
1. RUN IN PARALLEL
2. RUN:
LHC equipment ready for injection in a bit less than 1 hour
Turn around of today’s morning shift with this new sequences and a smooth injection from injectors: 3.5 hours (new record)
Reyes Alemany

## Slide 8
Tested today for the first time. Once well tested it will be included in the LHC Nominal Sequence
Reyes Alemany

## Slide 9: Fill 1522
Emittances start injection:
B1-H: 2.5 B1-V: 2.3 B2-H: 2.6 B2-V: 3.2
Emittances end injection:
B1-H: 3.3 B1-V: 2.5 B2-H: 3.8 B2-V: 3.9
OK

## Slide 10: Transverse Damper: Well Damped
Wolfgang Hoefle checked.
Already maximum gain at injection.
Nothing to gain more…
However, during 450 GeV at injection (Friday morning): interesting perturbation on beam 2 vertical

## Slide 11: Damper Pickup B2
1000 turns
89 ms
The “hump”?

## Slide 12: Damper Pickup B1

## Slide 13: Fill 1522

## Slide 14: Lumi Spike During TCT Movement

## Slide 15: Fill 1522

## Slide 16: Status Ghost Bunches (JJ Gras)
Just before ramp: ~8% difference between DC and fast BCT on both beams.
Loss of real debunched beam during the start of the ramp.
Remaining difference close to 6.5% per beam.
Lost ~1.5% of debunched beam during the ramp: roughly the same amount than with the previous RF injection schema.

## Slide 17: Ghost Bunches

## Slide 18: Ghost Bunches Full Turn

## Slide 19: BSRT on Empty Slots

## Slide 20: Friday/Saturday 26/27.11.
22h18: ALICE access required to fix trigger problem on half of their muon chambers.
During Friday total: ~0.7 mb-1 delivered in stable beams.
00h10: Injection.
  Some time spent to sort out chromaticity.
03h00: Start ramp.
04h01: Stable beams #1523. 121b x 121b.
  Peak lumi: 2.8e25 - 3.2e25 cm-2 s-1
Still going…

## Slide 21: New Record Lumi
Un Grand Merci to the injectors.

## Slide 22: Peak Luminosity

## Slide 23: Integrated Lumi: > 5.3 mb-1

## Slide 24: Ahead
More stable beams… Well on track towards the week goal.
Next Tuesday: vdM scans.
Next week:
  Check 8 bunch injection
  Discuss a few MD-style studies (IR aperture, …)