## Slide 1: Saturday 25/11/10 & Night
12:24 Dump fill #1523 after more than 8 hours in physics
It takes some time to get back:
  Parallel sequences:
    Fewer clicks to turn around, always in the same order
    Ready for injection 50 minutes after dump
  14:20 During injection: TI8 magnet problem – EPC piquet
  Wait for ATLAS SOLENOID to ramp up – on slow ramp rate…
  Trip of power converter RCBCV7.L2B2. ‘Only’ a corrector, but needed….. (see later)
    Short access PM25, power converter rapidly changed
  20:20 Problem on the door of power converter in TI2 RQID_20700
    EPC piquet for TI2 ... unfortunately the CERN car that he has been issued with only summer tires on ....
21:30 Injecting for fill #1525
  Pauses during filling because of PS cavity trips
  23:56 Stable beams !
    This time it took 11h32 min to get back in physics again
7:50 Ion source problem – wait with refilling

## Slide 2: Fill #1523
Small emittances after filling at injection
  B1H/V: 3/2.5, B2H/V: 3.3/3.6
Good start lumi’s, although no record beam intensities
04:00 Stable Beams
12:20 Dump

## Slide 3: Power converter RCBCV7.L2B2
  Trip of power converter RCBCV7.L2B2. ‘Only’ a corrector, but needed…..this is close to the IP
  Jorg: There would be two 1 mm bumps after correction and one of these is at the Q5. With such bumps the correction may be difficult and also could have an influence on the crossing angle
  Decision to do the access and fix the problem rather than creating new ones
    EPC access is needed to fix it. Due to the snow the earliest that the piquet can get here is ~5:45, so the access starts at about 18:30
    MAD guardian got lost (in the snow) – another 30 min delay
    Power converter RPLB.UJ23.RCBCV7.L2B2 has been changed. Auxiliary power converter fault
Error not corrected out

## Slide 4: Midnight: Stable beams fill #1525

## Slide 5: Beam currents and lumi’s since Wednesday
Can spend your time analysing the lumi’s...

## Slide 6: (ALICE) Lumi vs. time
Saturday: Fill # 1523
Friday: Fill # 1522
Fill # 1523 / Fill # 1522
‘Elbow’
For both fills optimum time to keep it in would be about 5 hours, for 4 hours refill….
Keep it for 6 hours, for an 8 hours refill.....
We tend to keep it longer: you know what you have Confirmed by yesterday’s experience

## Slide 7: Total delivered lumi, this morning
Very close to the target for this week of 6 (µb)-1

## Slide 8: Plan
Get beam back again from Linac - refill
More physics 121 x 121
Next Week:
  Tuesday: Van der Meer Scans
  Injection tests with 8 bunches
  Discussing a few MD-style studies (IR aperture, …)