## Slide 1: Saturday 12 March
Morning: problem on RSD1.A12B2 – flow rate problem on the cooling water for the converter.
14:00: Loss map -500 Hz (positive energy offset) at 3.5 TeV unsqueezed.
  Very high loss on TCTV B2 in IR8.
21:00: Loss map end of squeeze H, V and +500 Hz (negative energy offset).
  Looking good.
23:30: Loss map end of squeeze -500 Hz (positive energy offset).
  Very high loss on TCTV B2 in IR8 - again.
  Dumped on unmaskable BLM Q7.L3.

## Slide 2: Positive dp/p, squeezed

## Slide 3: Night
00:00: Injectors
  Issues with SPS injection kicker – PFN1 to be replaced (1/2 day+) – trying to survive until Monday.
  PS POPS down…
02:00: SPS & PS back.
03:15: Asynch. dump test squeezed.
05:30: Ditto in collision.
  New settings OK.
  Realized that procedure (delay after RF off) tuned for nominal bunch in bucket 1. Statistics hopefully good enough from probe.
07:30: Next go. Issues in the squeeze with OFB switching off in H. some beam lost.
08:00: Loss map with positive dp offset in collision.
  Again TCTV in IR8 sticking out…

## Slide 4: Asynch dump squeezed - clean

## Slide 5: Asynch dump with colliding beams

## Slide 6: Summary of validations
Condition | Betatron H | Betatron V | Dp/p + | Dp/p - | Dump
Injection | X | X | X | X | X
Flat top | X | X | X | X | X
Squeezed | X | X | X | X | X
Collisions | X | X | X | X | X

## Slide 7: Saturday – Dump aperture
Aperture of dump line consistent with 2010 results.
Tested 14/15 kicker dump (using an orbit bump to simulate missing kicker).
  OK.

## Slide 8: Today
Decision for stable beams.
  Collimation and dump colleagues have to check all the data.
  Collimation OK – not worried about the TCTV in IR8.
Tentative planning:
  Test ramp to 1.38 TeV
  First fill with stable beams in the afternoon.
  Then a few fills until Monday PM to bridge the SPS MKP intervention – no beam from SPS ~10:00 to 14:00 on Mo.