## Slide 1: Weekend – brief resume
Lost ramp for physics around 2:30 Saturday
  Vacuum spike - R2.
Short fill overnight Friday to Saturday (1748) lost to trip of ROD.A12B1
Access for power converter repair
Saturday early afternoon: Stable beams (1749)
Lost to BLM communication problem ~16 hours later
Sunday morning: access for QPS controller reset, vacuum pump repair - inner triplet L5
Thanks to Mirko & Louis, Verena & Ron, Giula & GHH for holding it together over the weekend!

## Slide 2: Last night
Set-up for 768 bunches
  Lost first go at top of ramp with MKI UFO L2
  Into stable beams 19:00 Sunday
  20:30 lost to collimator position interlock on TCTs point 1 beam 1. SEE strongly suspected
  Communication lost on QPS controller for MB.A32L4 - access
Precycled and stayed forever at injection, first to verify the chroma (FIDEL corrections made it very stable) and afterwards for a PSB problem. Finally decided to fill despite the fact that the beam was not perfect as the piquet + the experts could not do better.

## Slide 3: Fill 1749 – overnight Saturday to Sunday
Peak luminosity | ~6.9 e32
Integrated luminosity | ~29.7 pb-1
Stable beams | 15 hours 53 minutes
Colliding bunches | 598
Average emittance from luminosity | ~2.5 micron

## Slide 5: UFO – L2

## Slide 6: “Not bad in the end”
Giulia Papotti

## Slide 7: Brief Summary week 17

## Slide 8: Delivered lumi over the last 7 days

## Slide 9: W17 physics fills – Monday to Thursday
FN | Stable beams | Peak [e32] | Int Lumi | EOF reason
1735 | 16h 34m | 4.85 | 20.2 | OP dump
1736 | 7h 4m | 4.27 | 5.9 | Slow loss in all of IR8, high vacuum spikes to 1E-6
1737 | 5h 7m | 4.71 | 7.5 | anticipating loss of cryo maintain.
1739 | 7h 44m | 5.2 | 12.1 | Loss of cryo in S78 (and later 81) due to fault on cooling of turbine.
1743 | 10h 2m | 7.05 | 20.6 | Beam Loss due to vacuum spike in IR8, triggering the BLM TCTVB.4R8 - 20 s RS

## Slide 10: W17 physics fills – Thursday to Monday
FN | Stable beams | Peak [e32] | Int Lumi | EOF reason
1744 | 43m | 6.11 | 1.5 | Fuse blew in the FE ctlxtim in a CCR rack,
1745 | 13h 22m | 7.19 | 26.0 | OP dump
1748 | 1h 49m | 7.21 | 4.3 | Octupole circuit ROD.A12B1 tripped due to fault in the auxiliary power supply.
1749 | 15h 53m | 7.29 | 29.7 | BLM comms.
1750/3 | 1h 29 | 8.37 | 4.2 | TCT position interlock
1755 | Still in | 8.84 |  | 

## Slide 11
losses on ramp

## Slide 12
bunch intensity distribution
bunch emittance
distribution after 6h run

## Slide 13: Timeouts
Energy extraction S34
Cryogenics
  Compressor stop – quick recovery
  Access for filter de-ice
  Turbine cooling fault
Atlas
Power glitch...ALICE both magnets, ATLAS both magnets and RF tripped. Lost 6 sectors and the undulator R4.
QPS controller resets…

## Slide 14: Issues
Dynamic b3 correction
Transverse CBI at 450 GeV
Energy extraction – S34
Vacuum R2 and R8
AGK
PM25 – sensitive - patrol lost*N
BPM front-end memory
  Flying blind in the ramp
Plenty of problems with communication/DIP servers: energy plots on page 1

## Slide 15: Dynamic b3 correction
Chromaticity swing at injection

## Slide 16: Chromaticity at 450 GeV
Marek Strzelczyk

## Slide 17: Thursday morning
Fill lost to slow beam loss on vacuum pressure bump R8

## Slide 18: Dumped on long running sum TCTVb.4R8
LHCb confirms that it was a real event, their BCM had a similar signature as the losses on the TCTVb.

## Slide 19: Vacuum layout R8 & R2
Interlock level increase to 2e-6 in all triplets Switched on the solenoids in point 2.
Giuseppe Bregliozzi Giulia Lanza

## Slide 20: AGK check
Following 72 bunches straight onto the TDI
Conclusion: AGK for B2 (which had the missing pre-pulse on 27/04/2011) seems to be fine and has a margin of 5 * 2.5 ns = 12.5 ns which should be sufficient for the system to be reliable. No changes relative to initial set-up on 11/03/2011.
Etienne Carlier, Jan Uythoven

## Slide 21: SEUs
QPS controllers – regular access
The collimator system for these two TCTs has rebooted by itself – strongly suspect SEE.
  See Roberto Losito

## Slide 22: Conclusions
Number of issues – SEEs being probably the one with the potential to hit availability…
on the back of excellent availability, great machine performance