## Slide 1: Monday 18.7.2011
1 fill with 1092 bunches (6 h stable beams)
3 fills with 1380 bunches (20 minutes in stable beams)

## Slide 2: Fill # 1955
9:49 Dump: RQTL7.L7B1 tripped fill #1955
  Integrated luminosity [pb-1]:
  Atlas: 18.8 CMS: 18.7 LHCb: 6.1
Remote reset of the QPS crate on RB.A81
  Unusually high temperature on collimator TCSG.D4L7.B1 (position “right up”) without beam: 55 deg  interlock masked

## Slide 3: Fill # 1955

## Slide 4: Fill # 1956
11:55 beam injected:
  Re-adjusting BPM phasing (E. Calvo)
  Tune, chromaticity
  MKI kicker length checked by M. Barnes
  Emittance(inj): ~ 2.5 μm rad bunch intensity: ~ 1.2E11
  Beam Intensity: 1.66E14
  Injection
    Beam 1 MSIB: 54% of BLM threshold
    Transfer line: BPM partly missing – partly high oscillations

## Slide 5: Fill # 1956
Waited 1 hour after injection for UFO’s to calm down
trip of RCD.A56B1 and RCO.A56B1 during the ramp, beam survived  reset and reloaded at flat top
Not obvious to find target luminosity Alice
15:40 DUMP: Cryo lost probably due to SEU on a thermometer at a current lead (beam2 IP5).

## Slide 6: Fill # 1956

## Slide 7: Fill # 1957
Injection:
  MKI vacuum B2: spike of 1.5E-8 bar
  Injection losses B1 up to 70% of BLM threshold (MSIB)
Wait ½ hour for UFO’s to calm down
  Emittance(inj): ~ 2.2 μm rad bunch intensity: ~ 1.3E11
  Beam Intensity: 1.77E14 Energy/Beam: 100 MJ
  35% of BLM threshold on TCTVB.4L2 83s integration time  consider adapting 83s thresholds

## Slide 8: Vacuum up to ~2E-7 mbar in IP3 and IP7

## Slide 9: Fill # 1957
BRAN Luminosity 1.4 – 1.5
But only for a couple of seconds

## Slide 10: Fill # 1957
DUMP: BLM voltage status interlock in IP7 caused by high losses when going in collision

## Slide 11: Fill # 1958
Wait ½ hour after injection for UFO’s to calm down
  Emittance(inj): ~ 2.0 μm rad bunch intensity: ~ 1.2E11
  Beam Intensity: 1.66E14
  mask the BLM HV status interlock in IP7 in the SIS for the first minutes of the collisions
    BLM_SR7_C_HV_STATUS would have given an interlock when adjusting LHCb luminosity
    Atlas and CMS adjustment before went without large losses
    Alice adjustment afterwards without big losses
    Alice optimized: factor 10 below target luminosity

## Slide 12: IP7: Vacuum spike and BLMs in warning when adjusting LHCb

## Slide 13: New record luminosity … but not for long
22:39
beam dump: cryo lost in sector 3-4

## Slide 14: PLAN
  Beam back: this afternoon
  Alice collision scheme?
  Luminosity production with 1380 bunches
  Adiabatically decrease emittance and increase bunch intensity
  BLMs:
    adapt 83s collimator thresholds
    SIS HV interlock?