## Slide 1: 1.8 K cycle and specificities
CC:
- 3D wheels
- Bearings (300K)
HX:
- Very Low Pressure
“Mixed” Compression P ratio ≈ 80
HX
Stainless Steel Plate
Axial-centrifugal
Impeller (3D)
Fixed-vane
diffuser
3-phase induction
Electrical motor
(rotational speed:
200 to 700 Hz)
Active
magnetic
bearings
300 K under
atmosphere
Cold under
vacuum
Inlet
Outlet
Pressure ratio
2 to 4
Spiral volute
Cold Compressor
200 to 800 Hz)

## Slide 2
125 g/s GHe from 15 mbar with 4 stages
Hydrodynamic cold compressors for 1.8 K ref.

## Slide 3: Cryo failure on Cold Compressor Unit
Cold Crompressor Unit:
  The CCU is composed of four compressors which by pumping on the helium bath allow to cool the magnets from ~ 4K down to 1.9K.
  The problem occurred on CC4
Several hypothesis:
  Single Event
  Driving Electronics
  Compressor
  …
Historic:
  13.08.2011 – 02:40am:
    Cryo is in Nominal conditions, Stable beam. The CC4 magnetic bearing controller has lost this feedback position value -> The PLC sees a difference between position – feedback -> send a stop order to CC4. During the stop the shaft’s magnetic center has moved.
CRG-OA
15.08.2011

## Slide 4: Cryo failure on Cold Compressor Unit
Historic (next):
  13.08.2011- morning:
    Access request needed, 3 tries to restart CC4, but each time it stops ~150Hz.
  13.08.2011- afternoon:
    Access request, recalibration of the magnetic center of the shaft.
    Restart around 5pm, CC4 at nominal speed during 7 hours.
  13.08.2011- 23:40:
    Same failure !!
  14.08.2011- 09am:
    Decision to change the electronics controlling the CC4 speed.
    Restart around 2pm, CC4 at nominal speed since then.
CRG-OA
15.08.2011

## Slide 5: Where do we stand ?
3.4K
3.6K

## Slide 6: Estimated Recovery time
Chart: Time [hrs]
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44
 | 2.3121 | 2.3033 | 2.2826 | 2.2499 | 2.2146 | 2.1807 | 2.1507 | 2.1225 | 2.0953 | 2.0702 | 2.039 | 2.0137 | 1.9876 | 1.9668 | 1.949 | 1.9323 | 1.9323 | 1.9212 | 1.9146 | 1.9138 | 1.9138 | 1.9113 | 1.9093 | 1.9098 | 1.9164
 | 3.8473 | 3.7824 | 3.7062 | 3.6292 | 3.54 | 3.4508 | 3.3602 | 3.2715 | 3.1849 | 3.0967 | 3.0151 | 2.9339 | 2.8569 | 2.7824 | 2.7107 | 2.6441 | 2.5825 | 2.5214 | 2.4614 | 2.4121 | 2.362 | 2.3238 | 2.2881 | 2.2583 | 2.2237 | 2.1863 | 2.1528 | 2.1224 | 2.0948 | 2.0661 | 2.0411 | 2.0237 | 2.0091 | 1.9836 | 1.9572 | 1.9312 | 1.9282 | 1.9196 | 1.9165 | 1.915 | 1.9263 | 1.9259 | 1.9244 | 1.9253 | 1.9284
 | 2.411 | 2.3803 | 2.3424 | 2.3041 | 2.267 | 2.2352 | 2.2046 | 2.1774 | 2.1513 | 2.1272 | 2.1055 | 2.0852 | 2.0659 | 2.0426 | 2.0235 | 2.0061 | 1.9859 | 1.9655 | 1.9488 | 1.9372 | 1.9256 | 1.9175 | 1.914 | 1.9145 | 1.9165 | 1.9201 | 1.9255
 | 2.6197 | 2.5774 | 2.54 | 2.495 | 2.4272 | 2.3627 | 2.3082 | 2.2627 | 2.2296 | 2.2002 | 2.1693 | 2.1381 | 2.1062 | 2.0732 | 2.0438 | 2.017 | 1.9928 | 1.9705 | 1.9502 | 1.9401 | 1.9407 | 1.9503 | 1.9594 | 1.963 | 1.9529 | 1.9499 | 1.9433 | 1.9373 | 1.9373 | 1.9388
Average | 3.8473 | 3.7824 | 3.7062 | 3.6292 | 3.54 | 3.4508 | 3.3602 | 3.2715 | 3.1849 | 3.0967 | 3.0151 | 2.9339 | 2.8569 | 2.7824 | 2.7107 | 2.6319 | 2.58 | 2.5307 | 2.4558 | 2.4065 | 2.3448 | 2.3098 | 2.2751 | 2.2433 | 2.2108 | 2.1784 | 2.1482 | 2.1196 | 2.0922 | 2.0663 | 2.0407 | 2.0182 | 1.9976 | 1.9767 | 1.958 | 1.9424 | 1.9399 | 1.9344 | 1.93 | 1.9248 | 1.926 | 1.9237 | 1.9219 | 1.9231 | 1.9273
~ 30 hours from now