## Slide 1: Fri – Sat - Sunday 30 Sept - 2nd October
Friday
  06:00 Operator dump fill #2171, integrated lumi 75 pb-1.
  90 m * optics
    Optics ok, collisions at all IPs, but no pots set-up or data taking
    Fill 1 lost due to problem with TCTs IP5 – access needed
    Fill 2 lost due to “hidden” inner limit on ALFA RP
    Fill 3 for optics measurement lost due trip RQTF.A45B2
    Fill 4 lost due to UPS down in UJ56 @ 03:05
Saturday
  Access
    IP2 and Alice: Her Excellency Pratibha Devisingh Patil
    Atlas UJ14 – ZDC, IP1 collimator resolver, CMS UL55
  15:00 Access required again for UPS in UJ56
  22:00 Stable beams #2177, Lumi 3.1e33 cm-2s-1
Sunday
  13:02 Operator dump fill #2177, integrated lumi 103/106/18.5 pb-1
  Access for QPS reset, cycle and take some time to optimise beams in injectors
  18:44 Stable beams fill #2178, peak lumi 3.2e33
    Alice instantaneous DIP lumi was off by a factor of ~100 (low), potentially dangerous
    OK again around midnight
    Still in

## Slide 2: Lumi over the week
Monday 00:00
Monday 08:00
3.5e33
Access QPS - Problem PS - Problem arming BIS - Coupling correction during squeeze -Electrical network reconfig, hits Atlas - Access Atlas - Beam dump self trigger, access
Problem Orbit Feedback - Abort Gap cleaning at 3.5 TeV postponed
UPS
90 m * - VIP

## Slide 3: Fill statistics
fill | Itot | n [rad] | L-peak | t-phys | L-int | dump
2156 | 1.83E+14 | 2.40E-06 | 3.00E+33 | 12:26 | 91.5 | QPS signal of IT.R1
2157 | 1.82E+14 | 2.25E-06 | 3.20E+33 | 1:48 | 18.7 | RF klystron vacuum
2158 | 1.79E+14 | 2.30E-06 | 3.00E+33 | 4:50 | 43.3 | PC triplet R2
2160 | 1.77E+14 | 2.30E-06 | 3.00E+33 | 1:56 | 18.9 | 4 circuits tripped in sector 56, likely SEU
2165 | 1.81E+14 | 2.20E-06 | 3.20E+33 | 5:50 | 52.5 | pc RCBCH6.R7B2
2168 | 1.81E+14 | 2.20E-06 | 3.20E+33 | 4:11 | 40.5 | UPS fault
2171 | 1.81E+14 | 2.25E-06 | 3.15E+33 | 10:04 | 75 | Operator dump*
2177 | 1.77E+14 | 2.15E-06 | 3.10E+33 | 15:00 | 105 | Operator dump
2178 | 1.82E+14 | 2.20E-06 | 3.20E+33 | 3:30 | 35 | 
 |  |  | Total | 56:05 | 480.4 | 
In one week 0.5 fb-1, while 1.5 days planned no physics
Previous operator dump 14 Sept.

## Slide 4: Emittances from lumi vs. Bunch current
M.Lamont

## Slide 5: 2011 so far
From CMS pages:
Atlas and CMS over 4.1 fb-1
LHCb @ 1 fb-1

## Slide 6: QPS on RQX.R1
Similar event as Sep 10th, where the QPS signal of Inner Triplet.R1 saturates and heaters were fired: SEU?
The only signal from QPS is on the RCBXH3.R1, where the U_res increases and saturates at 250 mV; there is no PM from the main circuit
Monday 26th September
10th September
One more QPS event afterwards, then a very good QPS week

## Slide 7: Vacuum over the week: “stable”
VGPB.123.4L2 (Alice), VGPB.183.1R5 (CMS)
1e-7
5e-7

## Slide 8: UPS problem Point 5 (UJ56)
Bras mutateur en défaut
Causes:
  l'IGBT (transistor de puissance) d'un bras mutateur a cassé. Une expertise plus profonde est en cours par APC/SCHNEIDER
Consequences:
  Arrêt LHC par PIC de EBS11/56.
Actions:
  Appel du piquet APC/SCHNEIDER intervention.
Diagnostique et dépannage: changement de 2 bras mutateurs, d'une carte alimentation et d'une carte mère
8 hours on Thursday
Same UPS bad contact early Saturday morning

## Slide 9: 90 m * optics
Filling scheme: 2 big, 13 small bunches

## Slide 10: Collisions found in all 4 IPs
Optimization of IR 1 and 5 after collisions were found
The BRANS in IP1 and 5 show nothing, but signals can be seen in IP 2 and 8

## Slide 11: Collimator in IP5: TCTH.4L5.B1 and TCTVA.4L5.B1
Found a short circuit somewhere on the 24V power supply used for switches and also other components
Problem came from the downstream anti-collision switches at collimator side (in the tunnel). There was a short circuit between one of the conductor and the ground of the connector
In the tunnel and finally we found that inside a 50 pins connector of the long cable, a small wire of copper was not correctly crimped and was slightly in contact with the metallic cover of the connector
This cable and his connectors have been installed during the cabling campaigns in 2006 and never touched since, so it's difficult to understand why the problem occurs only now...
Jerome Lendaro

## Slide 12: The small wire of copper...
Finally no pots aligned and no data taken with 90 m optics

## Slide 13: Abort gap
Fill yesterday

## Slide 14: Abort gap over the week
Always more population of B1 abort gap, later during fill
1e10

## Slide 15: Other things to note….(from Alick)
Again had to mask several stripline BPMs in YASP as they continued to give large position readings ( from 2 to 20mm), both with pilot and nominal bunches. As mentioned yesterday, this change has been present since Friday.
TI2 may benefit from a bit of re-steering next time around
  Generally injection OK, but transfer lines do need re-steering about every second fill
Injection Sunday afternoon:

## Slide 16: Present filln #2178
Reached 100/102/16.5 nb-1
Could be the third fill in a row to be dumped by operator

## Slide 17: Plan for week 40
Physics with some perturbations
  Abort gap cleaning at 3.5 TeV
  25 ns MD Thursday
  Large pile up MD, to be confirmed
This week’s coordinators: Barbara Holzer & Ralph Assmann