## Slide 1: Saturday 1st October
03:05 UPS trip at point 5:
  same UPS as Thursday – unit replaced
07:00 Visit
  Her Excellency Pratibha Devisingh Patil
Access
  UJ14 – ZDC, collimator resolver, UL55
Coming back problem various
  access biometry UJ14, PAD PM25
  patrol box YZBPC01=PM15
  QPS controller for the 4 circuits in XL5
15:00 Access required again for UPS in UJ56
  communication problem due to a bad contact in a relay

## Slide 2: Saturday afternoon
17:30 Pilots in
Some delay:
  SPS RF
  SPS BQM
  Transfer line steering while waiting for SPS
22:00 Stable beams #2177
  3.1e33 cm-2s-1
  1.77 e14
  1.28e11/bunch
  emittance from lumi 2.1 microns
  stables beams happily ongoing, and vacuum conditions well behaved.
  It seems that the strip-line BPMs are less well calibrated since a temperature correction was applied (on Friday), and this perhaps should be checked by BI

## Slide 3: 2177 bunch length
Markus Albert

## Slide 4: 2177 abort gap population

## Slide 5: Bunch currents

## Slide 6: Horizontal emittance

## Slide 7: Vertical emittance

## Slide 8: Luminosity lifetime #2105