## Slide 1: Tuesday morning
Trip of the four circuits seems to be due to a SEU.
  U-res of ROF.A56B1 is suddenly going to saturation and the circuit trips; the other circuits tripped by coupling.
08:05 lost S34 during “fix”
  access for QPS
Electrical network re-configuration
  Atlas cryogenics takes a hit
Ph.Baudringhien working on RF module M1B1

## Slide 2: Tuesday afternoon
Pre-cycle
Switch LHCb polarity
12:30 beam 2 in but problem with BIS beam 1
  Bruno Puccio: finally we could rearm the LBDS for B1, without a clear explanation. The BIS frequency was indeed well transmitted in simulation mode and we tried to rearm...
13:47
  ALICE dipole tripped: “apparently the EPC expert did some bad manipulation in connecting an oscilloscope.”
14:30 – 17:00 test ramp with pilots
  step through squeeze measuring and correcting coupling and chromaticity

## Slide 3: Tuesday evening
Access for Atlas during ramp-down
  Patrol lost – access finished 18:30
BPM crate power supply changed
  Problem unresolved 
21:00 machine full
  Had two shots at the beginning with high injection oscillations and then all below threshold. Average bunch intensity 1.34e+11. Vacuum not too bad.
21:30 lost in squeeze – LBDS self trigger
  Similar fault has occurred last Thursday and this morning
  Access required to change card

## Slide 4: Overnight Tuesday - Wednesday
01:30 Injecting
when filling for fill 2164, beams dumped by a trip of RCBXH3.L2:
  quench loop opened but no PM and communication witch crate was lost several minutes later. A power cycle was needed.
Refill. Injection OK, one latch on injection oscillation with 72 bunches, beam 1. The last but one injection of 144 bunches beam 1 was not seen by the IQC, neither by injection sequencer.

## Slide 5: Missed injection

## Slide 6: Overnight continued
RT orbit trims issue in ramp
2 dips in lifetime during the squeeze (40% of dump threshold).
  Orbit was not very well controlled in step from 1.5-> 1m (maybe due to the missing BPM crate)
Tune feedback did not switch off during the squeeze
  coupling correction looks to have helped

## Slide 7: Overnight continued
04:30 Stable beam #2165
  Initial luminosity 3.2e33
  1.3e11 per bunch
  Issues with Alice trigger/luminosity monitoring

## Slide 8: Tune fitting
Adjusted BBQ tune fitter settings to the equivalent of "MEDIAN FITTER 2" assuming a broader peak rather than applying the refined ''MEDIAN FITTER 1" that assumes narrow peaks.
the changes are visible but are fairly small and not impressive hoped...
Ralph Steinhagen

## Slide 9: RT orbit feedback induced tune shifts

## Slide 10: BPM crate - point 4
The power supply for BPM crate cfv-sx4-bpmb1rb was changed. It tripped however again shortly afterwards. Decided eventually to run without it. Will have to be fixed today.

## Slide 11: Today
Stable beams
Abort gap cleaning at 3.5 TeV – 6 hours