## Slide 1: Tuesday
Access….
  QPS intervention at 09:00 in point 8 (quench heater exchange)
  QPS installation oscillo for the ISRM measurement
  EPC intervention in point 4 (60 A module in S34)
  aperture Kicker intervention in point 4
  MKI AGK delay in point 8
  vacuum recabling in point 2
  vacuum : BPM cabling in point 8
  CNGS in point 8
  BI in UA43 for dev BBQ
  UX65 for RADMON installation
  UW25 : inspection from CV

## Slide 2: Frozen DFB in point 3
Insulation vacuum of DFBLC connection to the WRL was abnormally poor.
When the pump was restarted and the valve towards the insulation vacuum was opened, the pressure raised from 1e-8 to few e-5.
The ice was removed and the vacuum pumped back down to a good level.

## Slide 3: Tuesday-Wed
Morning: ISRM tests on RQ4.L8 and RQ6.R8
00:00 Precycle.
Injection a bit rocky – 50 ns quality not at its best (int. spread) – lot’s of injections blocked by SPS BQM.
  + steering of TI8.
Lifetime dip when bringing into collisions – 4 hours – and losses in IR7 to 67% of threshold (on B1 monitor from B2 losses).
04:20 Stable beams fill 2204, 3.3E33 cm-2s-1.

## Slide 4: Lifetime & losses

## Slide 5: Today
Stable beams.
ALICE reduced field test.
Abort gap at end of fill?