## Slide 1: Tuesday 7th August - morning
07:10 Reinjection after loss of fill 2920 to UFO near ALICE
  26 pb-1 in 1h16m; peak lumi 6.4e33 cm-2s-1
08:10 dump at 450 GeV when moving out injection protection at pt 8
  first to be a UFO. However, subsequent TDI position faults show that the loss was due to the TDI jaw not moving correctly, and one edge of the jaw going close to the beam. (Stefano)
Some delay to TDI – reset required
CHANGE OF PLAN – SWITCH OCTUPOLE POLARITY
  Simple flip at 450 GeV (6.5 A)
  417 A at flat-top & squeeze;
  down to 300 A in collision BP

## Slide 2: Step 1
Switch polarity at injection and inject full complement of 1374 bunches
  Octupoles on at ±6.5 A
  No signature selective blow-up seen
  Dampers reduced gain - ditto

## Slide 3: Step 2
14:00 Test ramp with pilot bunches
  Anticipatory Q’ trims performed (up to 12 units at 4 TeV)
  Thanks to Daniel and Themis – adjust of phase loop gain to avoid problem with RF modulation/low bunch intensity
  Reasonable Q’ measurement through ramp, squeeze and collide as a result.
  Chromaticity measurements fed-forward into settings, aiming for:
    +2 at 450 GeV
    Increasing to + 5 at end of ramp, through squeeze, and into collision
15:15 Beams dumped

## Slide 4: Chromaticity – beam 1 ramp

## Slide 5: Chromaticity – Vertical B1/B2 – flat top
Decay at 4 TeV

## Slide 6: Chromaticity – beam 1 – squeeze & adjust

## Slide 7: Step 3
Ramp with 12 nominal bunches – smooth
Beams dumped 18:10

## Slide 8: Step 4
Ramp, squeeze, collide, optimize with 480 bunches
  Sensible bunch intensities
  Ramp, squeeze, collide – no major issues
  Tune scan
  Stable beams for an hour
  Reduce octupoles in Adjust at end-of-fill

## Slide 9: Tune scan at start of collisions
Steps of 1e-3 both planes, both beams
Initial tune +3e-3 with respect to end squeeze (~nominal settings)
Given below – this tune increase in collision beam process removed
-1e-3
-1e-3
-1e-3
-1e-3
etc..

## Slide 10: Octupole reduction with 480b
Octupole current
Beam lifetime

## Slide 11: Octupole reduction – beam loss
3 non-colliding bunches go walkies at 23 A

## Slide 12: Step 5
Physics fill with 1374 bunches
  <Bunch intensity> ~1.47e11 at 450 GeV
Smooth ramp and squeeze
  Also enjoying effect of reduced emittances from injectors
Just after end of squeeze - strong vertical instability
  Clear visible on BBQ FFT at tune, beam 1 first
  Supressed by frantically increasing chromaticity
    Q’ trim H+2 V+6 B1/2

## Slide 13: Beam loss – end squeeze

## Slide 14: Beam loss – end squeeze

## Slide 15: Lifetimes through squeeze and adjust

## Slide 16: Beam sizes

## Slide 17: Tune – B1V

## Slide 18: Start of fill 2927

## Slide 19: Step 6
Increase octupoles to 475 A
  reverse polarity, from 417 A
Bump up vertical chromaticity in squeeze to around 7
Try again… today

## Slide 20: Misc
OFSU crashed 3 times during the shift
SPS intervention (EDF) Thursday 10:00 for 2-3 hours
TOTEM – third third of fill test incoming
Access list developing
  Markus Z. – point 4 – di/dt
  N. Magnin – LBDS
  RP – RAMSES reset
  Ralph S. – UA47 and tunnel