## Slide 1: Summary of week 33
Machine Coordinators: G. Arduini, E. B. Holzer
Many thanks to: Collective effects, Collimation and Injection and Injector teams Main aims: ALICE polarity switch and luminosity production

## Slide 2: Week 33
ALICE polarity
7x1033 cm-2s-1
LATLAS LCMS IB2 IB1

## Slide 3: Last 24 hours
5:14 OP dump. End of fill #2984 223 pb-1 in 19 h
8:30 Injecting physics beam fill #2985 (delayed by MKI2 temperature interlock)
9:15 beams dumped during ramp by trip of LHCb dipole
11:00 Intervention on LHCb dipole power converter completed Filling #2986 delayed by RF problem in the SPS
Dump during injection due to BLM in point 2 close to inection kicker (UFO?) after injection
12:00 Filling #2987
13:23 STABLE BEAMS #2987. Initial luminosities ~7.1x1033 cm-2s-1
13:59 RF Module M2B2 tripped (main coupler vacuum). Beam dump. ~14 pb-1 in 0.6 h.

## Slide 4: Last 24 hours
After that all afternoon/night with problems one after the other:
  Trip of Arc 45 (RQ7.R4 HTS interlock)
  RF problem in the PS (20 MHz) - twice
  Cryo PLC replacement in P18 (PLC)  no injection/ramp on request of cryo operator
  PS Main Power Supply (POPS)

## Slide 5: Main faults
Date | Duration [h] | Description
Mon 13/8 | 7 | PSB, QPS controller reset (main circuits in sector 45) RF cavity in the PS, ALICE solenoid power converter polarity switch
Tue 14/8 | 2.5 | Undulator trip and ML4 cryo lost, PS (POPS)
Thu 16/8 | 5 | ROF.A81.B2 replacement, QPS reset (RB.A12.C21.R1B) requiring access
Fri 17/8 | 3.5 | PS access (RF 40 MHz), CMS
Sat 18/08 | 0.5 | MKI2 temperature
Sun 19/08 | 14.5 | MKI2 temperature, LHCb dipole power converter (spurious temp. interlock), SPS RF, RF Module M2B2 trip (main coupler vacuum), Trip of RQ7.R4 (QPS trigger – HTS), PS RF (20 MHz) Cryo P18 (PLC), POPS
Mon 20/8 | 8 | PS RF (20 MHz), POPS

## Slide 6: Main faults by system
System | Time [h] | Comments
Injectors | 20.5 | PSB, PS (POPS, RF), SPS (RF)
PC | 7.5 | ROF.A81, ALICE solenoid, LHCb dipole
QPS | 6 | QPS controller resets + HTS on RQ7.R4
Kickers | 2.5 | MKI2 temperature
RF | 2 | M2B2 module (power coupler vacuum)
Cryo | 2 | P18 PLC
Experiments | 0.5 | CMS
Total | 41 (24%) | 

## Slide 7: Fills from 13/08 – 08:00
Fill | Nb | Duration [h] | Lint [pb-1] | Dump reason
2957 | 1374 | 1.8 (9.8) | ~20 (152.1) | TCT IP1, loss of b* information
2974 | 78 | 0.8 | 0.9 | OP dump
2975 | 474 | 0.5 | 3.9 | RQTL9.R7B1 QPS (SEU?)
2976 | 1374 | 11.3 | 148.4 | OP dump
2977 | 1374 | 0.01 | 0.1 | Trip of ROF.A81.B2 PC
2978 | 1374 | 1.3 | 27.4 | Vacuum interlock P7 (pressure spike)
2980 | 1374 | 2.8 | 54.9 | MKB ionic pump trip. LBDS trigger.
2981 | 1374 | 1.0 | 22.7 | QPS trigger on RQT12.R1B2
2983 | 1374 | 15.9 | 194.2 | OP dump
2984 | 1374 | 19.2 | 222.9 | OP dump
2987 | 1374 | 0.6 | 14.3 | RF module M2B2 trip
Total |  | 55.2 | 709.6 | 
STABLE BEAMS 55.2 h (33 %)

## Slide 8: Lost fills before stable beams (>450 GeV)
Event Timestamp | Phase | Beam Energy [TeV] | Fill Number | Comment
14-Aug-12 03.21.08 | ADJUST | 4 | 2959 | Enf of fill after setting up collimators
14-Aug-12 07.02.17 | SQUEEZE | 4 | 2960 | Loss map
14-Aug-12 22.05.10 | ADJUST | 4 | 2965 | Loss map
15-Aug-12 12.44.31 | ADJUST | 4 | 2966 | Loss map
15-Aug-12 02.59.43 | ADJUST | 4 | 2967 | Loss map
16-Aug-12 20.24.38 | RAMP | 1 | 2979 | UFO at TDCQ
17-Aug-12 09.52.20 | RAMP | 1.5 | 2982 | SIS (RB energy tracking)
19-Aug-12 09.15.42 | RAMP | 1.5 | 2985 | LHCb dipole power converter
No fill lost due to instabilities
c/o Post-Mortem DB

## Slide 9: Performance
~11.5 fb-1
~1.15 fb-1

## Slide 10: Performance
Chart: DATE
1.6x1011 p/b @inj

## Slide 11: Performance
7.4x1033 cm-2s-1 in ATLAS
2.2-2.3 mm

## Slide 12: Performance

## Slide 13: ALICE polarity switch + X-ing angle increase
Monday
  Orbit measurement and correction with opposite polarity
  Collimator alignment (TCTs pt. 2): up to the end of the squeeze
  Loss maps up to the end of the squeeze
Tuesday
  Injection and injection protection setting-up (point 2)
  Feed-forward of orbit corrections in ramp/squeeze (1st iteration)
  Collimator alignment (TCTs pt. 2): up to the end of the squeeze
  Loss maps in collision (including roman pots)
Wednesday
  Angular alignment verification TDI in point 8 following issues observed in week 32
  Feed-forward of orbit corrections in ramp/squeeze (2nd iteration)
Intensity ramp up: 78/480/1374 bunches

## Slide 14: Collimator set-up
 | Injection, inj prot. IN | Injection, inj prot. OUT | Flat-top | Squeezed, separated | Collision, RP in physics settings
Betatronic-H | Done | Done | Done | Done | Done
Betatronic-V | Done | Done | Done | Done | Done
Neg. off-mom | +1000 Hz | +1000 Hz | -- | -- | +500 Hz
Pos. off-mom | -1000 Hz | -1000 Hz | -- | -500 Hz | -500 Hz
Asynch dump | Done | -- | -- | -- | Done
Alignment
Loss Maps- all done. OK by Collimation team
Alignment | Injection | Flat-top | Squeezed, separated | Collision
IP2 TCTVs + TCTHs | done | done | done | done
Collimation team

## Slide 15: TDI deformation
Tuesday 8/8 dumped on beam losses on the TDI Pt8 when moved to parking and probably one side got stuck. After 1 hour with high intensity beams at injection: a large vacuum rise and probably significant heating.
Suspected deformation of the structure, seen as ‘drifts’ on the LVDT readings, much stronger than normal
Not clear at that point which part of the system (jaw or mechanism outside) is deformed
M. Di Castro, R. Losito, A. Masi, J. Uythoven

## Slide 16: TDI8 alignment check
Angular alignment:
  No change as compared to last measurement's changes by 10 mrad for the lower jaw
  we keep the same positions and angles as before
Retraction measurement:
  Lower TDI.P8 jaw at 6.8 (6.6 previous) s exactly at nominal setting, OK Upper jaw at 6.4 (6.4) s, closer to the beam and therefore OK
No evident damage
C. Bracco, W. Bartmann

## Slide 17: Emittance at injection
Emittances in the LHC larger than last Sunday for similar intensity. PS sees fluctuations since the week-end.
R. Steerenberg

## Slide 18: Emittance at injection
Further deterioration during Thursday
Some improvement after SPS inj. Kicker timing adjustment
B2V Fill 2978
E. Bravin
B2V Fill 2977
B2V Fill 2976

## Slide 19: Emittance at injection
Striking improvement on Thu night:
  Average emittance out of the PS of 1.1 mm and an intensity per bunch of 1.7x1011 p/b. Mainly due to working point optimization at low energy.
  SPS has confirmed the emittance reduction with emittances of 1.5 um
  Since then emittances at injection in the LHC in the range of 1.6-1.8 um
R. Steerenberg

## Slide 20: Instabilities
2980 - Q’H/V=11 – GainTFB=0.01
2983 - Q’H/V=11 – GainTFB=0.02
BBQ-B1H BBQ-B2H
BBQ-B1V BBQ-B2V

## Slide 21: Instabilities
2984 - Q’H/V=13 – GainTFB=0.04
2987 - Q’H=13 Q’V=15 – GainTFB=0.04
BBQ-B1H BBQ-B2H
BBQ-B1V BBQ-B2V

## Slide 22: Instabilities
IP8-V-SEP
Oct+Chrom
IP1-H-SEP
BBQ-B1V
IP8-V-XING
IP8-H-XING
BCT-B1

## Slide 23: Collision
Vertical blow-up of the tails of 36 bunch trains mostly on B1
Losses on the few percent level

## Slide 24: Settings
Present settings during squeeze and collision:
  Q’H=13 (ramping down to 11 during collision process), Q’V=15 (for next fill)
  Octupoles at 510 A during squeeze and ramped down to 394 A during collision process
  Transverse damper at maximum normalized gain (0.04  50 turns damping time for the low frequency coupled bunch modes)

## Slide 25: Kicker temperature
Data from kicker soft-start analyzed.
Slight increase in the interlock levels applied (particularly for magnet B – 2 deg.)
Magnet C: indications that we could be close to the Curie temperature, more data needed.
B. Goddard, V. Gomes Namora

## Slide 26: New Online Footprint Viewer
X. Buffat
Injection
Flat top
Collision

## Slide 27: Summary
Achieved new record luminosities >7x1033 cm-2s-1 with:
  High bunch intensity (~1.6x1011 p/bunch at injection)
  Small emittance from the injectors
No fill lost due to instability but still instabilities observed leading to blow-up of some bunches
All countermeasures for instabilities identified so far (octupoles, transverse damper, chromaticity) at or close to their maximum
Good production in spite of the setting-up time dedicated to the ALICE polarity change and yesterday….