## Slide 1: MD#4 Progress
MD Coordinators:
Giulia Papotti, Frank Zimmermann
Machine Coordinators:
Gianluigi Arduini, Eva Barbara Holzer
29 November 2012

## Slide 2: MD#4 News & Plan Mon – Tue (26. – 27.11.)
Day | Time | v | MP class | MP Comments
Mon | 06:00 | Ramp down if needed |  | 
 | 08:00 | 450 GeV: IR8 aperture | A | 450 GeV Pilote bunches(1e10p/bunch) to measure aperture.
 | 10:00 | 450 GeV: Beam instrumentation | B | BSRT vs WS, Schottky, WS PM saturation (partially done in MD3): 450 GeV B1: Pilot + 12b >=1.1e11p/bunch B2: Pilot + 50ns trains from 6 to 72 bunches Bumps at 450GeV and 4TeV Blow up with ADT 2) BGI, Gates BBQ, BSRT temperatures: 450GeV 50ns trains with minimum 600 bunches Bumps in B2 +- 3mm Blow up with ADT Gating with ADT off on some bunches 3) BPMs: Done in MD3 4) Matching: 450GeV Probe from 1 to 5e10p Inj, circulate (~100 turns) and dump (More details see slides )
 | 16:00 | 450 GeV 4 TeV: p-Pb test | C | From MD2 preparation: 450GeV and 4TeV Bunches of ~1.5e10p/bunch and >5e7Pb/bunch B2: few proton bunches and few Pb bunches B1: > 300 bunches with 10% ~1.5e10p/bunch, later with higher intensities. Test RF re-phasing procedure. Squeeze sequence and collisions. (More details see slides)
cancelled (QPS access S6-7 RQF/RQD,
MKI2 fault in softstart, dump line vacuum);
to be rescheduled as Operational Dev.
BPM studies and beam excitation, …
24 p batches from the SPS posed problems

## Slide 3: MD#4 New & Plan Mon – Tue (26. – 27.11.)
Day | Time | v | MP class | MP Comments
Tue | 00:00 | Ramp down |  | 
 | 02:00 | 450 GeV 4 TeV: MQY transfer function | A | 4 TeV. Pilote bunches (1-3e10p/bunch). Standard optics measurements with different MQY transfer funtions.
 | 06:00 | Ramp down |  | 
 | 08:00 | 450 GeV: RF study (longit. stability for batch or RF voltage modulation) | B | 450GeV A few nominal batches of 144b. RF Voltage modulation: fill half of the ring, to test the corrected algorithm of voltage set point adjustment Longitudinal stability: Full ring with max. bunch intensity. Excite a single mode in the beam with decreasing gain in the feedback loop. (More details see slides)
 | 16:00 | 450 GeV: beam-beam (noise or impedance) | C | 450 GeV In total 9 bunches per beam with different intensities (from 1e11 to 2e11), zero crossing angle in IP1, IP2 and IP5. Nominal crossing angle in IP8. Collision tune, Damper (ADT) off Introduce increasing noise with ADT Increase ADT gain in steps Scan separation in IP1 and 5 with 4 bunches (from 1e11 to 2e11) with damper of. (More details see slides)
 | 22:00 | 450 GeV 4 TeV: Collimation impedance & follow up from last MD | B | 4 TeV ~3b (1.3e11p/bunch) below SBF Alignment of collimators Impedance studies with tight collimator settings and moving IR7 collimators back and forth. (More details see slides)
successful!
successful
successful
successful

## Slide 4: MD#4 Plan Wed – Thu (28.-29.11.)
Day | Time | MD | MP class | MP Comments
Wed | 04:00 | Ramp down |  | 
 | 06:00 | 450 GeV 4 TeV: two –beam impedance | C | 4TeV, squeeze to beta*=1.5m 150 bunches per beam (nominal filling scheme) Move beam 2 clockwise Reduce octupole currents in 5 different configurations (0 turn, ¼ turn, ½ turn, ¾ turn and 1 turn cogging) (More details see slides)
 | 14:00 | Ramp down |  | 
 | 16:00 | 450 GeV: transverse impedance localization at injection | C | 450GeV 8bunches with different intensities, equally spaced (5e9 … 1e10 … 5e10 … 1e11 … 1.5e11 … 2.2e11) Create kick with AC dipole or kicker Tune shift 2.1e-3 Move TDI Parallel measurement with ADT? (More detials see slides)
 | 18:00 | 450 GeV: TCDI automatic setup | A | 450 GeV Pilot bunches (1e10p/bunch)
 | 22:00 | 450 GeV 4 TeV: bunch flattening with RF phase modulation | B | 450 GeV and 4TeV Nominal LHC beam, i.e. 1374b per beam Add flattening signal (sine-wave close to the synchrotron frequ.) The MD will have ramp and all steps before physics. Measure effects of heating and transv. Instabilities.
Thu | 02:00 | Ramp down |  | 
 | 04:00 | End of MD#4 |  | 
successfully executed -
→new questions & theories
successful
successful
successful

## Slide 5
78 nominal bunches (6+2*32), 1.5 E11, 1.5 micron emittance
nominal squeeze down to 0.6 m
RF cogging of beam2 at -12 Hz (10E-4 in dp), inducing clockwise rotation of beam2 (beam1 fixed).
4 cogging configurations: 0 turn (overlap in IR1 and IR5), 1/4 turn (IR2 only), 1/2 turn (no overlapp), 3/4 turn (IR8 only), 1 turn (back to 0 turn)
in each cogging configuration, MO scan was performed, some with tune split: always moving the most stable beam down along the diagonal
Two-beam impedance MD - conditions
P. Baudrenghien, S. Fartoukh, E. Metral, A. Burov
Result 1: cogging worked nicely, even in presence of moving LR encounters at full intensity (1.5 E11) & 9 sigma normalised crossing angle in IR1 & IR5

## Slide 6
cogging (turns) | common IR | int. (av. b1/b2) [1e13] | MO thr. [A] | gain from tune split
0 | 1 & 5 | 1.15 | 400 | -100 A (B1: -0.005,-0.005)
¼ | 2 | 1.05 | 200 | small effect
½ | none | 1.00 | 150 | - (not tried)
¾ | 8 | 0.95 | 100 | 
1 | 1 & 5 | 0.95 | always stable (scanned 520 to -520 A; also changed Q’ by +10 ) | 
1+1/2 | none | 0.85 | still rock stable | 
MD ruled out scenarios were stability would be explained by negative Q’ or by LR tune spread
main "belief”: Landau damping can only come from longitudinal plane (strictly no LR tune spread in the last configuration certainly transverse + longitudinal blown up)
Two-beam impedance MD – 2nd result
P. Baudrenghien, S. Fartoukh, E. Metral, A. Burov

## Slide 7
line 2*Qy (actually 1-2*Qy) systematically observed in the presence of instabilities regardless of the cogging configuration, i.e. with *and* w/o LR beam-beam
possible explanation (to be confirmed off-line): this line reflects beam response to machine nonlinearities, further amplified by tune proximity to 3rd order resonance after the first step of the squeeze (so coupled to Qx and actually found to be moving when trimming Qx), but also and mainly beyond the ADT tune window:.. so coherent mode (m=0) possibly undamped at this frequency ?? in general: Two-Beam-impedance effect seems to be excluded. In the presence of LR beam-beam the situation seems to get worst. There is a source of Landau damping which is strongly suspected in the longitudinal plane. Machine (and LR) nonlinearities certainly add frequencies to the beam spectrum (m*Q1+n*Q2); “for some of us, the behaviour of the ADT is not clear under these conditions”
Two-beam impedance MD – more results

## Slide 8
Two-beam impedance MD – illustrations
instability signals during the MD
B2H
B1V

## Slide 9
Two-beam impedance MD – illustrations
B1 emittances after 1-turn cogging (~11:16);
blown up everywhere, especially in the tails

## Slide 10
Two-beam impedance MD – illustrations
1-2Qx

## Slide 11
Impedance MD – Transverse Localization
AC dipole kicks on high intensity bunches
ADT & octupoles off, increase Q’ for better beam stability
measurements with TDI close to the beam & TDI at 30 or 31 mm, mostly on beam 1 due to fault on LBDS2
phase beating with intensity

## Slide 12
Injection MD – TCDI Automatic Setup
Inj & dump for TCDI setup software (setup beam flag limit raised to 6e10p)
pilot ; checked steering ; opened TCDI thresholds
3 scans with two different collimators in TI8
TCDI stayed once armed after the scan (not for the next scans)
correct detection when beam is not extracted (collimator not moved)
improvements: normalization to intensity ; zoom-in window ; automatic entry in logbook
manual checks of automatic analysis results (1st scan only movement)
  2nd scan: +/- 2 sigma scan window too small for good fit
  3rd scan: automatic centre: -0.242 sig, manual centre: -0.236 sig
not checked: automatic trim-in of new centres
The application works
correctly and can be used
for the next setup!
C. Bracco et al.

## Slide 13
Injection MD – injection matching monitor
timing correct ; Al screen well centered
intensity was too low for OTR measurements (limited time prevented scraping high intensity bunch in the SPS down to below the limit of 6e10)
C. Bracco,
F. Roncarolo,
et al

## Slide 14
Test of phase modulation with individual bunches of different intensity at 450 GeV: difference in incoherent synchrotron frequency between low and high intensity bunches around 1 Hz. Effect of flattening observed through bunch phases and profiles.
Successful test with nominal beam in both rings on flat bottom,
effect observed on beam spectrum and profiles before and after application of phase modulation. Beneficial effect on ALFA heating also visible.
Test of RF voltage reduction from 10 MV to 6 MV on flat top, no losses, but some transverse (B1V) activity could still be observed at end of squeeze; detailed analysis required for comparison w higher voltage case.
Test of phase modulation with 10 MV in squeeze. When applied to B2 at revolution harmonics with phase loop on → bunch length variation around the ring was produced. Flattening of B1 was done with phase loop off and smaller amplitude. Heating in ALFA was significantly reduced for both beams. To be analysed for other equipment. At the end average BQM bunch length was 1.6 ns. During phase modulation of one beam, excitation could be seen on the other beam in the transverse (V) plane.
Finally beam was dumped due to slow losses in Point 5
RF MD – bunch flattening w RF phase modulation

## Slide 15
RF MD – bunch flattening w RF phase modulation
amplitude of phase oscillations
spectrum before
modulation
spectrum after
modulation
J. Esteban, T. Mastoridis
E. Shaposhnikova,
B. Salvant, et al

## Slide 16
RF MD – bunch flattening w RF phase modulation
modulation in bunch length along all bunches of B2, following the RF modulation applied.
J. Esteban, T. Mastoridis
E. Shaposhnikova,
B. Salvant, et al

## Slide 17
beam spectra: clear effect of RF modulation
Roman Pot: temperature decreases after flattening bunches MD → very sensitive
TDI: no change noticeable
vacuum: VGI.210.5R6 quite high, tbc with vacuum experts
BSRT: changes of T slope also indicate beneficial effect of flattening bunches
MKI magnets: steady increase, difficult to see changes. MKI tube temperatures: steady increase. change of slope observed on MKI8C tube up temperature
TCTVB.4L8 and TCTVB.4R8: temperature probes show clear correlation with bunch length.
TCP.B6L7: no clear impact observed
beam screens or Q6R5: Nothing special observed (except for usual noise between 3am and 4am), according to TE/CRG operator, to be confirmed offline
RF MD – effects of bunch flattening

## Slide 18
RF MD – effect of bunch flattening on BSRT

## Slide 19
RF MD – effect of bunch flattening on ALFA RP
long
long
short
short
Sune Jakobsen

## Slide 20
RF MD – spectrum evolution during the MD