## Slide 1: Saturday 12th January
01:00 - 05:00 squeeze in steps down to 80cm
05:42 Dump beam at 4 TeV, end of beta beat measurements over squeeze
06:48 Start TDI alignment following intervention on TDI during TS
13:30 TDI alignment finished successfully
13:30 Start of BPMS interlock check after installation of new attenuators during TS
16:30 Interlock checks finished successfully
16:30 Check of BPMS intensity limit with a single bunch: 1.5e9
17:30 Start check of BPMS with bunch trains at injection
19:15 Mains ‘perturbation’, cryogenics lost… and a lot more
22:03 Confirmation that an electrical rack has caught fire in RE88.
00:20 Cryo conditions
01:30 UPS repair ongoing

## Slide 2: TDI alignment Chiara & Wolfgang
Part of the mechanics of the left(upper) jaw of TDIs in IP2 and IP8 were replaced during Xmas stop and LVDTs re-calibrated
  References no more valid and new setup needed.
Procedure
  Defined orbit with indiv
  Checked alignment with pilot (all 4 jaws checked)
  Defined new settings plus position and energy interlocks:
Results
  TDI.IP2: Left (=upper) jaw: -3.03 mm & 0 urad Right (=lower) jaw: -4.39 mm & -840 urad
  TDI.IP8: Left jaw: 3.19 mm & -157 urad Right jaw: 1.59 mm & -175 urad
Checked retraction with respect to TCP (X-measurement):
  TDI.IP2 both jaws at 6.4 sigma (nominal 6.8 sigma)
  TDI.IP8 both jaws at 6.9 sigma (nominal 6.8 sigma)

## Slide 3: BPMS checks Eva
BPMSs interlock the beam position +/- 3 mm relative to reference to be sure that the beam passes through the beam dump channel.
Filters changed during TS so cross-over between high and low sensitivity mode is not at 2e10 p+, which is where we expect to be working for the coming pPb run.
Interlocking was checked
  All channels interlock correctly, with an error of up to 0.5 mm
  This error was smaller in the past, 0.1 mm, but is still acceptable
Checked with single bunch minimum intensity
  At 1.45e9 interlock channels triggered
Plan was to check multiple bunches of 1 – 2 e10 p+
  Difficult: injection oscillations but no IQC data. Injected beam lost after few turns. ADT still adjusted for high intensity bunches….
  Did not get very far on this as ->

## Slide 4: 19:15 Mains perturbation
Explosion of a circuit breaker on the stable filter in BE9
  This effects mainly the SPS. Repair most likely on Monday. Have to see if SPS can deliver some beam without this filter
Main damage on the LHC side is a UPS in point 8 and point 7
  Fixable, but also needs external company
  Repairs ongoing at this moment
Trips
  ‘All’ circuits lost including Experimental Magnets
  Cryogenics OK lost – but compressors stayed on
  RF lost
  QPS in fault
  Injection and beam dump kickers in fault
  ...

## Slide 5: Outstanding
Problems to be fixed
  LHC: UPS interventions ongoing UJ76 and RE88. To be finished early evening. Then pre-cycle and sanity check.
  LHC: BLM CPU problem point 2 – intervention this morning
  LHC: TDIs stuck – to be investigated
  SPS: ‘Stable Filter’ not operational till Monday.
  SPS: Beam dump errors on energy tracking
  SPS: For the moment no protons from the SPS
Ramp up experimental magnets
  ATLAS in the evening
If beam back, start with optics corrections through the squeeze.
Access requests (could be done this morning)
  Ralph Steinhagen to change BBQ sensitivity