## Slide 1: 01/04/2010

## Slide 2: 01/04/2010
Start of the studies delayed due to trip of RQD.A12 at 08:43 at the end of pre-cycling  nQPS triggered but no signal observed above threshold.
Injection started at ~12:00 for RF capture optimization. Due to the low longitudinal emittance delivered by the SPS the capture voltage could be decreased from 8 to 5 MV at injection
Trim to new values implemented in the sequencer

## Slide 3: 01/04/2010
Preliminary tests of the chromaticity measurement by RF frequency modulation

## Slide 4: 01/04/2010
Smooth ramp in preparation of squeeze test
15:00 Beam lost at flat-top due to bad manipulation with the sequencer
Finally ready to start the squeeze at 18:30
No losses during the squeeze (except to over enthusiastic use of AC dipole)

## Slide 5: 01/04/2010
b* = 9 m
Tune and chromaticity OK

## Slide 6: 01/04/2010
b* = 9 m
Beta beating measurement
Beam 2
Beam 1 (lost 80 % of the beam during AC dipole excitation)

## Slide 7: 01/04/2010
b* = 7 m
Tune and chromaticity OK

## Slide 8: 01/04/2010
b* = 7 m
Beam 2

## Slide 9: 01/04/2010
b* = 5 m - Tune and chromaticity OK. Coupling increases to ~0.01

## Slide 10: 01/04/2010
b* = 5 m
Beam 2

## Slide 11: 01/04/2010
Coupling Beam 2
b*=9 m b*=5 m

## Slide 12: 01/04/2010
Important loss during the ramp  beam unstable. Likely chromaticity too low

## Slide 13: 01/04/2010
Today:
  05:00 Ramp (without feedback) - OK
  06:37 – lost cryo (oil pump?) – beams dumped
  access in PZ45 for CRYO intervention
  around 14:00 – recover from cryo
  09:00 Tune feedback / chromaticity measurement during the ramp
  14:00 Non linear chromaticity measurement and off-momentum beta beating
  17:00-18:00 LHCb polarity change
  Prepare fill for the night

## Slide 14: 01/04/2010
Saturday to Monday:
  2 fills/day with an end of fill or beginning of fill study (2-3 hours)
Beginning/End of fill study list in work
  Working point in collision
  Machine protection tests
  Non-linear chromaticity measurement at flat-top
  b3 correction checks