## Slide 1: Weekend Summary
Main tasks - goals:
  Finish LBDS measurements at 450 GeV:
    Beam dump with transverse and energy offsets.
    Simulation of asynchronous beam dump.
  Adjustment of TOTEM Roman Pots at 450 GeV.
  Optimization of longitudinal blow-up procedure.
  Fills for Physics.

## Slide 2: Week 25
Week 24 | 
Mon 21/6 | LBDS setup and validation at 450 GeV
Tue 22/6 | LBDS and collimation validation continued Cryo problem in Pt4
Wed 23/6 | Access for RB78 and BIC/RF IR4. Cryo recovery (Pt4 and Pt2) Technical stop in the SPS; RF problems in injector complex
Thu 24/6 | Feedback studies (Q, Q’ and Orbit); Damper tests Ramp test and asynch beam dump validation
Fri 25/6 | Finishing up LBDS validation TOTEM setup at 450 GeV Transverse damper setting-up for operation with >1 bunch
Sat 26/6 | Test ramp with new sequence for squeeze and collapsing of separator bumps. Fill for Physics with 'Stable Beam' conditions  L = 5 1029 cm-2 sec-1
Sun 27/6 | End of fill studies on Q’; Octupole settings and beam size measurement Loss of cryo in Sector 34  no beam for rest of the day

## Slide 3: Saturday 26.6
Summary of Saturday’s Physics fill’:
  Emittances of beams at end of ramp:
    Beam1: horizontal 5.0 mm; vertical 7.6 mm
    Beam2: horizontal 6.0 mm; vertical 5.9 mm
  Peak luminosity above 5 1029 cm-2 sec-1!
  But luminosity in ALICE ca. factor 2 smaller than in other experiments!
  Nb = 0.9 1011 ppb
  Measured b* values:
  IP1 (ATLAS) horizontal: 3.27m - 3.52m vertical: 3.82m - 3.76m
  IP2 (ALICE) horizontal: 3.45m - 3.34m vertical: 2.65m - 4.23m
  IP5 (CMS) horizontal: 3.70m - 3.69m vertical: 3.45m - 3.93m
  IP8 (LHCb) horizontal: 3.42m - 3.64m vertical: 3.89m - 3.07m
   2.4 1029 cm-2 sec-1!!!

## Slide 4: Sunday 27.6
Morning: End of Fill measurements for last physics fill:
  Re measure Q’ (still looking for explanation of intensity drop during last fill):
    Beam2: Qx’ = +4.4; Qy’ = +4.2
  Re-measuring transverse emittances:
    end of squeeze:
    Beam1: horizontal 5.0 mm; vertical 7.6 mm
    Beam2: horizontal 6.0 mm; vertical 5.9 mm
    end of run:
    Beam1: horizontal 5.6 mm; vertical 10.4 mm
  Beam2: horizontal 10.6 mm; vertical 13.4 mm
  Reducing Octupole strength (100A  40A).
    No change in tune spectrum
    But some losses in IR7

## Slide 5: Sunday 27.6
Losses in IR7 during change of Octupole settings:

## Slide 6: Sunday 27.6
Morning: End of Fill measurements for last physics fill:
  Transverse offset scans at ALICE:
    Horizontal scan with both beams at 1 s  Optimization for Horizontal rate is ok.
    Vertical scan with both beams at 1 s  Optimization for Vertical rate is ok.
    11:50: setting up for reducing the instantaneous luminosity by a factor of 30 for ALICE by opening the Horizontal separation.
    12:10: Both beams dumped via SMP interlock in the SIS which was generated when the SMP detected an energy mis-match from the BLMs. The reason for the mismatch was due to a BLM crate being down (cfv-sr7-BLMR).
    12:18: Ramp down.
    14:00: Ready to inject.
    15:33: Lost cryo conditions in sector 34: the 4.5 K cold compressor is down. We are probably out for 10-12 hours.

## Slide 7: Saturday 26.6
Stable beams with L ≈ 5 1029 cm-2 sec-1:

## Slide 8: Sunday 27.6
Luminosity over fill:

## Slide 9: Sunday 27.6
Intensity and lifetime versus time:

## Slide 10: Sunday 27.6
Bunch length versus time:

## Slide 11: Sunday 27.6
Beam intensity and lifetime:

## Slide 12: Sunday 27.6
Beam1 Tune lines and intensity: DQv = 5 10-3

## Slide 13: Sunday 27.6
Beam1 Tune lines and intensity: DQv = 5 10-3

## Slide 14: Sunday 27.6
Beam size from synchrotron light monitor (average):
  Philippe mentions later that only bunches 1 and 3 saw their length decreased down to 1.3 ns

## Slide 15: Monday 28.6
Plan for the weekend:
  Physics fills with 3 on 3 1011ppb.
  Horizontal beam separation for ALICE with aim of factor 30 luminosity reduction.
  Hump measurements at 450 GeV (if time permits).