## Slide 1: Progress with Beam
Ralph Assmann
LMC, 30.6.2010
For the coordination team:
  Week 26: Mike Lamont, Ralph Assmann
  Week 25: Oliver Bruening, Joerg Wenninger
Acknowledgements to EIC’s, Operators, System Experts, …

## Slide 2: Main Progress
Collimation setup and MP qualification for nominal bunch intensity completed. Settings into sequence.
Machine setup for July/August configuration:
  Squeeze with separated beams to b* = 3.5 m
  Beta beat measurements
  100 mrad crossing angle in IR1 and IR5
  Transverse damper for beam stabilization up to 3.5 TeV
  Reduction of chromaticity during ramp (measurements)
Four physics fills with nominal bunch intensity:
  New step up in instantaneous luminosity: 7-8 × 1029 cm-2 s-1.
  Approaching the 100 nb-1 earlier than promised.
  Working on characterizing interesting loss features.

## Slide 3: Collimation and Machine Protection

## Slide 4: High Intensity Collimation Setup for 3.5 TeV
Orbit and optics are different for 3.5 TeV and physics conditions, compared to injection. This requires a new beam-based collimation setup.
  Setup at 3.5 TeV involves 76 collimators, covering the two beams and x, y, skew and off-mentum phase space.
  Tertiary collimators have to be set up for three conditions due to change of setup in experimental areas (squeeze, separation, crossing angle, …).
Had to perform 108 collimator setups at 3.5 TeV.
  Each setup takes 15 min  27 hours of beam time at 3.5 TeV required.
  Reduced by factor 2 by doing both beams in parallel.
  Losses of time due to beam efficiency. Several beam dumps due to loss of 0.1% of intensity, when touching halo.
In the end took ~30 h of beam time with single bunch of 1e11 p at 3.5 TeV. Time distributed over 10 days with ~1 collimation shift per day.
Finally, setup of smooth ramp functions including interlock thresholds.

## Slide 5: Collimation Setting Overview (in terms of b beam size, status 25.6.2010)
Last campaign established the collimation settings for set 2, 3 and 4!
Ramp functions move smoothly from set 1 to set 2 during energy ramp!

## Slide 6: Qualification of Collimation Setup (3.5 TeV, squeezed, separated, 18.6.2010)
Beam 2
vertical
Beam 1
vertical
Beam 1
horizontal
Beam 2
horizontal
Beam 1 & 2
off-momentum
Qualification by provoking rapid beam losses on 1/3 resonances and by changing RF frequency (beam momentum)
Beam Intensity [p]
30 min

## Slide 7: Example of Achieved Collimation Performance (Beam 1, Vertical Plane, 1.3s)
factor 10,000 cleaning to SC arc magnets
TCT
TCT
Dump
TCT
TCT
Off-momentum
Betatron

## Slide 8: Zoom into Betatron Cleaning Region (Beam 1, Vertical Plane, 1.3s)
Expected loss locations in IR7 dispersion suppressor
TCT
Dump

## Slide 9: Beam Dump Qualification 3.5 TeV
Dump
Off-momentum
Betatron
TCT
Brennan et al

## Slide 10: Beam Dump Qualification 450 GeV
Dump
Off-momentum
Betatron

## Slide 11: Roman Pot Calibration with 450 GeV Beam

## Slide 12: Machine Setup for Summer

## Slide 13: Chromaticity Measurement: New Fitter
R. Steinhagen et al

## Slide 14: Chromaticity Measurement During Ramp
 BPM modulation versus time as RF frequency is modulated
R. Steinhagen et al

## Slide 15: Chromaticity in Ramp: B1
R. Steinhagen et al
H: 0  6.5
V: 0  5
June 24th
Stabilized with transverse damper

## Slide 16: Chromaticity in Ramp: B2
R. Steinhagen et al
H: 0  7
V: 0  5.5
June 24th
Stabilized with transverse damper

## Slide 17: Beta Beat (Rogelio Tomas Garcia et al)

## Slide 18: Beta Beat (Rogelio Tomas Garcia et al)

## Slide 19: Beta Beat (Rogelio Tomas Garcia et al)

## Slide 20: Beta Beat (Rogelio Tomas Garcia et al)

## Slide 21: Physics with Nominal Bunches

## Slide 22: 1st Physics Fill Nominal Bunches: Lifetime
Start of collisions
Sudden loss
~ 45 min
June 25
~ 3 × 1011 p per beam

## Slide 23: Scanning point 8 – vertical plane
tune amplitude
M. Lamont
~ 3 × 1011 p per beam

## Slide 24: Tune amplitude - zoom
beam intensities
M. Lamont
~ 3 × 1011 p per beam

## Slide 25: Bunch currents – beam 2
M. Lamont
~ 3 × 1011 p per beam

## Slide 26: 2nd Physics Fill Nominal Bunches: Intensity
June 26
~ 3 × 1011 p per beam

## Slide 27: 2nd Physics Fill Nom. Bunches: Lifetime, Int.
after ~6 hours
June 26
~ 3 × 1011 p per beam

## Slide 28: 2nd Physics Fill Nominal Bunches: Lumi
June 26
~ 3 × 1011 p per beam

## Slide 29: 3rd Physics Fill Nominal Bunches
June 29
~ 3 × 1011 p per beam
 New highest luminosity…

## Slide 30: Orbit Tune Up

## Slide 31: Orbit Change After 4 Hours (DE corrected)
Instrumental effects  1 mm at interlocked BPM in IR6

## Slide 32: 3rd Physics Fill Nominal Bunches: Lifetime
Collision
Crossing angle
~ 3 × 1011 p per beam
June 29
From luminosity (collision rate) expect lifetime of ~330 h!
Why is lifetime reduced to ~10 hours?
Indication of slow diffusion process as seen before (loss of tails).

## Slide 33: 3rd Physics Fill Nominal Bunches: Losses
Lifetime recovering after collision
Sudden loss
Intensity B1
Intensity B2
June 29

## Slide 34: What is this sudden loss?
It is a vertical beam size blowup (factor ~1.5). Stabilizes itself.
Mechanism not understood.
Could it be loss of Landau damping due to cut of beam tails with reduced dynamic aperture (R. Assmann)?
  Collision introduces lower lifetime than expected from collision rate.
  Proves that a diffusion process is generated: reduced dynamic aperture with beam-beam.
  The beam tails outside of dynamic aperture are lost with time. As tails are lost, lifetime improves with time.
  Big part of Landau damping is generated from the beam tails. As the beam distribution is cut, stability is lost at some point.
  Blow up of beam size. Beam stabilizes again with new tails.

## Slide 35: See Literature…

## Slide 36: Loss in Stable Beams – Problem for Collimation? 25.06.2010, 02:19
Sudden beam loss during stable beams.
Peak beam loss rate: 6.3e10 p/s for beam 2. Relative loss rate: 26 %/s
Reminder: Specified peak beam loss rate at 7 TeV is 4e11 p/s!
During this fill we reached with 0.1% of nominal intensity already 16% of nominal loss rate!
Relative loss rate was 260 times beyond specification!
Good case to analyze collimation performance.
6.25e10 p in 1 s

## Slide 37: BLM Readings during Losses with Stable Beams (3.5 TeV, 1.3 s)
Leakage peak:
6 × 10-5 Gy/s
BLM abort threshold SC magnets @ 3.5 TeV
factor 25 below threshold for 3.5 TeV and loss rate of 6.3e10 p/s.

## Slide 38: From Collimation: Can we Increase Intensity?
With the present beam stability we can push intensity by a factor ~25 before hitting the BLM threshold in SC magnets: 3e11  7.5e12 (~70 nominal bunches)
All losses at collimators: no problem for damage!
Must work on beam stability to enter the regime above 1e13 protons:
  Factor 10 better beam stability  reach 2010/11 goal of 6e13 p per beam.
  Factor 50 better beam stability  reach nominal beam intensity 3e14 p per beam.
Note:
  Assumes that BLM thresholds are accurate for 3.5 TeV. VERIFY!
  More severe loss rates in shorter time bins (fast loss spikes).

## Slide 39: Luminosity Performance
+ 7 nb-1 not included

## Slide 40: Ahead
Physics, physics, physics, … with increasing intensities: reach and surpass luminosity of 1030 cm-2 s-1
Four physics fills so far with 3 x 1011 p per beam. A fifth is under preparation.
Tighten operational procedures (squeeze into sequence, beam process of collapse of separation bump, crossing angle, …).
Tune up and improve machine and its stability.
Next week start preparing in parallel multi-bunch injection.