## Slide 1: Friday 23.7
18:00 on Thursday Machine Closed.
  Start requalification of all systems (magnets and RF).
  MKI.Ua23 Beam 1 kick delay changed from 88505 ns to 88515 ns (Etienne Carlier).
  5:30: Tripped Inner Triplet in IR8 when putting it in standby. Tripped again later without losing the QPS OK signal  the problem is probably coming from the PC. The piquet will go to point 8 to do some diagnostics (6:30)  needed to change optical fiber
  5:50: QHPS in sector 45 (magnet C18.R4) is slowly discharging. The MPE piquet must intervene  changed the switch
  6:32: Start pre-cycle with 10 A/s with whatever circuits are available:
    IT IR2 tripped
    ROD/Fs have no function associated
    RMSD.LR6 have no function associated
    RD34.LR3 gave an out-of-rate-limit error
    RQD/Fs in four sectors out of 8 don't charge the function.

## Slide 2: Friday 23.6
Plan for the day and weekend:
  pre-cycle and dry-run without beam
  Beam dump and IR6 BPM tests at 450 Gev.
  Ramp of single pilot bunch per beam with beam dump test at 3.5 TeV.
  test ramp of single nominal (0.9 1011) bunch per beam; SMP; full cycle, optic verification (AC dipole); loss maps for collimation verification.
  Friday to Saturday: Fill with 13 bunches per beam with stable physics.
  Saturday noon: multi bunch injection studies.
  Saturday evening: Fill and ramp with 25 bunches per beam with stable beams if possible.