## Slide 1: Week 33
Main goals for week 33:
  Luminosity production;
  First 150 ns bunch train attempts;
  Roman Pots: check movement at 3.5 TeV, with 1b;
  Off momentum loss maps for Beam2 in collision configuration;
  Moving to 48bx48b

## Slide 2: Week 33
Operation with 25 on 25 and 48 on 48 bunch configurations:
  3 fills with up-to 240 nb-1 per fill 36.5 h of luminosity production
   ca. one fill every other day; peak luminosity: L = 9.5 1030 cm-2 sec-1
  average fill time above 12 hours (10.5, 12, 14, [>7])
  integrated luminosity: 640 nb-1 (105, 105, 240, [190])
   ca. 22% efficiency (wrt to scheduled time = 1 week); 48% machine availability

## Slide 3: Week 31

## Slide 4: Week 33
  ca. 45% efficiency relative to available beam time
  ca. 22% efficiency per scheduled time

## Slide 5: Monday:
Started the day with physics fill from previous night.
Morning: End of fill studies
  Damper studies.
Afternoon: Access for various interventions:
  Among others: BLM updates;
  Finished access at 00:30 at night.
Night:
  Some delays due to problems with PC trips and QPS;
  Then BLM validation test with beam after firm ware update.

## Slide 6
Damper used at 3.5 TeV with different gains (horizontal plane)
red: beam 2 kicked
gain beam 2 damper
increased x16
in steps of x2
blue: beam 1 kicked
gain beam 1 damper
increased x16
in steps of x2
Data from bunch 1 oscillations (8192 turns), Qkicker used at full strength
gain setting: -25 dB to -1 dB in steps of 6 dB (-19 dB used operational)

## Slide 7
Time domain data (-25 dB and -7 dB gain) horizontal plane, beam 1
data from bunch 1 oscillations (8192 turns), Qkicker used at full strength
gain setting: -25 dB and -7 dB, beam 1 kicked, horizontal plane
factor 8 gain increase on one beam does not lead to a factor 8 increase of damping
 beams coupled, gain for damper on other beam was kept constant
-7 dB
-25 dB
beating of two modes,
both well damped
Damper used at 3.5 TeV with different gains (horizontal plane)

## Slide 8: Tuesday:
Morning: Bunch Train Studies:
  Ready for other systems (ADT, RF…) to make test on 1 train of 4 bunches ( B1);
  Non closure of LHCb spectrometer bump after polarity inversion;
Afternoon:
  Dispersion measurements and Loss map measurement for Beam2 at 3.5 TeV:  Hierarchy not satisfied for off momentum particles (-1kHz RF shift)
  Issue with Q-feedback and damper cohabitation during ramp: feedback system locks onto Hump signal.
Night:
  Struggling to prepare new fill for physics with 25 bunches (QPS; trips & SPS).

## Slide 9
Orbit in the LHC for injection with bunch trains:
Orbit after LHCb
spectrometer
polarization
change:
Top: initial orbit
for new polarity
Bottom:
After correction.

## Slide 10
Tune and Hump with damper on:
Beam 2: Vertical tune and Hump signal
are approximately equally
strong with damper on.

## Slide 11: Collimators – Loss maps on momentum Stefano Redaelli, Walter Venturini, Joerg Wenninger
1bx1b, Physics conditions -1000 Hz RF trim
BLACK = collimators
RED = warm elements BLUE = cold elements
TCTs see about ~0.01 of the primary loss spike and the cleaning efficiency to the cold elements is 99.25% (4 stage hierarchy is respected).
Operation with 25 bunches can continue in these conditions
To be repeated for B2

## Slide 12
Beam Losses in the LHC during injection with bunch trains
Daniel Wollmann:
The hierarchy is violated in this case: The TCSG.B5L3.B2 acted as primary collimator.
One can also see, that the losses
on the TCLA.A5L3.B2
are quite high
(~64% of the losses at
the TCSG).

## Slide 13: Wednesday 18.8.
Morning: Physics fill with 25 bunches:
  07:00: Injection;
  07:25: Start ramp;
  09:00: End of squeeze and stable beams;
  Emittances: ex1 = 3.0 mm; ey1 = 3.0 mm; ex2 = 3.4 mm; ey2 = 4.0mm;
  Initial peak luminosity: L = 3 1030 cm-2 sec-1;
   total delivered luminosity after 12 hours: 90nb-1; (105nb-1 with eof studies )
  19:00: Start moving Roman pots in steps:
   30s to 25s; 20s;
  21:00: Luminosity scan in IP1 to verify optimized collisions point;
  21:30: Beam dump & ramp down
22:00: Access for quench heater power supply problem on RB.24L2:

## Slide 14: Thursday 19.8.
Morning: Machine in access:
  BLM crate in Pt7 (broken power supply);
  RQT12.R1B1 repair of FGC: access in PM15;
  09:00: RCBCH6.R8B1 tripped  access required in Pt8;
  ATLAS asked if they could have short access in shadow of Pt8 intervention;
13:00: LHC ready for beam but now we have problems in the SPS:
  MST extraction septum in fault;
  Problem with the access chain.
15:00: Beam back in the SPS:
  Injection setup in the LHC;
  Loss map studies in IR3  looks good at 450 GeV;
  Tested Radial-Loop using external RF frequency trims;

## Slide 15: Thursday 19.8.
16:45: MPS fault in the SPS:
  No beam for 1 hour;
  Second loss map measurement;
  Dispersion measurement at 450 GeV for Beam2;
18:15: Inject nominal bunches for Q-feedback & Damper studies:
  Initial problems with BQM (SPS used old bunch structure);
  Observe some ‘odd’ excitations in horizontal BBQ for B2;
  Measure PLL and BBQ spectra with different damper gains  good result for PLL measurements;
19:10: Dump beams to prepare new fill:
  XPOC error due to losses at TCDS Beam1  BLM thresholds for new – shorter bunch spacing?;

## Slide 16: Thursday 19.8.
Horizontal
BBQ for
Beam2:

## Slide 17: Thursday – Friday 19-20.8.
Thursday: First physics fill with 48 bunches per beam:
  20:30: Injection finished  4.5 1012 protons per beam in 48 bunches;
  ex1 = 2.9 mm; ey1 = 2.9 mm; ex2 = 3.3 mm; ey2 = 3.5 mm;
  21:00: Start ramp;
  21:40: End ramp;
  22:20: Start Squeeze
  Initial luminosity: L = 6.65 1030 cm-2 sec-1;
  23:30: Stable physics; L = 6.15 1030 cm-2 sec-1;
 fitted average emittances for bunch current of Nb = 9 1010:
s = 4.05mm; with b* = 3.6m (average of three 1/b* measurement in IR5)
   integrated luminosity = 240 nb-1 after 16 hours;

## Slide 18: Fill 1295
  IPs: 1 5 2 8 - 1 5 8 - 1 5 2 - 1 5 - 2 8 - 8
1 LR in 2 (33m)
1 LR in 2 (33m)
1 LR in 8 (33m)
1 LR in 8 (33m)
1 LR in 2 (22m)
1 LR in 2 (22m)
no Long Range interactions
with Long Range
giulia papotti (BE/OP/LHC)

## Slide 19: Friday 20.8.
End of Fill studies:
  Luminosity scans in all IPs (large scan in IP1);
  Damper studies;
  Orbit feedback test for radial loop correction;
  16:15: Beam dump; very clean & without any unusual losses
Afternoon:
  Cryo problem in Pt6 right after the beam dump.

## Slide 20: Friday 20.8.
Lumi scans
in IR1:
average
beam
emittances:
ex = 4.4mm
ey = 4.9mm
growth of
10% to 20%
over the fill!

## Slide 21: Saturday 21.8.
Morning & Day: Recovery from Cryo problems:
  20:00: Cry recovered for pre-cycle in S56 and S67;
  22:15: Starting injection;
  22:30: Injection kicker fault - sparking (called experts); spark occurred after clean injection;
  22:30: Beams dumped due to Cryo problem for right IR5 triplet (back by 01:00);
Preparing second fill with 48 bunches:
  03:30: Injection finished  4.5 1012 protons per beam in 48 bunches;
  ex1 = 2.6 mm; ey1 = 2.6 mm; ex2 = 2.8 mm; ey2 = 3.2 mm;
  03:40: Start ramp; losses in IR3 at beginning of ramp;
   Beams dumped by SIS TCDQ_B2 interlock triggered by the
  TCS_BEAM_OFFSET_B2;
  04:50: Trip of RCBYVS4.L1B1 during the ramp down combo;
   power module to be exchanged on RCBYVS4.L1B1, access needed in Pt 1;

## Slide 22: Sunday 22.8.
Morning: Access following perturbation of electrical network:
  06:50: PC permit sector 45 lost due to perturbation on electrical network; ALICE and LHCb dipoles also tripped;
  RD1.LR5 also down (water cable fault);
  QPS: RQS.A12B2 and RQTF.A81B1 we changed QPS board;
  09:00: Access finished and experiments back up running;
Morning and afternoon: Trying to get machine ready for beam:
  09:00: Start pre-cycle (RQTL11.L5B2 needed change of board channel and several ciruits tripped);
  RQ6.L1B1/B2 tripped several times due to a bad contact (caused too low threshold) that was probably generated during intervention in the morning.
   need access again. Access finished by 12:15.
  13:50: Machine ready for injection;
  Asking for mastership resulted in a PM - with no beam in the machine - first triggered inputs in PM seem to be BLMs in 6  search for BPM expert; interventions finished by 18:00.

## Slide 23: Sunday 22.8.
Morning and afternoon: Trying to get machine ready for beam:
  09:00: Start pre-cycle (RQTL11.L5B2 needed change of board channel and several ciruits tripped);
  RQ6.L1B1/B2 tripped several times due to a bad contact (caused too low threshold) that was probably generated during intervention in the morning.
   need access again. Access finished by 12:15.
  13:50: Machine ready for injection;
  Asking for mastership resulted in a PM - with no beam in the machine - first triggered inputs in PM seem to be BLMs in 6  search for BPM expert; interventions finished by 18:00.
  18:00: Starting injection;
  19:00: Staring over injection with nominal bunches  Beam dumped by BPM interlock in point 6 (BPM L & R for Beam 1);
  19:30: Problems in IP6 (BPM error: CALIBRATION MODE); fixed by 21:15;

## Slide 24: Sunday – Monday 22-23.8.
Third fill with 48 bunches per beam:
  22:20: Injection finished  4.7 1012 protons per beam in 48 bunches;
  Emittances between 2.5 mm and 3.0 mm (measured in the SPS);
  22:30: Start ramp;
  00:40: Start Squeeze
  Initial luminosity: L > 9.4 1030 cm-2 sec-1;
  00:50: Stable beams after optimization:
  L = 9.1 1030 cm-2 sec-1;
 fitted average emittances for bunch current of Nb = 9.8 1010:
s = 3.35mm; with b* = 3.6m (average of three 1/b* measurement in IR5)
   integrated luminosity = 190 nb-1 after 7.5 hours;

## Slide 25: Sunday-Monday 22-23.8.
Initial luminosity
above
9.4 1030 cm-2 sec-1!

## Slide 26: Monday 23.8.
Plan for the week:
  Continue physics fills with 48 bunches;
  Continue preparatory studies for bunch train injection;
  Loss maps and b* measurement via Q1 modulation;
Coordinators for week 34:
  Ralph Assmann & Roger Bailey

## Slide 27: Week 33
Open Issues for next Technical Stop:
  CMS cooling for central tracker.
  Ion pumps in dump line MKB (B2 only 4 out of 8 pumps working; few days intervention).
  BLM racks (in buildings SR1 and SR5 and both at position BY02): would like to correct the way the power cable for the multi-plug arrives inside the rack.
  QPS boards: several boards had to switch from channel A to B.
  Access team to replace oxydized connectors for PAD-PX24 (3 hours).
  CV needs to replace a motorization of the water valve of the sector 56 (3h).
  RCBH18.R7B2 – Miguel Cerqueira Bastos.
  RCSSX3.L1 super blocked for cryo.