## Slide 1: Saturday
14:10 Cryogenics back [26 hours 40 minutes]
Pre-cycle
15:30 Beam 2 in
  Interlock on TCLIB.6R2.B1. Alessandro Masi found a broken sensor, it would dump at random - disabled it
15:45 Lost sectors 12 and 23 – AUG TI2
  First BIC input Triggered: First USR_PERMIT change: Ch 14-FMCM_RBXWTV.L2: A T -> F on CIB.UA27.R2.B2
  RP, Fire brigade and EL piquet into TI2 via BA7
  AUGs shunted – restricted access for the moment
  Recovery – power converters, QPS etc.
19:15 Start pre-cycle
20:15 Beam back

## Slide 2: Saturday night
21:10 Start ramp – pilots
  Tune feedback off in ramp -> lifetime dip at start of squeeze
  Briefly into collisions
22:50 Sector 78 off for DFB level adjustment (CM loss during manipulation) – finished at midnight
01:06 start ramp - two nominal bunches
01:13 Lost beams...LBDS self-trigger
  MKD analysis XPOC faulty for beam 1
  Access required in point 6 to exchange the faulty power trigger power supply
  P.Burkel & W.Senaj wrestling with software among other things

## Slide 3: Sunday morning
05:10 Beam back in
06:50 Colliding – two nominal
  Atlas collision point off…
07:20 Stable beams
08:40 Change ADJUST for loss maps
Aim to re-fill for Van der Meer scans
And then back to 50 ns - 228b

## Slide 4: Miscellaneous
XPOC
  Expert reset required every time – vacuum readings
Still fairly bad trajectory in H TI 2. Did not take the time in the end to correct on LHC4. Needs some attention still.

## Slide 5: RF
Measurements done when re-starting the cavities on Thursday evening showed that the 380 MHz reference Beam2 had drifted by ~ 8 degree (60 ps). We do not know why (aging, temp,humidity...?).
This reference is common to all 8 cavities B2. The drift has two effects: It reduces the stability margin of the RF fdbk (not much... the margin is 60 deg) AND it displaces the collision point. I have re-adjusted all beam 2 cavities by 8 degrees. That should be completely transparent EXCEPT that it should rotate the IP by... 8 mm. As these 8 mm are the amount of displacement noticed by the experiment, I prefer NOT to change the IP point until we have IP data with the new setting.
Philippe Baudrenghien