## Slide 1: Friday AM
Some oscillations of the cryo conditions in MSR8 perturbed the setup for injection.
RF frequency interlock fixed – required a reset of RF controls in Pt4.
Injection protection:
  Check of TDI and TCLI setup, confirmed with loss maps.
  Summary:
    TDIs are at the assumed settings and consistent with the TCPs - upper jaw of TDI. B1 needs moving IN by 0.4 sigma, all others are correct  done.
    Protection is good with the current settings of TDI/TCLIb/TCLIa, but we still risk having large beam loss on a TCLIb. The TCLIb of at least point 8 will be opened up more (next week) to reduce the load on the Q6 in case of injection loss problems, and pending full FLUKA simulations.

## Slide 2: Friday PM
16:00 Start filling 912x912
  Vacuum OK – one large spike around Q5.L1 (S81) at the beginning of injection
18:15 Ramp - beautiful beams (intensity+emittance).
  Dumped by the new RF interlock on total voltage at 563 GeV.
  >> disabled again. RF will now first monitor the interlock.
21:00 Refill
22:40 Stable beams fill 1809 – almost 1.1E33 cm-2s-1.
  DIP problem at start of fill…
00:30 Dumped by FMCM on RD1.LR5 – electrical perturbation.

## Slide 3: Vacuum spike during first HI injections

## Slide 4: Friday Night
Refill…
  Vacuum spike on MKI B2 again.
  Problems with Q measurements – almost no signal…
  Beam dumped on flat top – again RD1.LR5. Also problem on RB.23 – electrical perturbations

## Slide 5: Friday Night / Saturday morning
Refill once more.
  Vacuum interlock on MKI B2. Reset by expert needed.
  Problem with the MTG – no timing event sent.
  Reboot of timing system stops all 60A CODs and send out access events for 2 sectors…
  At 07:00 the MTGA is found dead again. Switch the MTGB.
08:15 Stable beams fill 1812
  Again DIP problem with luminosity.

## Slide 6: Today
Keep this fill a while… end of RF off tests (ADJUST).
If fill is lost before RF test: special cycle – only to flat top – for the RF test (no squeeze, no collisions).
Off momentum loss map (required by coll team).
Increase number of bunches if time is reasonable (not in the night)