## Slide 1: RF interlocks for higher intensities (LMC 15 June)
Now:
  We connect the RF interlock sum to the beam dump. As a consequence any RF trip will dump the beam. Conservative but safe...
  We install filters on the Waveguide Arc Detectors to reduce false alarm rate. Done
  We install new hardware in the Main Coupler Arc detectors for the remaining 12 cavities. Done in 15 out of 16 cavities
During next Technical Stop: we re-configure the FPGA in the Interlock crates to generate a Beam Interlock Sum signal taking a selection of the inputs from the RF Interlock system:
  Higher Order Mode power (4 signals: Wideband A, Narrowband A, Wideband B, Narrowband B)
  Main Coupler vacuum
  Maximum Cavity Field
in addition to the signals already connected to the BIS:
  Main Coupler Arc Detector
  Helium pressure and level
We cannot do this before the technical stop as it must be tested for validation.

## Slide 2: RF trip statistics since 30 May
HV trips:
RF trips:
Cause | Real | Spurious | Comments
Main Coupler arc detectors |  | 6 | Beam dump: direct connection to BIS 15 out of 16 detectors now replaced with new model
Waveguide arc detectors |  | 6 | All detectors now fitted with filter
HOM temp > 6K | 2 |  | Real temp >6K of 2 probes Software interlock at 15K
Klystron current out of range | 2 |  | Under investigation (twice on same klystron, no data in logging)
Main coupler vacuum | 1 |  | Should dump the beam to protect coupler!
Totals | 5 | 12 | 
Cause | Real | Spurious | Comments
Helium pressure | 2 |  | Cavity micro-quenches
Focus power supply | 1 |  | Hardware failure
Crowbar | 1 |  | 
Totals | 4 |  | Total voltage interlock dumps beam

## Slide 3: Summary
Since 30 May, RF generated 10 beam dumps
Arc detector improvements would have avoided 6 of these
Connecting the interlock sum would have given an additional 5 beam dumps
  including 1 Main Coupler vacuum interlock which is desirable to protect the coupler